## Slide 1
Shared delivery establishment and subsequent signalling - For discussion

## Slide 2: Related TDOCs
Tdoc number | Title | Source | Affected clauses |  |  |  | Note | WF proposal
 |  |  | 7.2.1.3 | 7.2.1.x (shared path establishment) | 7.2.1.y path release | 7.2.1.z (deactivation) |  | 
S2-2102291 | 23.247: Update [7.2.1.3] MBS join and Session establishment procedure | Ericsson |  |  |  |  |  | Should be merged into one
S2-2102387 | 23.247: MBS Session Join and Establishment | Huawei |  (7.2.1 a few) |  |  |  |  | 
S2-2102434 | 23.247: MBS Join and Session Establishment Procedure | Tencent |  |  |  |  |  | 
S2-2102438 | 23.247: Multicast session join procedure | CATT |  |  |  |  |  | 
S2-2102675 | 23.247: [7.2.1]-UE requested session join | vivo |  |  |  |  |  | 
S2-2102797 | 23.247: Modification to MBS session join procedure | ZTE |  |  |  |  |  | 
S2-2102941 | 23.247: Shared delivery establishment and support of subsequent signalling from MB-SMF | Nokia |  |  |  |  | 7.2.1.x/y/z: should consider together with related docs. | 
Tdoc number | Title | Source | Affected clauses |  |  |  |  | Note | WF proposal
 |  |  | 7.2.3.1 | 7.2.3.2 | 7.2.3.3 | 7.2.3.4 | 4.2.x |  | 
S2-2102290 | Signaling efficiency for Shared Delivery and others | Ericsson |  |  |  |  |  | Discussion paper, (update of the docs submitted to CC#1) | 
S2-2102393 | Discussion on Signalling Efficiency for MBS solutions | Huawei |  |  |  |  |  | Discussion paper (update of the docs submitted to CC#1) | 
S2-2102356 | 23.247: Multicast session start/stop/update&activation/de-activation/modification procedures | Samsung |  |  |  |  |  | Basic procedure: activation involve SMF. | Should be merged into one
S2-2102772 | 23.247: MBS Session Activation and Deactivation | Huawei |  |  |  |  |  | Basic procedure. | 
S2-2102942 | 23.247: MBS session activation. | Nokia |  |  |  |  |  | Session activation based on option 2 of 1017: SMF provides UE list to AMF | 

## Slide 3: Different proposed options
Option 1: Shared delivery establishment triggered by RAN, no RAN nodes and SMFs stored in MB-SMF (Huawei)
All subsequent signalling from MB-SAMF related to multicast session (e.g. for activation and deactivation) would need to go via SMF, as MB-SMF is not aware of AMFs and NG-RAN nodes in multicast session.

## Slide 4: Different proposed options
Option 2: Shared delivery establishment triggered by RAN, MB-SMF stores RAN node IDs (Nokia)

## Slide 5: Different proposed options
Option 3: Shared delivery establishment triggered by RAN, AMF stores RAN node IDs
In a variant of Option 2, AMF also stores GTP Tunnel endpoint for multicast transport and avoids signalling to MB-SMF if multicast transport is used and additional RAN nodes request shared delivery for that multicast session.

## Slide 6: Different proposed options
Option 4: AMF centric approach: AMF triggers establishment of shared delivery and stores UEs and RAN nodes in multicast session
(Ericsson)

## Slide 7: Different proposed options
Option 5: Signalling Piggybacked in PDU session signalling (Vivo)
All subsequent signalling from MB-SMF related to multicast session (e.g. for activation, deactivation) would need to go via SMF, as MB-SMF is not aware of AMFs and NG-RAN nodes in multicast session.
Signalling also piggybacked in Xn/N2 HO

## Slide 8: Status quo: technically endorsed S2-2103074
Option 2 with editor´s notes about option 1, option 3 and option 5
UE
NG-RAN
AMF
SMF
UPF
NRF
MB-SMF
MB-UPF
AF
1a. UL NAS message (N1 SM container (PDU Session Modification Request))
1b. Nsmf_PDUSession_UpdateSMContext request
5. Nsmf_PDUSession_UpdateSMContext response
3. Nnrf_NFDiscovery request/response
4. Nsmf_MBSSession_Create request/response
6. N2 message request
13. Multicast data
14. Multicast data
15. Bear selection
16. Multicast data via PTP or PTM
Transmission via 5GC shared MBS traffic delivery
17. Multicast data
18. Multicast data via PDU Session
19. Multicast data via PDU Session
Transmission via 5GC Individual MBS traffic delivery
2. Authorization check, see clause 6.1.1
Establishment of resources for 5GC shared MBS traffic delivery
7a. N2 message
7b. Nsmf_MBSSession_Create request
7c. Configuration for Shared delivery
7d. Nsmf_MBSSession_Create response
7e. N2 message
9. N2 message response
10. Nsmf_PDUSession_UpdateSMContext request
Establishment of resources for 5GC Individual MBS traffic delivery
11a. Configuration for Individual delivery
11b. Nsmf_MBSSession_Update request
11c. Configuration for Individual delivery
11d. Nsmf_MBSSession_Update response
11e. Configuration for Individual delivery
8. RRC message (PDU Session Modification command)
12. Nsmf_PDUSession_UpdateSMContext response

## Slide 9: Status quo: TS 23.247, Mobility procedures, N2 based Handover, Figure 7.2.3.3-1
Option 1

## Slide 10: Comparison of Options
 | Option 1 | Option 2 | Option 3 | Option 4 | Option 5
State about multicast session in AMF | Not required | Not required | RAN nodes | RAN nodes, UEs, MB-SMF | Not required
State about multicast session in MB-SMF | SMFs, RAN node addresses | SMFs, AMFs RAN nodes, RAN node adresses, UEs | SMFs, AMFs, RAN node addresses, UEs | SMFs, AMFs, RAN node addresses | SMFs, RAN node addresses
State about multicast session in SMF | MB-SMF, UEs, RAN nodes | MB-SMF, UEs | MB-SMF, UEs | MB-SMF, UEs | MB-SMF, UEs, RAN nodes
subsequent direct signalling (without intermediate SMF) for multicast session (e.g. deactivation) from MB-SMF to RAN nodes possible | yes | Yes | Yes | Yes | No
activation for multicast session from MB-SMF to RAN nodes (assuming group paging in specific paging area determined based on UEs in multicast session) | Via SMF and AMF (includes UE list) | Via SMF and AMF (includes UE list) | Via SMF and AMF (includes UE list) | Via AMF | ?
AMF involvement in activation (same assumption) | AMF determines paging area based on received UE list | AMF determines paging area based on received UE list | AMF determines paging area based on received UE list | AMF determines paging area based on stored UE list in MBS session | ?
Possibility of dublicated signalling from different AMFs for same MBS session at RAN node | Only session activation | Only session activation | Only session activation | Yes | Only session activation
SMF involvement in multicast session management (activation, is not considered session management) | No | No | No | Yes | No
Same solution for shared delivery establishment when first UE is handed over to RAN node | yes | yes | yes | yes | Again piggybacking, but in different messages

## Slide 11
subsequent signalling and other aspects
Slide added by Ericsson
In the following slides:
Option-SMF refers to SMF handling MBS Session
Option-AMF refers to AMF handling MBS Session

## Slide 12: MBS Session Activation
Option-SMF (Nokia S2-2102942)
Slide added by Ericsson
Option-AMF: MB-SMF -> AMF -> RAN (see red rectangle below)
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)
Q1: If joined UEs does not have UP in SMF, but in CONNECTED state for other reason, how would such UE be added in MBS Session in RAN?
Nokia: UE will not be added to multicast session via activation but via join and will have an SMF assigned
Q2: If all joined UEs in SMF have UP activated, does it mean that no MBS Session activation message will be sent to the NG-RAN? If so, how to bring the “inactive” MBS Session in RAN to Active again?
Nokia: Reception of multicast data would trigger RAN node to activate inactive UEs (similar to existing procedures for unicast). Alternative proposal is to include all UEs in list, also with deactivated PDU session, and notify all RAN nodes about activation. (Similar to Ericsson)
Nokia Q1: How can exact UE location be determined without service request? Is that part only not shown?
Nokia Q2: Can SMF involvement be avoided in Individual fallback is supported

## Slide 13: MBS Session Deactivation
Option-SMF (from S2-2101017)
Slide added by Ericsson
Option-AMF: (see red rectangle below)
Option 2
AMF
UE
SMF
MB-SMF
MBS deactivate
NG-RAN
MBS contexts and N3 may be kept for connected and inactive UEs
Variant 2c
DeActivate (MBS session id, list of NG-RAN nodes)
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)

## Slide 14: MBS Session Update (adding/deleting/modifying MBS QoS Flow)
Option-SMF: Which path to follow ?
  Path: MBS Session Activation, or
  Path: MBS Session Deactivation?
Nokia: SMF will need to know QoS updates for associated QoS flows and Ues in individual fallback.
For homogeneous deployments also direct signalling from MB-SMF via AMF feasible for options 2 and 3
Should be discussed separately.
Slide added by Ericsson
Option-AMF: same path as for MBS Start/Activate/Deactivate
UE
NG-RAN
AMF
SMF
MB-SMF
NRF
MBS Session Update Request/Response
MBS Session Update
Update

## Slide 15: Other aspects
Alignment/misalignment between handling of PDU Session and handling of MBS Session ?
  SMF and MB-SMF discovery
    AMF discovers SMF for PDU Session (based on DNN, S-NSSAI, location…), while Option-SMF discovers MB-SMF for MBS Session => misalignment?
    Nokia: In all options AMF will need to discover MB-SMF based on TMGI
  NG-RAN info in CN
    SMF is only aware of NG-RAN tunnel entity for PDU Session, while in Option-SMF, MB-SMF will have knowledge of NG-RAN node (in addition to NG-RAN’s tunnel info) => misalignment?
    Nokia: not considered problematic, but is avoided in Option 3
  SM/MM split but AMF is already aware of session info, e.g.
    AMF handles EBI associated with QoS Flow (which is SM info),
    In NB-IoT case, AMF needs to know whether PDU Session’s UP has been established to limit the max no. of radio bearers
    Nokia: We have the opportunity to do this better for multicast
Slide added by Ericsson

## Slide 16: Comparison of Options considering subsequent signalling and other aspects
 | Option-SMF | Option-AMF | Comment
Consistent logic of different procedures (involved entities, failure handling possibilities etc) | Ericsson: No, every procedure is different, unless signaling efficiency is not considered Nokia: Only two types of procedures: with and without SMF involvement. | Ericsson Consistent and signaling efficient Nokia: Proposal is incomplete and ignores that SMFs need to be involved due to associated QoS flows and individual fallback. If that is considered procedures become similar to option SMF | 
Potential issues with MBS Session activation | Ericsson: Yes, see Q1 and Q2 in slide “MBS Session Activation” Nokia: Already answered | Ericsson: Not identified so far Nokia: Yes: see related questions added | 
UE join with only TMGI allocated | Ericsson: How UE can be associated with MBS Session when it’s started/estalbished is not clarified | Supported Nokia How can QoS be determined for such a MBS session | Nokia: This seems a misunderstanding and unrelated.
Complexity to support foreseen future scenarios (e.g., ETSUN scenarios, roaming) | Ericsson: Expected to be very complicated unless AMF is involved Nokia: Ericsson seems to assume entirely different procedures without SMF involvement in JOIN handling and without possibility for individual fallback in those scenarios. Other proposals avoided that and no significant difference foreseen. | Ericsson AMF selecting MB-SMF follows the same logic as for I-SMF selection Nokia: MB-SMF selection will always need to select the MB-SMF handling the multicast session and is thus different to I-SMF selection also for ETSUN. | 
Slide added by Ericsson

## Slide 17
Thank You!