## Slide 1
New SID proposal on
Enhancement of 5G AM Policy in R18
Zhuoyi Chen
China Telecom

## Slide 2
  AM Policy alignment in interworking scenario (4G and 5G)
  New parameters and provisioning procedure to assist AM policy decision
  Potential requirement from SA1 conclusion
The Access and Mobility Policy control introduced in 5G encompasses the management of service area restrictions, the management of the RFSP functionalities and UE-AMBR by PCF.
Some potential enhancements for study in AM Policy are identified based on the Rel-17 SA2 issues and Rel-18 SA1 requirements:

## Slide 3
  Potential Enhancement for Study (1/3)
  AM Policy alignment in interworking scenario (4G and 5G)
A PING-PONG Issue from RFSP Index conflict:
While the UE is in 5G, the PCF decide to change the subscription RFSP Index to direct the UE to 4G.
While the UE is in 4G, the MME select its RFSP Index according to Subscription Data or Local configuration, and direct the UE to 5G.
  AM Policy is NOT supported in EPC. It may result in AM parameters conflict while a UE is in an interworking scenario.
A dynamic mechanism needs to be investigated to support AM policy update for the EPC side.

## Slide 4
  Potential Enhancement for Study (2/3)
  New parameters and provisioning procedure to assist AM policy decision
How does PCF-AM handle among different applications’ requirements, if
App1/2/3 are reported activate at the same time, and
App1/2/3 request conflicted AM policy
  As conclusion from DCAMP, the PCF serving a UE may receive notification from PCF(s) serving a PDU session that specific application traffic starts/stops and trigger AM policy check and update.
The PCF may need information about the priority level between applications while deciding or updating the AM policy. Accordingly, the parameters and provisioning method are needed.
PCF-AM
PCF-SM 1
PCF-SM 2
Detection of App 1
Detection of App 2
Detection of App 3
HOW to decide the
AM policy?

## Slide 5
  Potential Enhancement for Study (3/3)
  Potential requirement from SA1 conclusion
Some new requirements identified in TS22.844 that related to AM policy:
[PR.5.1.6-1]5G system shall be able to support for a UE to be provided with the temporary connectivity service over unlicensed spectrum at specific locations and specific period.
[PR.5.5.6-3] The 5G system shall support means for a hosting network to create policies and configure resources for the requested time and location for the 3rd Party Provider services based on the received request.
  New enhancement requirement might comes from SA1 Rel-18 conclusions. For example, the 5G networks Providing Access to Localized Services (FS_PALS):
The SA2 work should be aligned with the outcome of the SA1 work in AM policy enhancement.

## Slide 6
THANK YOU