## Slide 1: New WID: Extensions to the TSC Framework to support DetNet
SA2
Ericsson
S2-2103968

## Slide 2: Deterministic Networking
Deterministic networking is a requirement for several application areas
  Includes industrial communication and IIoT
Historically deterministic networking has been handled by proprietary / fieldbus technologies
Standardization efforts to address deterministic networking in global open standards
  Ethernet: IEEE 802.1 TSN
  IP: IETF DetNet
IP benefit: flexibility and scalability
Status of IETF DetNet has reached high level of maturity
https://www.comsoc.org/publications/ctn/quick-and-dead-rise-deterministic-networks
IETF RFC 8578, Deterministic Networking Use Cases

## Slide 3: Possible use cases for DetNet
Industrial machine-to-machine communication in discrete and process automation
Building automation
Smart grid communication
Media
Larger industrial installations
…

## Slide 4: DetNet overview
DetNet provides Layer 3 (IP/MPLS) networking aspects in support of applications requiring bounded low latency, low delay variation, and extremely low loss
DetNet covers
  characterization of flows
  data plane, including encapsulation
  required forwarding behavior
DetNet network (L3: IP/MPLS)
DetNet flow (L3)
DetNet

## Slide 5: DetNet Standardization Status in IETF

## Slide 6: Re-use TSC framework for DetNet integration
Re-use mechanisms for QoS and for transferring management information.
DetNet AF exposes 3GPP system as a logical DetNet router
Re-use existing 3GPP routing mechanism; no new routing function is defined.
Multicast and DetNet edge functionality are out of scope.
No new functionality for time synchronization is needed.
Only for IP DetNet; MPLS is out of scope
UE1
UPF
DS-TT
UE2
DS-TT
NW-TT
SMF
PCF
DetNet AF
DetNet Controller
AMF
RAN
DetNet
5G system as a logical DetNet router

## Slide 7: DetNet conclusion
DetNet has reached maturity in the IETF standardization
It is one deterministic transport solution based on IP and it is relevant for IIoT
Ericsson proposes to introduce DetNet support reusing TSC architecture and concepts, as applicable, for 5GS, and by defining a DetNet AF