## Slide 1
SA2#145E
Discussion on the format of SUPI/SUCI of a UE from credentials holder when accessing to a SNPN
vivo

## Slide 2
Background
In rel-16, the SUPI of a SNPN UE can be format of NAI or IMSI. Roaming is not supported, A SNPN is only allowed to be accessed by a UE of the SNPN.
SUPI Formats | AUSF/UDM selection
When IMSI based SUPI is used, the NID is not captured in the SUPI - the UE shall additionally indicate the selected NID to NG-RAN. NG-RAN shall inform the AMF of the selected NID | the AMF performs the AUSF and UDM selection based on the PLMN ID from SUPI) and selected NID from the NG RAN.
When NSI based SUPI is used, the NID is not captured in the SUPI | the AMF performs the AUSF and UDM selection based on the PLMN ID and NID from SUPI

## Slide 3
Issues
In rel-17, an SNPN-1 can be accessed by a UE from Credentials Holder, e.g. SNPN-2 UE or a PLMN UE. Two issues raised when IMSI format SUPI is used
  Issue#1 how the AMF in SNPN-1 knows the NID of the SNPN-2 UE.
    There is argument that the following note in 23.501 is sufficient to fix Issue#1.
      “NOTE 1: When Credentials Holder is an SNPN, and the MCC and MNC of the SNPN is not unique, then IMSI based SUPI is not supported as the MCC and MNC need not be unique always; instead USIM credentials are supported using Network Specific Identifier based SUPI.”
    However, “not unique” can be understood as 1) not unique to identify a PLMN, e.g. value “999”; or 2) unique to identify a PLMN, but is not unique to identify a SNPN, shall use NID together. We believe 1) is the correct understanding for the note, so Issue#1 still exits.
  Issue#2 how to distinguish SNPN-1 and PLMN in case their MCC and MNC are same.
    There is argument that it is a corner case. However, NID is introduced because PLMN ID are not sufficient to identify SNPN. So a PLMN and a SNPN having the same PLMN ID is not a corner case.

## Slide 4
Solution option for Issue#1
Solution option for Issue#1
Option#1: When Credentials Holder is an SNPN, in case of SNPN-2 UE accessing to SNPN-1 and using IMSI based SUPI, it additionally provides its NID in the Registration Request message. The AMF in SNPN-1 use the PLMN ID of the SUPI and NID in the Registration Request message for AUSF/UDM selection.
Option#2: Update the Note “When Credentials Holder is an SNPN, and the MCC and MNC of the SNPN is not unique, then IMSI based SUPI is not supported as the MCC and MNC need not be unique always; instead USIM credentials are supported using Network Specific Identifier based SUPI.” as “When Credentials Holder is an SNPN, USIM credentials uses Network Specific Identifier based SUPI.”
Proposal1: It is proposed to take the above options into account.

## Slide 5
Solution option for Issue#2
Solution option for Issue#2
Option#1: When Credentials Holder is an PLMN, when the PLMN ID of the SNPN accessing by the UE and PLMN are same, the UE use the NSI based SUPI to access the SNPN.
Option#2: When Credentials Holder is an PLMN, the UE use the NSI based SUPI to access the SNPN.
Proposal1: It is proposed to take the above options into account.

## Slide 6
Thank You!