## Slide 1: 5GS Leaving procedure for 5GC/NR and Busy indication from RRC_Inactive
Intel
SA2#145E, Electronic meeting, 17 – 28 May 2021
S2-2104276

## Slide 2: Outline
  How to handle the 5GS Leaving procedure for 5GC/NR in the light of the RAN2#113bis-e meeting agreements.
  How to handle the Busy indication from RRC_Inactive in the light of the RAN2 LS (R2-2104354).
  Summary of proposals

## Slide 3: 5GS Leaving for 5GC/NR (1/3)
RAN2#113bis-e have reached the following agreements on RRC leaving:
    1 RRC signalling is used for switching procedure without leaving RRC_CONNECTED state in network A for UE temporarily switching to network B as a baseline. FFS on additional need of MAC signalling.
    2 During switching procedure for leaving RRC_CONNECTED state, UE is allowed to enter RRC_IDLE state if it does not receive response message from network within a certain configured time period. FFS for RRC_INACTIVE state.
Regarding Agreement 1:
    This leaving procedure (with UE remaining in RRC_Connected state) is completely transparent to the CN. It can be used for short activity in the other network (e.g. performing mobility or periodic update, or Busy indication). During UE’s absence, the NG-RAN can e.g. silently drop packets, without declaring RL failure.
    Agreement 1 has no impact on the work in SA2 other than referencing it as a possibility (e.g. in the functional description or in a NOTE in the Leaving procedure).
Regarding Agreement 2:
    Currently it covers only the RRC_Idle state and addresses the error case where the RAN’s ack is somehow lost.

## Slide 4: 5GS Leaving for 5GC/NR (2/3)
When the end state of the 5GS Leaving procedure is RRC_Idle:
    Is NAS Leaving procedure still needed for 5GC/NR in addition to the RRC Leaving procedure?
      We think NAS Leaving is needed in order to cope with the case of non-supporting RAN node
      NAS Leaving is also needed when UE wants to use Paging Restrictions (we assume that PRs are not supported with RRC Leaving)
      When RAN node supports RRC Leaving and UE does not need to use PRs, the choice of procedure (i.e. RRC Leaving vs NAS Leaving) can be left to UE implementation (the expectation being that RRC Leaving should be slightly faster)
Proposal 1: The standard shall support NAS Leaving for 5GC/NR in addition to RRC Leaving.

## Slide 5: 5GS Leaving for 5GC/NR (3/3)
  When the end state of the 5GS Leaving procedure is RRC_Inactive:
    Should this case be supported?
      SA2#144E agreed that for NAS Leaving with 5GC/E-UTRA case the end state can only be RRC_Idle (refer to the technically endorsed S2-2103027). Introducing support for RRC_Inactive in the 5GC/NR case would be a further discrepancy compared to the 5GC/E-UTRA case
      If RAN2 decide to support RRC Leaving with end state RRC_Inactive, we assume that the use of Paging Restrictions is not possible.
      With NAS Leaving it is possible to support RRC_Inactive including the provision of Paging Restrictions to NG-RAN (e.g. as described in TR 23.761 Figure 6.5.3.1.1-1 step 2).
      It is noted that support for (NAS or RRC) Leaving with end state RRC_Inactive will require some work in RAN3 and may have impact to charging due to silently discarded data in NG-RAN for prolonged period of time.
      For short absence (e.g. performing mobility/periodic udate or Busy indication in the other network) the UE can use the “RRC switching procedure without leaving RRC_Connected state”
      For absence of undetermined duration the UE might as well be put in RRC_Idle state. Indeed, if silent discarding of DL data by NG-RAN is considered an issue for charging, then UE should better be released to RRC_idle
Proposal 2: NAS Leaving with end state RRC_Inactive is not supported. Inform RAN2 of the decision so that they can discontinue their work on RRC Leaving with end state RRC_Inactive.

## Slide 6: Busy indication from RRC_Inactive
RAN2#113bis-e have reached the following agreement on Busy indication from RRC_Inactive (R2-2104354):
    1 Only support NAS-based busy indication (for IDLE and INACTIVE)
Consequences of this agreement for SA2:
    Based on offline discussions, the majority of SA2 companies seem to support the alternative where the UE uses the 5GS NAS Leaving procedure to reject RAN paging
      If Proposal 2 in this document is agreed, this means that after rejecting RAN paging (by using the 5GS NAS Leaving procedure) the UE is put in RRC_Idle
Proposal 3: UE uses the 5GS NAS Leaving procedure in response to RAN paging to request connection release. At the end of the 5GS NAS Leaving procedure the UE is put in RRC_Idle.

## Slide 7: Summary of proposals
Proposal 1: NAS Leaving for 5GC/NR shall be supported in addition to RRC Leaving.
      Proposal implemented in S2-2103791
      Draft LS OUT in S2-2103792
Proposal 2: NAS Leaving with end state RRC_Inactive is not supported. Inform RAN2 of the decision so that they can discontinue their work on RRC Leaving with end state RRC_Inactive.
      Draft LS OUT in S2-2103792
Proposal 3: UE uses the 5GS NAS Leaving procedure in response to RAN paging to request connection release. At the end of the 5GS NAS Leaving procedure the UE is put in RRC_Idle.
      Proposal implemented in S2-2103790