## Slide 1: New SID on network enhancements for 5G broadband media services (FS_NE_5GMEDIA)
Hui Ni
Huawei

## Slide 2: New media services are emerging with challenging requirements
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity |  | 
 | Max allowed end-to-end latency | Service bit rate: user-experienced data rate | Reliability | # of UEs | UE Speed | Service Area
Cloud/Edge/Split Rendering | 5 ms (i.e. UL+DL between UE and the interface to data network) | 0,1 to [1] Gbit/s supporting visual content with 4K, 8K resolution and up to120fps | 99,99 % in uplink and 99,9 % in downlink | - | Stationary or Pedestrian | Countrywide
Gaming or Interactive Data Exchanging | 10ms | 0,1 to [1] Gbit/s supporting visual content with 4K, 8K resolution and up to120fps | 99,99 % | ≤ [10] | Stationary or Pedestrian | 20 m x 10 m; in one vehicle (up to 120 km/h) and in one train (up to 500 km/h)
Consumption of VR content via tethered VR headset | [5 to 10] ms | 0,1 to [10] Gbit/s | [99,99 %] | - | Stationary or Pedestrian | -
4K/8K VoD
Cloud VR/AR
The next wave of media services: high resolution, more interactive, more immersive
Various new video-based media services are emerging: cloud VR/AR, cloud gaming, 4K/8K VoD (Video on Demand), video-based remote control, machine vision etc.
Challenging requirements: ms level end-to-end delay, high reliability (e.g. 99.99%), and up to 1Gbps bitrate in a form of huge bursts. All these lead to challenges to 5G network to support large-scale deployments of such services.
Cloud Gaming
KPI for high data rate and low latency service (Source: 3GPP TS 22.261)
Media services contributed dominating traffic in the mobile network, the proportion can be over 70%.
Considering the stringent KPIs and high data rates of media services, it is proposed to investigate how the 5G network can be enhanced more efficient transmission of 5GS media services..
Video-based remote control

## Slide 3: 3GPP activities related to media services
SA1:
New Services and Markets Technology Enablers (SMARTER) (TS 22.261)
Study on Network Controlled Interactive Services (NCIS) (TR 22.842)
Service requirements for video, imaging and audio for professional applications (VIAPA) (TS 22.263)
  SA2:
  Work item on 5G System Enhancement for Advanced Interactive Services (SP-190564) : Introduces new 5QIs to identify the requirements from SA1 NCIS
  Study on enhanced support of Industrial IoT (IIoT) (SP-190932): Addresses the deterministic requirements of SA1 VIAPA
SA4:
Study on Extended Reality (XR) in 5G (TR 26.928): XR use cases
Feasibility Study on Typical Traffic Characteristics for XR Services and other Media (SP-200054): XR traffic characteristics.
RAN WGs
RAN1: Study on XR Evaluations for NR (TR 38.838): Traffic model, evaluation methodology and KPI, performance evaluation
RAN3: Study on NR QoE (Quality of Experience) management and optimizations for diverse services (TR 38.890): Define QoE management method for services including video streaming, VR, etc.
Some sporadic studies for media/video/XR services has been discussed/under discussion in RAN/SA WGs.
A systematic study in Rel-18 will be helpful to investigate how the characteristics of media services from E2E point of view can be leveraged by the 5GS for a more efficient support.

## Slide 4: Potential issues for study
1. Enhancements of 5GS QoS mechanisms considering media traffic information for more efficient transmission of media services
  (1) Frame-level integrated transmission
    The real-time media services are transmitted in the form of packet bursts, each burst carries one video frame.
    Frame-level integrated transmission may be helpful for media service transmission, scheduling and QoS control. e.g.
      Each burst consists of multiple packets. Loss of one packet may cause all other packets of the same frame become useless.
Example of XR traffic: 60fps, 16.67ms frame interval, and 1 frame with 60 IP packets
  (2) Layered QoS
    A media stream can include packets with different importance for the QoE of the service, e.g. I/P frames, base/enhancement parts, FoV(Field-of-View)/non-FoV packets.
    Layered QoS handling can improve media service transmission efficiency. e.g. by providing
      High priority/reliability for important packets.
      Selective drop of less important packets if congestion happens.

## Slide 5: Potential issues for study
  (4) Application-behavior awared QoS control
    When user initially starts the VoD playback or seeks to new segment of the video, higher bandwidth is beneficial to complete the buffer filling ASAP to reducing the waiting time of user.
    After that, the bandwidth can be reduced to a suitable value considering the average bitrate.
    Examples of architecture enhancements are given as following:
    Awareness of playback behavior from application
    Adjust QoS policy based on playback behavior in real time.
  (3) Uplink-downlink transmission coordination
    E2E performance (e.g. MTP delay for cloud VR) depends on RTT of uplink transmission and downlink transmission, instead of PDB of one-way transmission.
    Examples enhancements can be:
    Identify UL-DL packets belong to one user-server interaction.
    Uplink-downlink transmission coordination considering RTT.
1. Motion capture
2.Uplink transmission
5G Network
Cloud server
4.downlink transmission
3. Cloud processing
5. Display
E2E MTP delay

## Slide 6: Potential issues for study
  2. Mobility management enhancement considering the traffic pattern of media services
    The handover procedure may cause interruption in case huge frame are transmitting when HO happens.
    The traffic pattern can be considered for potential power saving on UE/RAN part.
  3. Utilize multicast mechanism for XR (AR/VR) transport
    To investigate how to utilize multicast-unicast transmission for XR services to improve the network capacity, e.g. transmit the background scene via multicast.
  4. Coordination with upper layer protocols
    To investigate potential coordination with upper layer (e.g. TCP, UDP, SRT) to improve end-to-end performance. E.g. For TCP-based media service, the re-transmission may cause long delay and slow startup of TCP window, which may be not necessary for some uncritical packet in the media traffic.
  5. Support of network slice for mobile media.
    To investigate whether a network slice for mobile media is needed for supporting the functionalities specific for media services.
  6. Definition of Network XQI (XR Quality Index)
    There is no network level metric directly reflecting network transmission impact (including RAN and CN) on XR user experience.
    The network XQI is possible defined to evaluate the the QoE of mobile media services running over the 5GS considering network factors, e.g. PDB, PER.,

## Slide 7: Rel-18 study proposal on architecture enhancements for 5G media services
Study the R18 architecture enhancements for media services with the following objectives:
Mobile Media Slice
(Media specific transmission enhancement)
NEF/PCF/
NWDAF
UPF
Media level semantics
Perception of media level characteristics
Media
Application server
SMF
AF
User device
RAN
Media
Application client
  1) Enhancements of 5GS QoS mechanisms considering media traffic information for more efficient transmission of media services, including, e.g.:
    - Support Frame level integrated transmission considering the traffic burst pattern and/or dependency between packets within a media stream.
    - Support Layered QoS handling for different packets within a media stream considering importance of packets on media layer.
    - Support QoS control with low latency based on media application-behavior, e.g. initiating playback, seeking or buffer refilling.
    - Support uplink-downlink transmission coordination to meet RTT (Round-Trip Time) requirement.
  2) Mobility management enhancement considering the traffic pattern of media services.
  3) Utilization of multicast mechanism for XR (AR/VR) transmission.
  4) Co-ordination with upper layer protocols, e.g. TCP/UDP/QUIC/SRT.
  5) Support of network slice for mobile media.
  6) Definition of Network XQI (XR Quality Index) for evaluation the QoE of mobile media services considering network factors, e.g. PDB, PER.
    Note: The SA2 work shall be coordinated with other WGs, e.g. RAN 1/2/3, SA3, SA4.

## Slide 8: Thank You!