## Slide 1: Discussion on ATSSS Enhancements
Lenovo, Motorola Mobility

## Slide 2: Potential Key Issues for ATSSS/R18
Enable unsupported use cases
    An MA PDU Session using a Branching Point or UL Classifier is not currently specified. How can it be supported?
    An MA PDU Session to an LADN is not currently supported. How can it be supported?
Improve / enhance the ATSSS functionality
    Define the MPTCP proxy outside from UPF.
    Define a high-layer steering functionality for non-TCP traffic based on QUIC (initially, without the multipath extensions).
    Other enhancements, e.g. PMF enhancements, steering mode enhancements, improved GBR support, etc.
Support new use cases
    A roaming UE cannot use ATSSS if the VPLMN does not support MA PDU Sessions. Can the UE use ATSSS without establishing an MA PDU Session?
    An MA PDU Session contains two non-3GPP access paths, e.g. one path [using NWu via an SNPN] and another path [using NWt via trusted non-3GPP access].
    An MA PDU Session contains more than two paths.

## Slide 3: Potential Key Issue #1
  Enhancements to be studied
    Support an MA PDU Session using a Branching Point or UL Classifier
  Motivation
    Enable ATSSS towards remote hosts and towards edge hosts using a single MA PDU Session
ATSSS-LL

## Slide 4: Potential Key Issue #2
  Enhancements to be studied
    Allow a MA PDU Session to be established towards an LADN
    Relevant to Edge Computing
  Motivation
    Enable ATSSS when the UE accesses services in local area data networks (LADNs)
    These services are accessible only when the UE is localed in a given “service area”
  Problem
    When the UE is idle over 3GPP access and gets out of the LADN service area, the UE may keep exchanging data over non-3GPP access (although it shouldn’t). To avoid this problem, it was decided to prohibit MA PDU Sessions towards LADNs in Rel-17.

## Slide 5: Key Issue #3
  Enhancements to be studied
    Allow the ATSSS proxy to be located outside the UPF
  Motivation
    Decouple the ATSSS proxy functionality from the UPF functionality
  ATSSS proxy = MPTCP proxy and/or MASQUE proxy (if QUIC can be used for transport)
  Where is the PMF located in the network?
  How does the SMF receive the proxy information (e.g. IP@, port, type)?
  Apple, Charter, Comcast support this
  Can the MPTCP proxy be deployed by a 3rd party?

## Slide 6: Key Issue #4
  Enhancements to be studied
    Define a high-layer steering functionality for non-TCP traffic based on the QUIC protocol (even without the multipath extensions)  continuation of KI#2 from the Rel-17 study
  Motivation
    It is worth considering a high-layer alternative to ATSSS-LL because:
      When ATSSS-LL is used, the traffic distribution is performed by low-layers transparently to the apps. The apps do not know and cannot control the traffic distribution. In some scenarios, this is problematic.
      QUIC maintains its own delay/loss measurements, so PMF measurements may not be required or may be reduced.
      Easy migration path towards MPQUIC: Traffic splitting can easily be supported later when the QUIC multipath extensions are defined by IETF.
  QUIC cannot support traffic splitting without the multipath extensions, but QUIC can support traffic steering and switching based on policy rules (ATSSS/N4 rules).
  The Connect-UDP (this is WG draft in IETF) and Connect-IP drafts could be considered in order to enable a multi-access transport over QUIC.
  QUIC with NULL encryption will be defined by SA3, e.g. by specifying a "3GPP 5G profile for QUIC”.
  Consider the MASQUE proxy outside the UPF in key issue 3

## Slide 7: Key Issue #5
  Placeholder for additional small enhancements
  In Rel-17, time was limited for considering more enhancements
  PMF enhancements, e.g.
    Perform the measurements more efficiently
  Steering modes, e.g.
    Additional / enhanced steering modes
  Improvements for GBR traffic, e.g.
    Splitting the GBR traffic across accesses

## Slide 8: Key Issue #6
  Enhancements to be studied
    Consider supporting ATSSS without a MA PDU Session
  Motivation
    A roaming UE cannot use ATSSS if the VPLMN does not support MA PDU Sessions.
  ATSSS could be supported either with (a) two separate single-access PDU Sessions, or (b) with one single-access PDU Session and a connection using NSWO.
  Is this something that can be already supported?

## Slide 9: Key Issue #7
  Enhancements to be studied
    Support an MA PDU Session using two non-3GPP access paths, e.g.
      One path [using NWu via an SNPN] and another path [using NWt via trusted non-3GPP access] or
      One path [using NWu via an SNPN] and another path [using NWu via untrusted non-3GPP access]
  Motivation
    Enable traffic steering and switching between two N3GPP accesses (e.g, NWu and NWt). This can simplify mobility procedures.
  UE has two registrations to the same PLMN via non-3GPP access.
An example deployment configuration with a fixed broadband access to the same factory allowing NWt usage (ref: 23.316 / fig 4.10-1)

## Slide 10: Key Issue #8
  Enhancements to be studied
    Support an MA PDU Session with more than two paths.
  Motivation
    Simplifying the overall mobility procedure when UE is switching traffic from one path to another by using the same ATSSS procedure.
  UE has three registrations to the same PLMN, one via 3GPP access and two via non-3GPP access. Currently not supported.
1. Transition between Nwu and Uu requires 3GPP-N3GPP handover procedure
2. Transition between two Nwu requires MOBIKE
3. ATSSS feature allows data delivery to both 3GPP and N3GPP radios without mobility procedure
3GPP pieces:
- N3IWF: -Local mobility anchor within untrusted non-3GPP access networks using MOBIKE per IETF RFC 4555 [57].
- if the UE supports IETF RFC 4555 [23], the UE may include the MOBIKE_SUPPORTED notify payload as specified in IETF RFC 4555 [23].
4. If UE is able to establish another Nwu (i.e., two independent Nwu) or a new NWt, the use of both radio access paths (3GPP + N3GPP) in this combination is not possible because only one link specific address is allocated to N3GPP leg from CN side in current ATSSS feature
IP1
IP2
IP3