## Slide 1: Study on Architecture Enhancement to support Ranging-based services and relative positioning
S2-2104673
Xiaomi

## Slide 2: Definition of Ranging
Ranging refers to the determination of the distance between two UEs and/or the direction of one UE, i.e. target UE, from the other one, i.e. observer UE, via direct communication connection.
  Relative positioning between 2 UEs can be derived based on ranging
The observer UE has a zenith and a reference direction, and its reference plane is the plane orthogonal to the zenith.
The direction of the target UE to the observer UE is represented by the Azimuth direction and the Elevation direction.
  Azimuth direction: the angle formed between a reference direction and a line from the observer UE to target UE projected on the reference plane of the observer UE.
  Elevation direction: the angle above the reference plane of the observer UE.
Source: TR 22.855

## Slide 3: Use case 1 Smart Home TV control
Both UE and smart TV have ranging capability
Ranging of UE to the TV reference point
  Distance: d
  Azimuth direction: a1
  Elevation direction: e1
Ranging of TV reference point to the UE
  Distance: d
  Azimuth direction: a2
  Elevation direction: e2
With (a1, e1), (a2, e2), and d, the smart TV can derive the area of the TV screen where the UE points to, so that it can determine where to place the curser and which content the user selects
Sports
News
Movies
Education
Game
Shopping
TV reference point

## Slide 4: Use case 2 Remote Access Right authorization
CICI’s door, Alice’s UE and Bob’s UE are all ranging capable
Alice is a visitor of CICI building, who has no access right of the door.
Bob, who is a CICI stuff, triggers ranging service to monitor ranging of Alice’s UE to the door.
When Alice’s UE is in 10cm distance to CICI’s door, Alice is authorized the access right.

## Slide 5: Use case 3 Museum Tour
Under each painting in the museum, there’s an IoT device which is ranging capable
The Museum Tour Server monitors ranging of the IoT device of each painting to the UE.
When UE moves close (<5m), points to “The Starry Night” and triggers ranging service, Museum Tour Server knows the ranging result and plays the introduction of “The Starry Night” to the UE, because the Azimuth direction < 10 degree, and the Distance < 5m.
UE reference direction
Azimuth direction < 10 degree
Distance < 5m
5GS
Museum Tour Server

## Slide 6: Use case 4 Stuff tracking based on energy efficient ranging
Jerry (Tom’s pet dog), wearing a smart dog collar, was lost in a place far away from Tom. The smart dog collar is a ranging capable IoT device powered by a coin battery
Tom couldn’t get Jerry’s location using LCS service, which is not supported by the smart dog collar, and there’s no network coverage.
Jerry was discovered by Tom’s Drone, which is ranging capable and is under the network coverage.
The Drone reported to Tom’s smart phone (Drone controller) its location (based on Location Service) and Ranging result of Jerry’s smart ranging capable IoT device.
Tom’s smart phone derived the location of Jerry based on Drone’s location and Jerry’s ranging result to the Drone, and then Tom found Jerry.

## Slide 7: Use case 5 Immersive sound based on multiple-UE ranging
Speaker A/B/C and Tom’s cell phone are ranging capable. No-LoS paths are between Speaker B & Tom’s cellphone and between Speaker B and Speaker A.
Speaker A determines the relative position of speaker B through coordinated ranging with speaker C, i.e. Speaker A uses the ranging result of Speaker A to Speaker C, and the ranging result of Speaker B to Speaker C to calculate/calibrate/corroborate the ranging result of Speaker A to Speaker B.
Speaker B also determines relative position of Tom using the same mechanism.
The speakers adjust the sound field to provide an immersive audio experience to Tom.

## Slide 8: Scenario
Ranging-based positioning and services can be supported with or without 5G coverage.
If licensed band is used, it shall be fully under operator control.
Source: TR 22.855

## Slide 9: Ranging service flows (examples)
UE initiated Ranging service flow
AF initiated Ranging service flow

## Slide 10: Ranging related study in SA1
The SA1 SID Ranging (SP-200575) has reached 85% completion up to SA#91e.
  Functional requirements and Performance requirements that have architecture impact are identified
Ranging WID approved at SA#91e, expected to be completed at SA#92e.
TS 22.186 (Enhancement of 3GPP support for V2X scenarios) has required that “The 3GPP system shall support relative lateral position accuracy of 0.1 m between UEs supporting V2X application.
  This is a R16 requirement, however, it has not been realized in R17.

## Slide 11: Ranging related Study in RAN2
FS_NR_pos_cov (RP-201518, Study on scenarios and requirements of in-coverage, partial coverage, and out-of-coverage NR positioning use cases) R18 SID approved to study on positioning use cases, requirements and scenarios for V2X and public safety UE in in-coverage, partial coverage, and out-of-coverage
Similar architecture enhancement to 5GC as that of supporting Ranging-based Positioning and Services is foreseen.
Proposal: Develop a common architectural enhancements to 5GC for V2X and public safety UE use cases as well to avoid potential divergence or overlapped work.

## Slide 12: Relationship with ProSe
ProSe features consist of: ProSe discovery, ProSe Direct Communication, ProSe UE-to-Network Relay and ProSe UE-to-UE Relay.
Ranging will reuse a subset of ProSe features with the enhancement and optimization, e.g.:
  ProSe discovery and communication based on distance and direction
  Service authorization and policy/parameter provisioning enhanced with ranging parameters
  …
Solutions to support Ranging specific requirements, e.g.
  QoS handling for ranging
  Discovery of coordinated ranging UE
  Multiple UE coordinated ranging for no LOS path
  Ranging service request initiation and service exposure
  Energy efficient UE ranging services and operation for low power consumption UEs
  …
Proposal: While Ranging studies solutions to support Ranging specific requirements, it will reuse ProSe solutions as much as possible.

## Slide 13: Relationship with eLCS
eLCS defines service-based architecture used for location services in the 5G system, and corresponding Network Functions (NFs), NF services and procedures, to meet the service requirements defined in TS 22.261 and TS 22.071
eLCS is to develop solutions on how to acquire UE absolute location.
Ranging refers to the determination of the distance between two UEs and/or the direction of one UE, i.e. target UE, from the other one, i.e. observer UE, via direct communication connection.
Ranging capabilities may be used by eLCS to determine UE absolute location
  When UE is out of network coverage
  To acquire more accurate UE location
Solutions on ranging based services and relative positioning are common.
Proposal
  Common solutions are developed for ranging based services and relative positioning.
  eLCS focuses on the study of how to determine UE absolute location and refers to ranging procedures for details when relative positioning is invoked.
  Ranging focuses on developing solutions on ranging based services and relative positioning.

## Slide 14: Conclusions
A SID is needed in SA2 to enable Ranging-based services and relative positioning over direct communication for commercial, V2X and public safety use cases in in-coverage, partial coverage, and out-of-coverage of 5G network, with the following architectural considerations:
  Overall architecture reference model
  Service authorization and policy/parameter provisioning for a UE or a group of UE
  Assurance of UE Ranging privacy;
  Ranging device discovery and service execution between 2 UEs and coordinated ranging among multiple UEs to enable ranging between UEs with no LOS path;
  QoS handling for different use case scenarios based on stage 1 performance requirements, in terms of ranging accuracy, availability, latency, effective ranging distance, coverage, NLOS/LOS, relative UE velocity, ranging interval, number of concurrent ranging operation for a UE, number of concurrent ranging operation in an area;
  Ranging service request initiation and service exposure;
  Energy efficient UE ranging services and operation for low power consumption UEs;
  Enabling ranging service between UEs subscribed to different operators and for roaming users;
Time schedule: TBD