## Slide 1
MBS session Information in NRF, UDM and UDR - For discussion

## Slide 2: Issue 1
How to provide preconfigured information about MBS session?
  TS 23.247, 4.2.1 Multicast data provisioning
    - MBS Session Configuration: MBS Session Configuration is used by the AF to configure the MBS Session towards 5GC, which may also include TMGI allocation procedure. This step is optional.
  TR 23.757 key issue 1 conclusions:
    For multicast service parameters storage, the UDR shall be able to store the AF provisioned or preconfigured service parameters per MBS session.
How to provide input for policy rules for an MBS session to PCF?
Proposal 2: Store information about MBS sessions in UDR that enables policy decisions about those MBS sessions

## Slide 3: Issue 2
Where to store configuration about location dependent MBS services?
  TS 23.247:
    6.2 Local MBS service Information about different MBS service areas for a location dependent MBS service may be provided by one or several AFs or may be configured. Different ingress points for location dependent points for the MBS session are supported for different MBS service area dependent content of the MBS session; different MB-SMFs and/or MP-UPF may be assigned for different MBS service areas in an MBS session.
    7.2.4.2.1 Multicast context and Multicast flow setup/modification via PDU Session Modification procedure When SMF requests multicast context via Nnrf_NFDiscovery request (MBS Session ID), the NRF provides information about location areas stored within the multicast context, via Nnrf_NFDiscovery response (MB-SMF ID, Area Session ID, location area). The SMF selects location dependent multicast context information based on the location area where the UE is residing
    7.2.4.2.2 Configuration for local MBS NEF requests storage of multicast session at NRF and provides multicast session ID, selected MB-SMF ID and location area.
  Currently NRF is used, but NRF contains NF profiles and is used for discovery of NFs rather than information about multicast sessions
    NRF is not well suited for preconfigured information about multicast session, because an MB-SMF might not be assigned.
    The NRF discovery service allows for a discovery of NF profilers and a subscription of profile changes of MB-SMF profiles. However, NF profiles contain lots of information and can become very large. CT4 introduced message fragmentation and allows the NRF to truncate information to cope with such issues. Discovery results are supposed to be cached to avoid a need for constant discoveries.
    NRF thus not meant for fast-changing information
    If several MB-SMFs may be involved, multicast context information would be split into several MB-SMF profiles
Proposal 2: Store information about location dependent contents of multicast session in UDM

## Slide 4: Issue 3
Subscription to multicast services?
  TS 23.247:
    6.5 Subscription to multicast services The user's profile in the UDM contains the subscription information to give the user permission to use multicast services. The user may have following subscription for multicast services:
    - Allowed to join any multicast service;
    - Allowed to join the indicated specific multicast service(s).
    Editor`s note: It is ffs how to express that some multicast services are allowed to be accessed by any user and others only by a restricted set of users. It is ffs if the information about users allowed to join a multicast service should be organized per multicast service instead of per user.
  Scenario in editor´s note seems realistic and can hardly be expressed via per UE subscription information: If a specific multicast service is not listed, is the UE not entitled to use it because it is not listed, or is the UE entitled to use it because it is meant for any UE?
Proposal 3: UDM needs to contain per multicast service information to express whether any UE is entitled to use multicast service, and possibly with information about groups of Ues or Ues enbtitled to use it

## Slide 5: Issue 4
Where to store source specific IP multicast address as multicast session IDs?
  The following conclusions for MB-SMF detection and join were agreed in TR 23.757:
    MB-SMF is discovered by querying NRF using multicast session ID:
    - The MB-SMF registers its NF profile, which includes e.g. S-NSSAI, DNN and MB-SMF service area, to the NRF. The NEF/MBSF discovers the MB-SMF, if not locally configured, by querying the NRF using these information during multicast/broadcast session configuration.
    - When a multicast/broadcast session is configured/established, the MB-SMF updates its NF profile with the multicast session ID to the NRF.
    - During UE join procedure, if needed, the SMF retrieves the MB-SMF ID from the NRF using the multicast session ID and, selects an MB-SMF based on the MB-SMF information returned by the NRF. For local MBS services, the SMF takes MB-SMF service area into account when selecting the MB-SMF.
    NOTE x1: It needs to be verified in the normative phase whether the NRF is suitable to store dynamically changing multicast session IDs and possible area session IDs associated with the multicast session IDs.
    NOTE y2: It needs to be decided in the normative phase whether a database to hold information about the multicast session is required.
    Source specific IP multicast address or TMGI may be used as MBS Session ID in NAS messages exchange between a UE and a CN when the UE requests to join/leave a multicast session.
    A TMGI is allocated also for MBS multicast sessions that the UE joined with a source specific IP multicast address. The TMGI is sent to the UE and used in other signalling messages between RAN, CN and UE.
  NRF is not well suited to store source specific IP multicast addresses in MB-SMF profiles:
    The NRF discovery service allows for a discovery of NF profilers and a subscription of profile changes of MB-SMF profiles. However, NF profiles contain lots of information and can become very large. Discovery results are supposed to be cached to avoid a need for constant discoveries. IP multicast addresses are allocated by external entities (AF) and can thus not easily be pre-allocated or distributed in advance to MB-SMFs. In some cases, source addresses may be configured based on business agreements., but this does not hold for all cases. That would result in high load by distributing the entire very large MB-SMF profile each time a new source specific IP multicast addresses is added to the MB-SMF profile. In comparable previous cases, the NRF was not used to store such information:
      The NRF does not contain any information about subscribers or PDU sessions served by SMFs and AMFs. (The UDM holds such information)
      The Nudr_GroupIDmap service was introduced to allow NF consumers to retrieve a NF group ID corresponding to a subscriber identifier. This is used e.g. for the HSS discovery based on IMS public identities (which can be fragmented due to number portability)
Proposal 4: Store source specific multicast addresses and related TMGIs in UDM as part of the information about the multicast session

## Slide 6: Issue 5
Selection of 5MBS capable SMF by AMF?
  TS 23.247:
    6.5 Subscription to multicast services The SMF selection subscription data is provided by the UDM to the AMF as described in clause 4.2.2.2 of TS 23.502 [6].
    Editor`s note: It is ffs if the SMF selection subscription data need to be extended.
  Technically endorsed S2-2103074 against TS 23.247: based on the indication DNN and S-NSSAI use for of establishing a PDU Session associated with multicast session(s), and/or an indication that the user is allowed to join multicast sessions in the UDM the AMF selects an SMF capable of handling multicast sessions based on DNN and S-NSSAI, or locally configured data or a corresponding SMF capability stored in the NRF. For indirect discovery, the AMF requests the SCP to select an SMF capable of handling multicast sessions. Editor's note: Whether the indication in the UDM is needed or not is FFS.
  Taking only DNN and S-NSSAI seems to assume that operator uses specific slides for PDU sessions that allow a multicast join. On the other hand, the PDU session can also contain contents unrelated to multicast. It seems too restrictive to require all operators to deploy specific slices to support multicast. On the other hand, not all UEs may be multicast capable or have a subscription for multicast services. Thus an entry in the SMF selection subscription data about need for multicast support seems appropriate. This can be considered by the AMF in combination with DNN and S-NSSAI to decide whether to select an 5MBS capable SMF
Proposal 5: Extend the SMF selection subscription data with an indication whether multicast support is required.
Proposal 6: Extend the SMF profile in the NRF with an indication about multicast support

## Slide 7
Thank You!