## Slide 1: Accelerate recovery of IMS voice service after S1 disable
Huawei, HiSilicon, China Telecom, China Unicom

## Slide 2
Overview
Solution introduced in #143 meeting partially solves the issue, but the drawback is unacceptable.
Case 1： Operators do NOT support 3G/2G
The UE ends up with no voice service, before the S1 mode disable timer expires.
New solution needs to be developed to accelerate the UE to recover voice service, or increase the possibility to recover voice service.
Case 2： Operators support 3G/2G
UE has to remain in 3G/2G, before the S1 mode disable timer expires.
New solution can be developed to configure the UE to stay 5G, and provides the voice service when S1 mode is disabled.

## Slide 3: Case 1: No 3G/2G
Assumption:
1）Network only supports VoLTE, but not VoNR.
2）UE is set to "voice centric" , i.e., normal smartphone.
Solution introduced #143
In case the UE has signalled that S1 mode is disabled for a network that only supports IMS voice via EPS Fallback, the AMF will indicate that IMS voice over PS session is not supported over 3GPP access.
Scenario:
1） The UE initiates TAU procedure/Attach, but the procedure fails for 5 times. For example, the UE enters an area like an underground garage, or purely unstable radio link status.
2) The UE disables its S1 mode. The default S1 mode (E-UTRA) disable time is 12 mins (i.e., T3402). The UE selects other RATs of the registered PLMN.
3) The UE registers to 5GC. Due to the "IMS voice over 3GPP is not supported" and the UE is "voice centric" , the N1 mode of UE is disabled.
4) The UE tries other RAT(i.e., 3G/2G). But UE fails, as the operator does not support 3G/2G.
5) The UE tries other PLMN other than HPLMN. But UE fails, as no other PLMN can be selected.
6) The UE enables its N1, and re-camps on the Registered PLMN(i.e., HPLMN).
Issues：
Due to “IMS voice over 3GPP is not supported”, The UE considers the network is UNCAPABLE to provide IMS voice service. Therefore, it will not try to get voice service before the S1 disabled timer expires, e.g., even when the radio condition of the UE recovers.
Observation:
The solution introduced in #143 does not completely resolve the issue.
EPC
5GC
① 5 times failure
② S1 disable ; Select NR and register in 5GC.
④ Selects other RAT, fails
⑤ Selects other PLMN, fails
⑥ Enable N1, remains in 5GS
Issue：
The UE considers the network is UNCAPABLE to provide IMS voice service and will not try.
③ IMS over 3GPP access is not supported

## Slide 4
Case 1: No 3G/2G
Objective:
New solution enables the voice-centric UEs to recover the IMS voice service, after The UE enables its N1 and re-camps on the Registered PLMN(i.e., HPLMN).
Solutions:
SA2:
1) In addition to "IMS voice over 3GPP is not supported" , provide to the UE the networks CAPABILITY of EPS fallback.
CT1:
1) When the UE enables its N1 and re-camps on the Registered PLMN(i.e., HPLMN), the UE re-enables the S1 mode capability, so that the UE may obtain the IMS voice services.
2) Describe the detailed handling of the UE about the new EPS fallback capable information in corresponding clauses.
EPC
5GC
① 5 times failure
② S1 disable ; selects 5GC.
④ Selects other RAT, fails
⑤ Selects other PLMN, fails
⑥ Enable N1, remains in 5GS
⑦ UE re-enables its S1 mode capability as the network is EPS fallback capable.
③ IMS over 3GPP access is not supported and EPS fallback capability.

## Slide 5
Case 2： With 3G/2G
Scenario :
Same step from 1) to 3)
4) The UE tries other RAT(i.e., 3G/2G). The UE stays in the 3G/2G network.
Issues：
The limited rate speed in 3G/2G is not acceptable. Users will complain to UE vendors/network vendors if they find that the UE is staying 3G/2G.
Objective:
Avoid the UE to stay in 3G/2G, unless there is voice service to be happening.
Solutions:
CT1:
1) The 5G/4G of equivalent PLMN has priority over 3G/2G of the registered PLMN.
2） If no other PLMN can be selected, the UE still stays in 5G and re-enables its S1 mode capability.
- The possibility of voice call is low.
- For MO voice service, the UE tries EPS fallback. If fails , switch to 3G/2G.
- For MT voice service, the network tries EPS fallback. If the UE detects a failure,
switch back to 3G/2G.
EPC
5GC
① 5 times failure
② S1 disable ; Select NR and register in 5GC.
④ Selects other RAT, stays in 2G/3G
Issue：
The limited rate speed in 3G/2G is not acceptable.
③ IMS over 3GPP access is not supported

## Slide 6: Annex