## Slide 1: ATSSS_Ph2 Status Report to be updated after the end of SA2#145e
Apostolis Salkintzis
Lenovo

## Slide 2: ATSSS_Ph2 status after SA2#144e (1/3)
WI Code | Work Item Title | WP | Target Date | WID#
ATSSS_Ph2 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture; Phase 2 | 55%(#143E) -> 85% | Jun, 2021 | SP-200977
General
  This was the second meeting for ATSSS_Ph2
  Good progress achieved with 13 CRs approved against TS 23.501/502/503
  There are still some open issues (see next slide) but work remains on track
  Plan to resolve the open issues at SA2#145E
  No request for exception is expected

## Slide 3: ATSSS_Ph2 status after SA2#144e (2/3)
WI Code | Work Item Title | WP | Target Date | WID#
ATSSS_Ph2 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture; Phase 2 | 55%(#143E) -> 85% | Jun, 2021 | SP-200977
Task 1.1: PMF Enhancements to support per-QoS measurements
  Good progress and several issues were resolved. However, there is still a challenging and controversial open issue: How can a PMF message be transmitted on the target QoS flow?
Task 1.2: Load-Balancing without pre-defined split percentages
  The “Autonomous load-balance indicator” has been introduced in TS 23.501 and in TS 23.503.
  Completed (100%)
Task 1.3: UE-assistance indication
  The “UE-assistance indicator” and the supporting PMF enhancements have been introduced in TS 23.501/503.
  Open Issues: (a) Whether it can be applied to additional steering modes, (b) whether the UE can use arbitrary split percentages, (c) details about the “correlation information”.
Task 1.4: Threshold conditions
  Good progress. Has been agreed that threshold values for RTT and/or PLR can be provided with load-balance and priority-based steering modes. Completed, although proposals on ‘hard’ thredholds may still show up.
Task 2.1: Supporting MA PDU with 3GPP access leg over EPC and Non-3GPP access leg over 5GC
  1 CR agreed against TS 23.501 and 2 CRs agreed against TS 23.502.
  Completed (100%)

## Slide 4: ATSSS_Ph2 status after SA2#144e (3/3)
  RAN impacts and dependencies:
  None
Contentious Issue:
  None
Focus for the Next Meeting (SA2#145e):
  Work to resolve the open issues
Overall Plan:
  Coordinate work and improve collaboration to reach full completion after SA2#145e

## Slide 5: ATSSS_Ph2 Status at SA#92-e
WI Code | Work Item Title | WP | Target Date | WID#
ATSSS_Ph2 | Access Traffic Steering, Switch and Splitting support in the 5G system architecture; Phase 2 | 55%(#143E) -> 85% | Jun, 2021 | SP-200977
Progress since SA#91-e:
  ATSSS_ph2 is presented to SA for the first time (normative work initiated at SA2#143e)
  Good progress achieved in SA2#143e and SA2#144e
RAN impacts or dependencies:
  None
Next steps:
  Continue work to resolve the open issues
  Aim at reaching full completion after SA2#145e

## Slide 6: backup