## Slide 1
5SEAS:
5G System Evolution for
AI/ML-based Services
May 2021

## Slide 2: Summary of SA1 FS_AMMT Potential Impacts on SA2 (I)
Session-specific model transfer split computation operations
  [P.R.5.5-001] Based on operator policy, the 5G network shall provide the means to allow an authorized third-party to monitor the resource utilisation of the network service that are associated with the third-party
  [P.R.5.5-002] Based on operator policy, the 5G system shall be able to expose QoS information and QoS update conditions to an authorized 3rd party
AI model management as a service
  [P.R.6.4-001] Subject to user consent, operator policies and the regional or national regulatory requirements, the 5G system shall be able to provide the capability to expose information (e.g. measured data rate, delay, network analytics results) to an authorized third-party application to support the training and monitoring of the AI/ML models
Shared AI/ML model monitoring
  [P.R.6.6-001] The 5GS shall be able to transfer an updated AI/ML model from the shared AI/ML model provider to the shared AI/ML model user within [1s-1min] latency for AI/ML models of a maximal size of [100-500] MB.

## Slide 3: Summary of SA1 FS_AMMT Potential Impacts on SA2 (II)
Prediction of AI/ML model distribution
  [P.R.6.7-001] Subject to user consent, operator policy and regulatory constraints, the 5G system shall support the provision of monitoring information or analytics information to a trusted 3rd party AI/ML server for allowing this 3rd party AI/ML server to make a prediction for a suitable AI/ML model to be downloaded to the concerned UE.
Group Performance “Flocking” Use Case
  [P.R.7.4-001] The 5G system shall be able to support ‘aggregated performance’ for a group of UEs where the worst performing member defines the performance of the entire group. E.g. the 5G system could achieve performance for the entire group so as to avoid members achieving either significantly less or more performance than others in the group.
  [P.R.7.4-002] The 5G system shall be able determine whether a required QoS for each member in a group can be maintained.
  [P.R.7.4-003] The 5G system shall be able to expose QoS information for a group of UEs to an authorized service provider.

## Slide 4: Proposed SID: 5G System Evolution for AI/ML-based Services (5SEAS)
Background
  Device-based AI/ML training/inference is expected to be used for both 1) performance optimization in NW domain 2) AI-based service (e.g. connected car, voice/image recognition) in application domain
  Data for AI-based services (model, training data) may require different QoS treatment from other internet traffic
  Rel-17 5GS plans to support AI/ML training and inference as sub-functions of NWDAF, whereas there is no support for device-based ML training/inference and inference feedback from UE to the network or vice versa
Required improvements
  Architecture/functional improvement to support for device-based AI/ML training/inference (e.g. split/federated learning)
  Support exposure of network status information (network load, congestion, etc.) to enhance UE AI/ML performance
  Framework for network distributed learning across different 5GS entities (e.g. UE, 5GC NF, AF).
NEF/
SMF
5GC NF (AF, NEF, NWDAF, …)
UPF
Data NW
5GC
UE
AI-based
Application
Service
Req for AI data transfer
AI data (in container)
Expose network status to AS
Expose network status to UE
On-device
ML Training/
Inference
(task offloading, Federation Learning)
Feedback of AI/ML performance

## Slide 5: 5SEAS Objectives
Objective 1: Architectural and functional extensions to support device-based ML training/inference and performance monitoring feedback in 5GS
  Support an inference feedback mechanism from AI/ML model user (e.g. application client running on the UE) to the AI/ML model provider (e.g. 5GC NFs, AF).
  Support local model training at the AI/ML model user and distribution of the local model to the AI/ML model provider.
  Support monitoring for resource utilisation at AI/ML model user (e.g. battery, quota, etc.).
Objective 2: Enhancement of network-assisted information/parameters
  Support exposure of network status information (network load, congestion, etc.).
  Support enhanced CN-assisted parameters (e.g. expected UE activity behaviour, expected HO behaviour, expected UE mobility, etc.).
Objective 3: Functional enhancements such as partitioning, aggregation, distribution, and execution of AI/ML models, to support network distributed learning across different 5GS entities (e.g. UE, 5GC NF, AF).