## Slide 1
2021.4
SID – Study Network of Networks

## Slide 2
Combination of 2 SA1 studies
  PIN & RESIDENT
Personal IoT Networks
  2 eco systems studies, Smart Home/Office and Wearables. PINs consist of collection of PIN Elements that mainly use PIN direct connections and can be managed and created locally or in the 5G core network.
    Terms can be found in TR 22.859 & S1-211085
RESIDENT
  Similar to the Smart Home / Office but more centered around traditional home/office LANs (i.e. local network) with the inclusion of a home base station that allows legacy devices to obtain service(s) from the local network.
What is a NETNET

## Slide 3
(Pro)consumers / Enterprises are building more and more networks, millions of devices creating traffic.
  Underlying technologies (WLAN, ZigBee®, Z-wave®, Bluetooth®), even though mature:
    challenge to deploy, maintain, migrate devices in networks.
    Security and data privacy are not high See speaker notes for references
    No roaming support (see slide 9 for one usecase)
    See speaker notes for more details
    Multiple technologies/ solutions with no interoperability
  Operators cannot identify any of these devices and thus cannot offer any specific services e.g. management, security, bundling packages, roaming etc.
In building coverage can be challenging as frequency increases, home base stations can help fill these gaps whilst supporting legacy UEs. They can also offload traffic when that traffic stays “local”.
Motivation
Notes: These references cover aspects of deployment, maintenance, security etc
https://www.entrepreneur.com/article/362497
https://www.mckinsey.com/spcontent/connected_homes/pdf/mckinsey_connectedhome.pdf
https://www.iotworldtoday.com/2019/12/23/overcoming-the-smart-home-markets-top-challenges/ (you need to enter some details to get a free copy of this report)
https://www.sciencedirect.com/science/article/pii/S1877050919316680
https://www.mcafee.com/blogs/other-blogs/mcafee-labs/the-tradeoff-between-convenience-and-security-a-balancing-act-for-consumers-and-manufacturers/
Roaming
Roaming is the ability to take a PIN Element e.g. smart earbuds or headset that is a member of one NETNET and easily join another NETNET (TR 22.859 see usecases 5.7, 5.11 and 5.2) or be Nomadic (see slide 9)

## Slide 4
Rel-18 FS_PINs (TR22.259) & FS_RESIDENT (TR 22.258) contain use cases and potential requirements (PRs)
  PIN – Use cases (SmartHome, Nomadic device [dog collar], Tour guide, games night, baby monitor, local service hosting etc)
  RESIDENT – Use cases (indoor base station + guest access+ PLMN sharing + multi-connectivity, local breakout, QoS, local service hosting etc)
  PRs cover - Onboarding, Connectivity, local device configuration and management, self built networks, resilient network design, roaming, local application hosting, concurrent RAT usage, guest access, dynamic network creation and evolution.
Studies to be combined into 1 WID, NETNET, expect 80% completion September 2021.
SA1 Work

## Slide 5
Expect to start with other studies
  12 TUs for study phase
Send to SA plenary information SA#95 March 2022
Approval SA#96 June 2022
Timeline

## Slide 6
Backup slides

## Slide 7
Definitions
NETNETs consist of collection of NETNET Elements.
  To make reading easy these will be called PIN Elements (see TR 22.859 & S1-211085) except for the Home base station which is called a Premises Radio Access station (PRAS) (See TR 22.858)
PIN Elements can be UEs or devices. Devices* use PIN Direct connections (S1-211095) to communicate (PC5 with or without out UICC).
  * When a Device has Uu it is a UE.

## Slide 8
Example smarthome NETNET
NETNET
Home Automation
GW
Relay
Relay
Relay
Relay
Notification
On smartphone
Ethernet
5G Core Network
Guest PIN
Element
(Uu)

## Slide 9
Example Nomadic (roaming) device (e.g. PIN Element)
Guest PIN
element
Relay PIN Element
Light bulb PIN Element
Door Bell PIN Element
Gateway PIN Element
Direct device connection
(operator Managed)
Direct device connection
(non operator Managed)
Direct network connection
Relay PIN Element
Light bulb PIN Element
Door Bell PIN Element
Gateway PIN Element
Smartphone
NETNET 1 (Home NETNET)
User plane pipe (user data passes transparently)
NETNET 2 (Visited NETNET)
Notes: In this usecase we have a lost dog (section 5.1A of TR 22.859) , it has a smart dog collar (Guest PIN Element) whose home network is NETNET1. As the dog wanders the streets it can pass many NETNET networks composed of the following e.g. smart door bells, peoples smartphones, security cameras etc. If these NETNETs are configured to allow the smart dog collar (Guest PIN) to use them the dog collar “can roam” onto that NETNET. Application layer the dog collar reports its position so owner can find it.
It is similar to any of the following:
https://www.wired.com/story/how-amazon-sidewalk-works/
https://www.apple.com/airtag/
https://www.thetileapp.com/en-us/

## Slide 10
Example NETNET with PRAS
Legend
PRAS – Premises Radio Access System
CPN – Customer Premises Network (NETNET)
eRG – evolved Residential Gateway