## Slide 1: UE assistance operation
Google

## Slide 2: Should UE assistance operation be applied to additional steering modes?
We believe there is benefit in applying UE assistance operation with all steering modes
  Only the UE is aware of its internal state (battery level, temperature)
  Only the UE can determine the energy cost of each access (throughput, channel conditions)
    Energy consumption is a dynamic function of several factors
    User location with respect to the gNB/WLAN AP, Traffic volume, UE implementation
  For some traffic flows, the network does not really care which access is employed
When both accesses are available, the UE may choose a different access than the access determined by the steering mode
  Active-Standby: not use the Active access
  Smallest Delay: not use the access with the smallest RTT
  Priority-based: not route traffic to the high priority access even if it is not congested
Network controls UE assistance operation
  Can disable UE assistance operation by pushing new ATSSS rules

## Slide 3: Should the UE apply arbitrary split percentage or only steer all traffic to one access?
Applies to Load-Balancing steering mode only
At any point of time, only a fraction of UEs are likely to be engaged UE assisted operation
From a network perspective, does not matter how these UEs split their traffic
From a UE perspective, splitting is beneficial
  Using a single access may not meet the throughput requirements of an application
  Splitting traffic over two accesses may be more energy efficient than using a single access under QoS constraints

## Slide 4: How does the UPF identify the SDF in UE assisted operation?
We think the UE should provide an identity in the PMF message to the UPF which determines the corresponding ATSSS rule