## Slide 1: eNS_Ph2 Status Report after SA2#146E
Jinguo Zhu
ZTE

## Slide 2: eNS_Ph2 status after SA2#146e (1/4)
WI Code | Work Item Title | WP | Target Date | WID#
eNS_Ph2 | Enhancement of Network Slicing Phase 2 | 85% -> 97% | Jun, 21 | SP-200976
General
  The exception for all key issues are progressed well. 40 CRs are approved.
  The completion for KI#7 depends on RAN3 feedback
Exception tasks for KI#1 and KI#2. Status: Closed
  Finalise NSAC control due to the UE mobility between AMFs/SMFs, and UE mobility between EPC and 5GC
    Status: CRs are approved. This item can be closed. Further explanations/clarifications on small open issues via Cat F CRs.
  How to trigger the notification and how to identify the AMF in EAC procedure
    Status: CRs are approved. This item can be closed. No further work is expected
  Continue in next slide

## Slide 3: eNS_Ph2 status after SA2#146e (2/4)
WI Code | Work Item Title | WP | Target Date | WID#
eNS_Ph2 | Enhancement of Network Slicing Phase 2 | 85% -> 97% | Jun, 21 | SP-200976
(continue)Exception tasks for KI#1 and KI#2: Closed
  Finalize the support EPC interworking
    Status: CRs are approved, This item can be closed. Further explanations/clarifications on small open issues via Cat. F CRs.
  Finalize the support roaming scenarios
    Status: Interaction between V-NSACF and H-NSACF is not agreed. No further work is expected in this release. This item can be closed.
Exception task for KI#4. Status: Closed
  Finalise how to specify the event exposure for multiple NSACFs
    Status: CRs are approved. The Sub/Notify model for NSACF event exposure is open and is to be resolved via Cat. F CRs.

## Slide 4: eNS_Ph2 status after SA2#146e (3/4)
WI Code | Work Item Title | WP | Target Date | WID#
eNS_Ph2 | Enhancement of Network Slicing Phase 2 | 85% -> 97% | Jun, 21 | SP-200976
Exception sheet for KI#5. Status: Closed
  Accurate enforcement of the Total Maximum Data Rate per S-NSSAI when multiple PCFs per S-NSSAI are deployed is FFS
    Status: CRs are approved. This item can be closed
  Finalize the NWDAF based solution
    Status: CRs are approved. This item can be closed
Exception sheet for KI#7. Status: Closed
  Whether to provide additional information to NG-RAN depends on RAN2/RAN3 input
    Status: We have received RAN2/RAN3 feedback. The remaining Editor Note will be removed via Cat. F CR.

## Slide 5: eNS_Ph2 status after SA2#146e (4/4)
  RAN impacts and dependencies:
  None
Contentious Issue:
  None
Focus for the Next Meeting (SA2#147e):
  Maintenance and alignment via coordination with RAN2 and RAN3
  Maintenance on remaining open items via Cat.F CR
Risk:
  None.
WI Code | Work Item Title | WP | Target Date | WID#
eNS_Ph2 | Enhancement of Network Slicing Phase 2 | 85% -> 97% | Jun, 21 | SP-200976

## Slide 6: 2.4) Rel-17 Study/Work (7/16)
WI Code | Work Item Title | WP | Target Date | WID#
FS_eNS_Ph2 | Study on Enhancement of Network Slicing Phase 2 | 100% -> 100% | Mar, 21 | SP-190931
eNS_Ph2 | Enhancement of Network Slicing Phase 2 | 85% -> 97% | Jun, 2021 -> Sep, 2021 | SP-200976
Progress since SA#92-e:
  WI Exception tasks on KI #1, #2, #4, #5 and #7 are resolved. 40 CRs are approved.
  Further clarification/explanations are expected on PDN connection rejection because of NSAC, service continuity for EPC interworking, AMF removal and Sub/Notify model for NSACF event exposure, etc.
  Contentious Issue - None.
  RAN impacts and dependencies:
  None.
Next steps:
  Maintenance and alignment via coordination with RAN2 and RAN3.
  Finalize the remaining open items via Cat F CRs.