SA WG2 Meeting #146E e-meeting	S2-21xxxxx

Elbonia, 16 – 27 August, 2021	(revision of S2-21xxxxx)

Source:	CATT

Title:	TS 23.304: 5G DDNMF Services used by AF

Document for:	Approval

Agenda Item:	8.8

Work Item / Release:	5G_ProSe / Rel-17

Abstract: This contribution proposes to add some 5G DDNMF Services used by AF.

# 1.	Introduction

The “Direct Discovery Update Procedures” in clause 6.3.1.7 reuses the procedures defined in TS 23.303 clause 5.3.6A, and 5G DDNMF takes the role of the “ProSe Function”.

Specifically, in the “Revocation of Discovery Filters” procedure in TS 23.303 clause 5.3.6A.2.2, the ProSe Application Server sends an Authorization Update message to ProSe Function to revoke Discovery Filters in step 1, and ProSe Function sends an Authorization Update Result message to the ProSe Application Server to notify the revoke result.

Figure 5.3.6A.2.2-1: Revocation of Discovery Filters for restricted discovery (roaming or non-roaming)

Under 5G service based architecture, the Authorization Update and Authorization Update Result should be implemented as 5G DDNMF Services and used by AF.

It is proposed to add new 5G DDNMF Services used by AF in TS 23.304 clause 7.1.

# 2.	Proposal

It is proposed to capture the following changes into TS 23.304.

# * * * * First change * * * *

### 7.1.1	General

The following table illustrates the 5G DDNMF Services.

Table 7.1.1-1: Services provided by 5G DDNMF

| Service Name | Service Operations | Operation Semantics | Example Consumer(s) |
| --- | --- | --- | --- |
| N5g-ddnmf_Discovery | AnnounceAuthorize | Request/Response | 5G DDNMF |
|  | AnnounceUpdate | Request/Response | 5G DDNMF |
|  | MonitorAuthorize | Request/Response | 5G DDNMF |
|  | MonitorUpdate | Request/Response | 5G DDNMF |
|  | MonitorUpdateResult | Notify | 5G DDNMF |
|  | DiscoveryAuthorize | Request/Response | 5G DDNMF |
|  | MatchReport | Request/Response | 5G DDNMF |
|  | MatchInformation | Notify | 5G DDNMF |
|  | AuthorizeUpdate | Request/Response | AF |
|  | AuthorizeUpdateResult | Notify | AF |

# * * * * Second change * * * *

#### 7.1.2.1	General

Service description: This service enables a 5G DDNMF to manage inter-PLMN ProSe Direct Discovery operations, or enables AF to revoke the Restricted ProSe Direct Discovery permission.

# * * * * Third change * * * *

#### 7.1.2.X	N5g-ddnmf_Discovery_AuthorizeUpdate service operation

Service operation name: N5g-ddnmf_Discovery_AuthorizeUpdate

Description: The consumer NF revokes discovery permissions relating to some other users.

Input, Required: Discovery type = "restricted", RPAUID, Banned RPAUID, Banned PDUID.

Input, Optional: None.

Output, Required: Result.

Output, Optional: None.

#### 7.1.2.Y	N5g-ddnmf_Discovery_AuthorizeUpdateResult service operation

Service operation name: N5g-ddnmf_Discovery_AuthorizeUpdateResult

Description: The 5G DDNMF informs the NF consumer of the revocation results.

Input, Required: Discovery type = "restricted", RPAUID, Banned RPAUID, Banned PDUID, Result.

Input, Optional: None.

Output, Required: None.

Output, Optional: None.

# * * * * End of changes * * * *