SA WG2 Meeting #146E e-meeting	S2-21xxxxx

Elbonia, 16 – 27 August, 2021	(revision of S2-21xxxxx)

Source:	CATT

Title:	TS 23.304: Identifiers for UE-to-Network Relay discovery

Document for:	Approval

Agenda Item:	8.8

Work Item / Release:	5G_ProSe / Rel-17

Abstract: This contribution proposes clarifications on identifiers for UE-to-Network Relay discovery.

# 1.	Discussion

## 1.1	Identifiers for Layer-2 UE-to-Network Relay discovery

In RAN2#113bis-e, RAN2 discussed AS criteria for relay (re)selection and the following agreements were made and an LS (S2-2103771/ R2-2104649) was sent to SA2 at SA2#145e meeting:

Agreements:

Proposal 2-1: For L3 relay, the use of PLMN ID and cell ID is up to SA2

Proposal 2-2: For L2 relay, PLMN ID is supported as additional AS criteria for relay (re)selection.  Whether cell ID is used can be further discussed by RAN2.

Proposal 3-1: Besides serving cell ID, PLMN ID, L2/L3 relay support (if agreed in discovery session) and relay load, other additional AS criteria are not considered in this release.

Proposal 16: Include the information required for agreed additional AS criteria in discovery message.

These issues were further discussed at RAN2#114-e and the following agreements were made:

Agreements:

Relay load is not considered as a (re)selection criterion in Rel-17.

Proposal 4: For L2 U2N relay, cell ID can be used as additional AS criteria for relay (re)selection. RRC states under which the cell ID may be applied by L2 remote UE and how to use it by L2 remote UE are left to be addressed for L2 specific discussions. And the usage of cell ID by gNB for RRC CONNECTED L2 remote UE is handled by CP procedure and service continuity topic for L2 relay.

Proposal 6: It is up to SA2 to decide how to include L2/L3 relay support in discovery message.

Proposal 4[18/22][Easy]: Whether L2/L3 relay support can be used as additional criteria for relay (re-)selection can be left to SA2.

It can be seen from the above agreements that for Layer-2 UE-to-Network Relay, PLMN ID and cell ID are used as additional AS criteria for relay (re)selection and are require to be included in the discovery message.

The following EN captured in TS 23.304 clause 5.8.3.3 can be removed based on RAN2 agreement.

Editor's note:	It is FFS what identifiers are used in addition to the identifiers specified in clause 5.8.3.1 for Layer-2 UE-to-Network Relay use case.

Proposal 1: PLMN ID and cell ID are included in the Layer-2 UE-to-Network Relay discovery message and corresponding EN is removed.

There is also another EN unresolved in TS 23.304 clause 5.8.3.3:

Editor's note:	It is FFS with what information the RSC is associated for Layer-2 UE-to-Network Relay use case.

The Relay Service Code is defined to identify a connectivity service the 5G ProSe UE-to-Network Relay provides to a Remote UE and also to identify authorized users the 5G ProSe UE-to-Network Relay would offer service to:

-	Relay Service Code: parameter identifying a connectivity service the 5G ProSe UE-to-Network Relay provides to a Remote UE. The Relay Service Codes are configured in a 5G ProSe UE-to-Network Relay for advertisement. Additionally, the Relay Service Code may also identifies authorized users the 5G ProSe UE-to-Network Relay would offer service to, and may be used to select the related security policies or information e.g. necessary for authentication and authorization between the Remote UE and the 5G ProSe UE-to-Network Relay (e.g. a Relay Service Code for relays for police members only would be different than a Relay Service Code for relays for Fire Fighters only, even though potentially they provided connectivity to same DN e.g. to support Internet Access).

For Layer-2 UE-to-Network Relay case, the Layer-2 Remote UE may not be interested in the services Layer-2 UE-to-Network Relay provides but the RSC can still be used to authorize particular users, e.g. RSCs for police members and Fire Fighters may be different.

However the RSC should not be associated with PLMN ID or cell ID which are used by AS layer for relay (re)selection and RSC cannot be understood by AS layer.

Proposal 2: It is proposed to clarify that RSC is used for authorized users and not associated with PDU session parameters for Layer-2 UE-to-Network Relay, and remove the EN.

## 1.2	Identifiers for Layer-3 UE-to-Network Relay discovery

It is already specified in TS 23.304 clause 5.8.3.2 that Relay TAI is included the Layer-3 UE-to-Network Relay discovery message to assist N3IWF selection:

The following parameters may be used in addition to the parameters specified in 5.8.3.1, in 5G ProSe Layer-3 UE-to-Network Relay supporting N3IWF discovery procedure (for both Model A and Model B) to assist with N3IWF selection:

-	Relay TAI: indicates the Tracking Area Identity corresponding to the serving cell of the 5G ProSe Layer-3 UE-to-Network Relay.

According to the concluded sol#23 of TR 23.752, PLMN ID is also required to be included in the Layer-3 UE-to-Network Relay discovery message to assist N3IWF selection:

To assist the Remote UE with N3IWF selection, the Relay UE advertises the PLMN ID and 5GS TAI corresponding to the serving cell in the PC5 UE-to-Network discovery Announcement message (for Model A) or the UE-to-Network Relay discovery Response message (for Model B) or in the Relay Discovery Additional Information message.

Proposal 3: PLMN ID is included in the Layer-3 UE-to-Network Relay discovery message.

# 2.	Proposal

It is proposed to capture the following changes into TS 23.304.

# * * * * First change * * * *

#### 5.8.3.2	Identifiers for 5G ProSe Layer-3 UE-to-Network Relay

The following parameters may be used in addition to the parameters specified in 5.8.3.1, in 5G ProSe Layer-3 UE-to-Network Relay supporting N3IWF discovery procedure (for both Model A and Model B) to assist with N3IWF selection:

-	Relay TAI: indicates the Tracking Area Identity corresponding to the serving cell of the 5G ProSe Layer-3 UE-to-Network Relay.

-	Relay PLMN ID: indicates the PLMN ID corresponding to the serving cell of the 5G ProSe Layer-3 UE-to-Network Relay.

For 5G ProSe Layer-3 UE-to-Network relay, a Relay Service Code in the Announcement Message is associated with a set of PDU session parameters (e.g. PDU Session type, DNN, SSC Mode, S-NSSAI, Access Type Preference). The Relay Service Code may also represent if the relay UE can provide secure N3IWF connection.

For remote UE discovering 5G ProSe Layer-3 UE-to-Network relay, the Relay Service Code in the Solicitation Message represents the PDU session parameters that a PDU session of the relay should be able to support. The Relay Service Code may also represent if the remote UE requires secure N3IWF connection.

# * * * * Second change * * * *

#### 5.8.3.3	Identifiers for Layer-2 UE-to-Network Relay

The following parameters may be used in addition to the parameters specified in 5.8.3.1, for both Model A and Model B, to assist the Layer-2 UE-to-Network Relay (re)selection:

-	Relay PLMN ID: indicates the PLMN ID corresponding to the serving cell of the 5G ProSe Layer-2 UE-to-Network Relay.

-	Relay cell ID: indicates the serving cell of the 5G ProSe Layer-2 UE-to-Network Relay

For 5G ProSe Layer-2 UE-to-Network Relay, the Relay Service Code is used to identify authorized users the 5G ProSe UE-to-Network Relay would offer service to and is not associated with PDU Session parameters.

# * * * * End of changes * * * *