## Slide 1: 146-E MBS categorization and way forward proposal
LiMeng
2021.08

## Slide 2: Topics
  Category 1 (topics need to have further discussion)
    Topic #1: Shared tunnel management;
    Topic #2: NF services for SMF/AMF/MB-SMF;
    Topic #3: Session activation/Deactivation;
    Topic #4: Way forward of Pre-configuration;
    Topic #5: UDM enhancement to support SMF selection;
    Topic #6: UE authorization
    Topic #7: Handover issues
    Topic #8: User plane management
    Topic #9: PCC
    Topic #10: local MBS
  Category 2 (topic can have merged documents)
Click here to join the meeting

## Slide 3: Category #1

## Slide 4: Topic #1: Shared tunnel management
Tdoc # | source | AMF stores RAN id | MB-SMF stores RAN id
S2-2105632 | Ericsson | Yes. | 
S2-2106338 | vivo |  | Yes.
S2-2105919, S2-2105920 | CATT | Yes. | 
S2-2106367, S2-2106358, S2-2106351 | ZTE | Yes. | 
S2-2106466 | Nokia |  | Yes.
WF proposal
Shared tunnel management, MB-SMF stores AMF id, and determine the following: MB-SMF stores RAN id? AMF stores RAN id?
Companies’ views
Huawei: For multicast it is possible for the MB-SMF stores RAN id, since it is the RAN that triggers the establishment of shared tunnel
Ericsson: AMF stores NG-RAN ID to align with PDU Session handling that SMF is aware of only NG-RAN tunnel info.
CATT: It seems that the MB-SMF needs not to know the RAN IDs, and this aligns with the current PDU session management mechanism where the SMF has no idea of RAN ID.
Nokia: Ran ID in MB-SMF necessary for Topic 2 reuse of Namf_Communication_NonUeN2MessageTransfer service operation
AMF
MB-SMF
RAN
MB-UPF

## Slide 5: Topic #1: Shared tunnel management (merge proposal?)
- | Shared tunnel management | - | Merging proposal | Affected clauses
S2-2105632 | 23.247: Update [7.2.1.4] & [7.2.2.4] & [7.2.5.2] & [7.2.5.3] & [7.2.6] Store RAN ID List. | Ericsson | Address the ENs in 7.2.5.3 | 7.2.1.4, 7.2.2.4, remove EN: 7.2.5.2, 7.2.5.3, 7.2.6
S2-2106338 | 23.247: Modification on release of shared delivery. | vivo | Merge into S2-2106367 | 7.2.2.4
S2-2105919 | 23.247: Establishment of shared delivery toward RAN node. | CATT | Address the issue in 7.2.1.4 | 7.2.1.4
S2-2105920 | 23.247: Release of shared delivery toward RAN node. | CATT | Merge into S2-2106367 | 7.2.2.4
S2-2106367 | 23.247: Update the clause 7.2.2.4 on Release of shared delivery toward RAN node. | ZTE | Address the issue in 7.2.2.4 | 7.2.2.4
S2-2106358 | 23.247: Clarification on Establishment of shared delivery toward RAN node. | ZTE | Merge into S2-2105919 | 7.2.1.4
S2-2106466 | 23.247: Multicast message transfer between MB-SMF and NG-RAN. | Nokia, Nokia Shanghai-Bell | Address the ENs in 7.2.6 | 7.2.1.4, 7.2.2, 7.2.5, 7.2.6
S2-2105905 | 23.247: Update to Clause 7.2.2.4: Release of shared delivery toward RAN node. | LG Electronics, LG Uplus, KT Corp. | Separate document | 7.2.2.4
S2-2106083 | 23.247: Clarification of Session Join procedure. | Huawei, HiSilicon, Qualcomm | Take out the change related to this topic if any (e.g., 7.2.1.4). | 7.2.1, 9.1.4.1

## Slide 6: Topic #2: NF services for SMF/AMF/MB-SMF
Tdoc # | source | MB-SMF to SMF | SMF to AMF | MB-SMF to AMF
S2-2105916 | CATT | SMF (new for MBS) | AMF (new for MBS) | AMF (new for MBS)
S2-2106121 | Huawei | MB-SMF (Notify) | AMF (new for MBS) | AMF (new for MBS)
S2-2106334 | Vivo | SMF (new for MBS) | AMF (new for MBS) | AMF (new for MBS)
S2-2106454, S2-2106466 | Nokia | MB-SMF (Notify) | AMF (new for MBS) | Use existing Namf_Communication_NonUeN2MessageTransfer service operation
S2-2105638 | Ericsson | MB-SMF (Notify) | AMF (new for MBS) | MB-SMF (Notify)
in CC#2:
For Activation/Deactivation
  Step 2: MB-SMF notify SMF
  Step 3,4 use AMF service
  Step 11 FFS
Among MBS session activation, deactivation, update procedures, for the interactions between MB-SMF and SMF, they are using same service operations
Among MBS session activation, deactivation, update procedures, for the interactions between MB-SMF and AMF , they are using same service operations
Suggest to use Namf_MTGroup_EnableReachability
WF proposal | Companies’ views
Services for join/session establishment: SMF fetches information from MB-SMF: (MB-SMF service?) Establishes tunnel between MB-UPF and PSA (if needed): (MB-SMF service?) Establishes tunnel between MB-UPF and NG-RAN: (MB-SMF service?) Services for activation/deactivation: Interaction between MB-SMF and SMF: (MB-SMF service?) Interaction between SMF and AMF: (AMF service?) Interaction between MB-SMF and AMF: (AMF service/MB-SMF service?) Services for session update: Interaction between MB-SMF and SMF: (MB-SMF service?) Interaction between MB-SMF and AMF: (AMF service/MB-SMF service?) (Other services e.g., leave/release can use the “counter”-service) | Huawei: support the minutes of CC#2, interaction between MB-SMF and AMF better to use AMF service.
 | [Ericsson0817: Our view is that the same Nmbsmf service should be used for MB-SMF interaction with AMF or with SMF as the operation is applied to the MBS Session context. What does “counter-service” mean?]
 | CATT：Namf_MTGroup_EnableReachability is not appropriate for MBS session deactivation, as well as session update when the UEs are in CM-Connected mode. For MB-SMF to AMF, prefer to use Namf_MBS_N2MessageTransfer or similar.

## Slide 7: Topic #2: NF services for SMF/AMF/MB-SMF
MB-SMF
AMF
RAN
1. Nmbsmf_MBSSession_ContextStatusNotify Notify
2. NGAP request ()
3. NGAP response ()
4. Nmbsmf_MBSSession_ContextUpdate Request
5. Nmbsmf_MBSSession_ContextUpdate Response
MB-SMF
AMF
RAN
1. Namf_MBSSession_Update Request
2. NGAP request ()
3. NGAP response ()
4. Namf_MBSSession_Update Response
Per tunnel?
Per node?
MB-SMF
AMF
RAN
1. Namf_NonUEN2MessageTransfer
2. NGAP request ()
3. NGAP response ()
MB-SMF notify;
AMF nonUEN2 Message;
AMF N2 message for MBS;

## Slide 8: Topic #2: NF services for SMF/AMF/MB-SMF
Alt#1: TMGI management and MBS session management are different services.
Alt#2: TMGI management and MBS session management are the same service.
S2-2106445
S2-2105817

## Slide 9: Topic #2: NF services for SMF/AMF/MB-SMF (merge proposal?)
- | NF services | - | Merging proposal | Affected clauses
S2-2105638 | 23.247: Update [9.1] MB-SMF services and Resolving ENs. | Ericsson | Merged into S2-2106427 | 9.1
S2-2105641 | 23.247: Add in [9.3] new AMF service for broadcast communication. | Ericsson | Baseline for AMF service for broadcast | 9.x (AMF)
S2-2105642 | 23.247: Update [7.3] with the new AMF service for broadcast MBS Session. | Ericsson | See the merging proposal of broadcast. | 7.3.1-3
S2-2105817 | 23.247: Add in [9.x] new NEF service for MBS. | Ericsson | Merged into S2-2106445 | 9.x (NEF)
S2-2105819 | 23.501 CR3092 (Rel-17, 'B'): Add NF services for 5G MBS | Ericsson | Baseline for the changes on 501. | 23.501
S2-2105907 | 23.247: Clause 9.1.4: adding MBS service area to Nmbsmf_Information service. | LG Electronics | Merged into S2-2106427. | 9.1.4
S2-2106454 | 23.247: AMF multicast service notification service. | Nokia, Nokia Shanghai-Bell | Baseline for AMF MTGroup service | 9.X
S2-2106427 | 23.247: MB-SMF Service Operation names. | Nokia, Nokia Shanghai-Bell, Huawei | Based line for MB-SMF service for multicast. | 9.1
S2-2106445 | 23.247: NEF MBS services. | Nokia, Nokia Shanghai-Bell | Baseline for NEF services | 9.X
S2-2105922 | 23.247: MB-SMF Services. | CATT | Merged into S2-2106427 | 9.1
S2-2105923 | 23.247: MBSF Services. | CATT | Refer to SA4 spec | 9.X (MBSF)
S2-2105924 | 23.247: SMF Services. | CATT | Merged or noted? | 9.X (SMF)
S2-2105925 | 23.247: AMF services. | CATT | Baseline for AMF service invoked by MB-SMF | 9.X
S2-2106449 | 23.247: Nmbsmf_TMGI and Nmbsmf_MBSSession service updates. | Nokia, Nokia Shanghai-Bell | Merged into S2-2106427 | 9.1
S2-2106463 | 23.247: Updates to Nmbsmf_Information service. | Nokia, Nokia Shanghai-Bell | Merged into S2-2106427 | 9.1.4
S2-2106465 | 23.247: Updates to Nmbsmf_Reception service. | Nokia, Nokia Shanghai-Bell | Merged into S2-2106427 | 9.1
S2-2106077 | 23.247: Local MBS term clarification | Huawei, HiSilicon | Remove the changes related to this topic if any (e.g., 9.X); | 3.1, 6.2, 7.2.4.2, 7.2.6, 9.X

## Slide 10: Broadcast related
- | Session broadcast | -
S2-2105911 | 23.247: MBS Broadcast clarification. | CBN, Huawei, HiSilicon
S2-2105921 | 23.247: MBS procedures for broadcast session. | CATT
S2-2105898 | 23.247: Update [7.3] MBS procedures for Broadcast Session. | Samsung
S2-2106525 | 23.247: Updates to Delivery Status Indication for Broadcast. | Nokia, Nokia Shanghai-Bell
S2-2105642 | 23.247: Update [7.3] with the new AMF service for broadcast MBS Session. | Ericsson
WF proposal (old)
Take S2-2106525 as the baseline for 7.3.5; Take S2-2105911 as the baseline for 7.3.1; Take S2-2105921 as the baseline for 7.3.2; Take S2-2105642 as the baseline for 7.3.3; Take S2-2105898 as the baseline for 7.3.4; For the documents above, remove the changes on other section(s).
WF proposal (alternative)
Take S2-2106525 as the baseline for 7.3.5; Take S2-2105911 as the baseline for 7.3.1-7.3.4; For the documents above, remove the changes on other section(s).

## Slide 11: Topic #3: Session activation/deactivation
Tdoc # | source | Proposals
S2-2105637, S2-2105650, S2-2105633 | Ericsson | Clarify that MB-SMF->AMF and MB-SMF->SMF for activation/deactivation/update can be executed in parallel. SMF can provide UE ID list and PDU Session ID list to AMF, to let AMF find SMF in later steps. For NW-triggered release, MB-SMF can deactivation session in advance to save resource waste.
S2-2105893 | Samsung | Let SMF address the individual paging issue.
S2-2105916 | CATT, CBN | NG-RAN keeps context when MBS session is inactive; Clarify that MB-SMF->AMF and MB-SMF->SMF for activation/deactivation can be executed in parallel. Specify the paging issue. Shared tunnel issue (could be resolved in another doc).
S2-2106121 | Huawei | Address the N2 info provisioning issue during activation; Handling context at UE/RAN/UPF; Handling the interaction for N4mb, and between PSA and MB-UPF;
S2-2106360 | ZTE | Clarification and resolve the editor’s note, and tunnel between MB-UPF and PSA will not be released
S2-2106334 | vivo | Handling the interaction for N4mb; MB-SMF provides QoS to SMF during activation.
Companies’ views
Huawei: no need to provide N1 message to UE in deactivation, AMF figures out the paging area, and SMF provide N2 info as analyzed in S2-2106121.
Ericsson0817: We understand there are different topics and could be grouped accordingly. #1 At MBS session activation, how to handle the paging; #2 at MBS Session deactivation, how to handle associated QoS Flows #3 At MBS Session release, whether NG-RAN resource should be released as soon as possible? #4 Activation/Deactivation from MB-SMF -> AMF, and from MB-SMF -> SMF are executed in parallel
CATT: During MBS session deactivation: RAN only marks the MBS Session context as inactive. Using existing PDU Session modification procedure to remove mapped unicast QoS flows. Release the tunnel between MB-UPF and PSA for individual delivery. During MBS session activation: For RAN nodes with shared delivery established, only activation notification is needed; for RAN node without shared/individual delivery established, using shared/individual delivery establishment procedure.
WF proposal
RAN context: RAN mark the context as inactive? Interaction with UE: no N1 message for deactivation? MB-UPF and PSA for individual during deactivation: kept or released? Paging for activation: let AMF figure out paging for individual issue? MB-SMF  SMF during Activation: will QoS info be included besides TMGI or not? N2 info issues: will SMF provide N2 info to RAN? #1 At MBS session activation, how to handle the paging; #2 at MBS Session deactivation, how to handle associated QoS Flows #3 At MBS Session release, whether NG-RAN resource should be released as soon as possible? #4 Activation/Deactivation from MB-SMF -> AMF, and from MB-SMF -> SMF are executed in parallel

## Slide 12: Topic #3: Session activation/deactivation (merge proposal?)
- | Session Activation/Deactivation | - | Merging proposal | Affected clauses
S2-2105637 | 23.247: Update [7.2.5][7.2.6] Parallel Activation/Deactivation/Update. | Ericsson | Separated document | 7.2.5.2, 7.2.5.3, 7.2.6
S2-2105650 | 23.247: Update [7.2.5.1] MBS Session Activation . | Ericsson |  | 7.2.5.2
S2-2105633 | 23.247: Update [7.2.2.3] Deactivation before SMF removing joined UEs. | Ericsson | Separated document | 7.2.2.3
S2-2105893 | 23.247: Update [7.2.5] MBS session activation and deactivation. | Samsung |  | 7.2.5
S2-2105916 | 23.247: Clarification on MBS Session activation and deactivation. | CATT, CBN |  | 7.2.5.2, 7.2.5.3
S2-2106121 | 23.247: Further clarification for MBS session activation and deactivation. | Huawei, HiSilicon |  | 4.3, 7.2.3.X, 7.2.5
S2-2106360 | 23.247: Resolving the ENs in the MBS session activation and deactivation procedure. | ZTE |  | 7.2.5.2, 7.2.5.3
S2-2106334 | 23.247: Modification on activation and deactivation. | vivo |  | 7.2.5.2, 7.2.5.3
One baseline for activation, and one for deactivation?

## Slide 13: Topic #4: Way forward of Pre-configuration
Tdoc # | source | SMF reject join if not configured | SMF can find MB-SMF even if there is no configuration
S2-2105915 | CATT | Yes. | 
S2-2106359 | ZTE | Yes (no MB-SMF is found)? | 
S2-2105890 | Samsung | Yes. | 
S2-2105636 | Ericsson | Yes (remove the preconfigured – established state transition). | 
S2-2106507 | Nokia |  | Yes: Addressing the QoS information issue (pre-configured at UDR).
S2-2106089 | Huawei |  | Yes: Resolving the racing condition that SMF facing no MB-SMF info: rejecting or, continue process as pre-configured condition?
Companies’ views
Huawei: Need to resolve the racing condition mentioned in the table. While for NRF it is needed to differentiated the case for MB-SMF discovery in configuration procedure, and in Session join procedure.
Ericsson0817: unclear how it works. For simplicity, recommend SMF reject join if not configured in Rel-17
CATT: For simplicity, prefer to not involving MBS configuration upon MBS join procedure in R17, and leave it to R18.
WF proposal
Clarify the following issues ([Section 7.2.1.2, 7.2.1.3, 7.1.2]) Session configuration: Is this procedure mandatory, or can be done by e.g., pre-configuration? SMF rejecting UE: No MB-SMF found? SMF finding MB-SMF: by pre-configured MB-SMF at NRF or must by configuration procedure?
Issue to be checked:
How to resolve MB-SMF selection issue?
  Is there any MB-SMF instance stored in NRF when pre-configuration is supported and no configuration procedure executed?
(Note that the pre-configuration at UDR is mentioned somewhere in section 7.1.1.2)

## Slide 14: Topic #4: Way forward of Pre-configuration (merge proposal?)
 | Pre-configuration |  | Merging proposal | Affected clauses
S2-2105915 | 23.247: MBS Session join and Session establishment. | CATT, CBN | For pre-configuration, Depends on discussion of Topic #4 | 7.2.1
S2-2106359 | 23.247: Modification on the Multicast session join and session establishment procedure. | ZTE | For pre-configuration, Depends on discussion of Topic #4 | 7.2.1.3
S2-2105890 | 23.247: Update [7.2.1] MBS Join and Session establishment procedure. | Samsung | For pre-configuration, Depends on discussion of Topic #4 | 7.2.1
S2-2105636 | 23.247: Update [4.3] Multicast session state model. | Ericsson | Irrelevant? For session state model, see page 31 | 4.3
S2-2106507 | 23.247: Updates to Multicast session join and session establishment procedure. | Nokia, Nokia Shanghai-Bell | For pre-configuration, Depends on discussion of Topic #4 For session state model, see page 31 | 4.3, 7.2.1.3, 9.1.1
S2-2106089 | 23.247: Updates to address the Editor's Note about how SMF requests MB-SMF to configure the multicast session. | Huawei, HiSilicon | Use S2-2106089 as the one for further discussion. | 7.1.2, 7.2.1.3

## Slide 15: Topic #5: UDM enhancement to support SMF selection
Tdoc # | source | SMF selection when establishing PDU session should not consider MBS | SMF selection when establishing PDU session should consider MBS
S2-2105915 | CATT | Yes. | 
S2-2106355 | ZTE | Yes. | 
S2-2105890 | Samsung | Yes. | 
S2-2106473 | Nokia |  | Yes.
Companies’ views
Ericsson0817: DNN/S-NSSAI would be sufficient, no separate capability is needed.
CATT: It seems using S-NSSAI and DNN can fulfill the current requirements.
WF proposal
Clarify in session join/establishment procedure [Section 7.2.1.2]: SMF selection when establishing PDU session should not consider MBS, or SMF selection when establishing PDU session should consider MBS? Resolve the associating ENs based on the agreement above.
Issue to be checked:
SMF selection when establishing PDU session should consider MBS:
  The benefits of having specific information in UDM for SMF selection is acceptable, i.e., not limit the MBS service for a specific DNN+S-NSSAI.
  The relationship between subscription for selecting SMF, and the subscription of whether UE is authorized to use MBS is clarified.
SMF selection when establishing PDU session without considering MBS:
  Whether it is possible that having MBS-capable SMF for “whole PLMN”.
  Or AMF can selecting SMF based on DNN+S-NSSAI.

## Slide 16: Topic #5: UDM enhancement to support SMF selection (merge proposal?)
 | SMF selection |  | Merging proposal | Affected clauses
S2-2105915 | 23.247: MBS Session join and Session establishment. | CATT, CBN |  | 7.2.1
S2-2106355 | 23.247: Clarification on the SMF selection. | ZTE | Use this one as the baseline for further discussion | 6.4, 7.2.1.2, 7.1.X
S2-2105890 | 23.247: Update [7.2.1] MBS Join and Session establishment procedure. | Samsung |  | 7.2.1

## Slide 17: Topic #6: UE authorization
Tdoc # | source | Alt #1: UE’s MBS authorization (incl. feature level and TMGI level) is stored in UDM when establishing PDU session | Alt #2: UE’s MBS authorization (incl. feature level only) is stored in UDM when establishing PDU session, while the TMGI level is stored at PCF and SMF interacts with PCF during join
S2-2106082 | Huawei | Yes. | 
S2-2105917 | CATT | Yes. | 
S2-2106473 | Nokia |  | Yes.
Companies’ views
Huawei: UE authorization includes 1) whether UE is authorized to use MBS, and 2) which TMGI(s) that the UE can use; and the transforming of per-session level info and per-UE level info is based on implementation.
[Ericsson0817: configuration in UDM/UDR if needed for group affiliation can be done by the AF as a separate procedure, e.g. after the MBS Session is created, following existing procedure as specified in clause 4.15.6.2 of 23.502 (NEF -> UDM -> UDR).
CATT: Similar view as Huawei’s. In addition, per-session level info is stored in the UDR during MBS Session configuration procedure, and per-UE level info is stored in the UDM after queried from the UDR.
WF proposal
Clarify [section 6.4]: What kind of information will be stored at UDM? i.e., 1) UE is authorized to use MBS, or also include 2) the TMGI list of the UE authorized for the MBS? Add a new clause to include the detailed subscription info.
Issue to be checked:
How to provide the UE list information to the 5GC?
  In configuration procedure (see S2-2105918 from CATT)?
For the case that the MBS service is open to all UE, how to deal?
Whether to treat local MBS separately or not (see S2-2105917)?
For Alt #1 :
  Whether it is possible to translate “per-TMGI info (i.e., UE list for the TMGI)” to “per-UE info (i.e., TMGI for a certain UE)”.
For Alt #2 :
  Whether PCF deployment is always required.
Ericsson0817: need some rewording?
Provisioning UE list: using external parameter provisioning procedure, or during configuration/creation?
SMF fetching UE authorizing info: during PDU session establishment, or during UE join request?
UE ID as the key, or MBS session ID as the key

## Slide 18: Topic #6: UE authorization (merge proposal?)
 | SMF selection |  | Merging proposal | Affected clauses
S2-2106082 | 23.247: Clarification on MBS UE authorization. | Huawei |  | 6.1, 6.4
S2-2105917 | 23.247: MBS information storage in UDM and UDR. | CATT |  | 6.4
S2-2106473 | 23.247: 5MBS Information in UDM. | Nokia |  | 6.4, 7.2.1.2

## Slide 19: Topic #7: Handover issue
Tdoc # | source | Proposals
S2-2106354, S2-2106356 (clarification) S2-2105432 | ZTE Ericsson | RAN provides its capability to AMF via NGAP procedures. SMF subscribes RAN node capability, and AMF provides such capability. NG-RAN MBS support level is removed from NGAP/aligned with NGAP stage 3 principles. AMF is aware of the support by existing implicit means or configuration.
S2-2105433, | Ericsson | AMF is aware of RAN capability via pre-configuration. Target NG-RAN deduces MBS Session is used via a specific pre-configured QFI value.
S2-2105888 | Samsung | 5GC Individual MBS traffic delivery might be used in case of priority user handling.
S2-2106123, S2-2106124 | Huawei | SMF sends uncast/MBS info to RAN, based on the received N2 SM information, the SMF determines the MBS data delivery method (i.e., accepted M-QFI be included or not). Lossless issue: a common 5GC-SN number is used for data forwarding.
Companies’ views
Huawei: lossless is to be guaranteed by 5GC side SN number. SMF determines RAN capability by checking the RAN response after sending MBS info to RAN.
Issue to be checked:
For the HO case from non-supporting to supporting:
  Choose one WF among the 3 alternatives.
For the lossless issue:
  Refer to RAN2/RAN3 agreement/progress.
WF proposal
Clarify [section 6.3]: Resolving the ENs. Clarify [section 7.2.3]: For the HO case from non-supporting to supporting: -- the SMF determines the delivery method: using indication from NG-RAN based on specific QFI, or accepted M-QFI, or based on subscription-notification from AMF or based on RAN3 WA to include an explicit indication? For the lossless issue: --- forwarding the data is addressed in SA2 in this meeting? Clarify [section 7.2.3.4: AMF NG-RAN support level configured/implicit known following NGAP principles? Clarify [section 7.2.1.3] Other possible update.

## Slide 20: Topic #7: Handover issue (merge proposal?)
- | Intra system mobility and Handover related | - | Merging proposal | Affected clauses
S2-2106354 | 23.247: Discussion and proposal on the SMF awareness of target NG-RAN MBS capability in Xn HO. | ZTE |  | 5.3.2.3, 5.3.2.6, 6.3.1, 7.2.3.4
S2-2105433 | 23.247: Update [7.2.3.4] Handover from non-supporting NG-RAN. | Ericsson |  | 7.2.3.4
S2-2105888 | 23.247: Update [6.3] Mobility support of MBS service. | Samsung |  | 6.3
S2-2106123 | 23.247: Resolve the EN for mobility support of MBS. | Huawei, HiSilicon | Deal with capability issue only. | 6.3.1, 7.2.3.2, 7.2.3.3, 7.2.3.4
S2-2106124 | 23.247: Minimization of data loss. | Huawei, HiSilicon |  | 7.2.3.5(X)
S2-2106356 | 23.247: Modification on the mobility clause 6.3.1 and 7.2.3 to resolve the EN and avoid the duplication. | ZTE | Deal with the other issues. | 6.3.1, 7.2.3.2, 7.2.3.3
Note: S2-2105432 is related to the RAN capability awareness issue.

## Slide 21: Topic #8: User Plane management
Tdoc # | source | Alt #1: One-to-many-based | Alt #2: two-step-based
S2-2105648, S2-2105649 | Ericsson | Yes. | 
S2-2106361, S2-2106362 | ZTE | Yes. | 
S2-2106469 | Nokia |  | Yes.
Companies’ views
Issue to be checked:
The benefit of having a two-step-based solution.
WF proposal
Clarify [section 6.7]: Resolving the ENs. Choose one of Alt#1 and Alt#2 as the final conclusion.
8.9 | S2-2106470 | CR | Approval | 23.501 CR3226 (Rel-17, 'F'): UPF configuration for traffic replication for MBS | Nokia, Nokia Shanghai-Bell
Ericsson0817: moved here

## Slide 22: Topic #8: User Plane management (merge proposal?)
- | User Plane management | - | Merging proposal | Affected clauses
S2-2105648 | 23.247: Update [6.7] MBS UP Management: packet detection and forwarding . | Ericsson | On-step and remove the EN. . | 6.7
S2-2105649 | 23.501 CR3055 (Rel-17, 'C'): MBS Packet detection and forwarding | Ericsson |  | 23.501
S2-2106361 | 23.247: Discussion and proposal on the UPF packet detection and forwarding for MBS data traffic. | ZTE | Merged into 5648/6469? | 6.7
S2-2106362 | 23.501 CR3202 (Rel-17, 'C'): Clarification on the packet detection and forwarding for MBS traffic | ZTE | Open to align CT4 conclusion to remove EN. | 23.501
S2-2106469 | 23.247: UPF configuration to replicate packets. | Nokia, Nokia Shanghai-Bell | Two-steps and remove the EN. | 6.7
 | 501 | nokia | Open. | 
Ericsson0817:
Ericsson 5648, ZTE 6361 can be merged
Ericsson 5649, ZTE 6362 can be merged
Proposal:
For MB-SMF and MB-UPF part, follow the solution of S2-2105648 (i.e., using multiple destinations with one FAR);
For SMF and UPF part, leave the work to CT4, and wait for CT4’s conclusion.

## Slide 23
PDR
FAR(internal)
PDR
PDR
PDR
FAR
FAR
FAR
RAN
RAN
PSA
MB-UPF
PDR
FAR
Dest. addr
RAN
RAN
PSA
MB-UPF
Carry on indication
PDR
FAR
Dest. addr
Dest. addr
PDR
FAR

## Slide 24: Topic #9: Initial configuration and PCC
Tdoc # | source | Proposals
S2-2105653 | Ericsson | Combine configuration with/without PCC together (two alternatives with subtle differences); MB-SMF provide service requirement to MB-PCF;
S2-2106076, S2-2106090 | Huawei | Separate configuration with/without PCC, for PCC, only document the delta part compared with w/o PCC. For initial configuration with dynamic PCC, update Policy later. (6090): Specify the case when MB-SMF let MB-UPF join N6 multicast.
S2-2106443, S2-2106453, S2-2106441 | Nokia | (6443) for initial configuration, if PCC used, MB-SMF will be provided by an indicator to tell whether there will be an upcoming update due to PCC is used. (6453) adopt updated services to the configuration procedures (6453) Separate configuration with/without PCC, for PCC, only document the delta part compared with w/o PCC. (6453) clarify update/activation call-flow; (6441) specify the policy info stored in UDR. (not related to others?)
S2-2106353, S2-2106352 | ZTE | Update configuration removal/update: for removal, MB-SMF terminates the policy association; Combine configuration with/without PCC together.
S2-2106198 | Tencent | Resolve the ENs.
S2-2105956 | Panasonic | NRF tells whether PCF is needed.
S2-2105918 | CATT | Clarify the UE list provisioning in configuration.
Companies’ views
Huawei: Support to document the delta part when PCC is used. Fine to optimize “PCC” + “initial configuration”+ “broadcast” procedure.
Ericsson0817: Suggest to have MBS session creation as one step (i.e. no split).
CATT: Support to keep current name “configuration”. Configuration procedure includes the MBS authorization information provision (as already defined in step 7) as well as MBS authorization information storage. Fine with document the delta part when PCC is used.
WF proposal
Clarify [section 7.1]: Keep the current name “configuration”? Keep the clauses with/without PCC separate? Clarify [section 7.1.1]: Configuration procedure include UE list provisioning? PCF updating the QoS for initial configuration? Clarify [section 7.1.2]: For removal, MB-SMF terminates association with PCF

## Slide 25: Topic #9: Initial configuration and PCC (merge proposal?)
- | MBS Session configuration and PCC | -
S2-2105653 | 23.247: Policy Control for MBS Session . | Ericsson
S2-2106076 | 23.247: Combine MBS session parameter provisioning. | Huawei, HiSilicon
S2-2106443 | 23.247: Initial MBS session configuration with PCC for broadcast. | Nokia, Nokia Shanghai-Bell
S2-2106353 | 23.247: Update the clause 7.1.1 Configuration for MBS Session. | ZTE
S2-2106352 | 23.247: Resolving the ENs in the clause 7.1.1.2 Initial MBS session configuration with PCC. | ZTE
S2-2106198 | 23.247: Update the Initial MBS session configuration procedure with PCC. | Tencent
S2-2106453 | 23.247: Updates to configuration procedures . | Nokia, Nokia Shanghai-Bell
S2-2106089 | 23.247: Updates to address the Editor's Note about how SMF requests MB-SMF to configure the multicast session. | Huawei, HiSilicon
S2-2105956 | 23.247: Update [7.1] MBS PCC configuration. | Panasonic Corporation, DENSO CORPORATION
S2-2105918 | 23.247: MBS authorization information provision during Session Configuration. | CATT
S2-2106441 | 23.247: 5MBS Information in UDR. | Nokia, Nokia Shanghai-Bell

## Slide 26: Topic #10: local MBS
Tdoc # | source | Proposals
S2-2105909, S2-2105906 | LGE | (5909) correction on Session Context for local MBS (separate?) (5906) correction the description of 7.2.4.3.
S2-2105627 | KPN | MBS service area could be a geographical one.
S2-2106357 | ZTE | SMF provides all MBS service areas to NG-RAN. Clarify the N2 HO for local MBS with location dependent service.
S2-2106420, S2-2106450 | Nokia | (6420): SMF subscribes UE location in case of individual delivery. (6420): specify the call-flow of the usage of Individual delivery for a local or location dependent multicast service. (6450): update of MBS service area for multicast, including the notification toward SMF and AMF from MB-SMF, by defining a new procedure.
S2-2106077, S2-2106122 | Huawei | (6077): update of MBS service area for multicast, including the notification toward SMF and AMF from MB-SMF, by modifying current procedure; (6122): SMF subscribes UE location in case of individual delivery (6122): specifies the procedure to stop sending local MBS data in case of UE moves out of Local MBS service area.
S2-2106335, S2-2106336 | vivo | (6335) Local MBS is only for supporting RAN node. (6336) MBS service area can be pre-configured to the UE.
S2-2105759, S2-2105760 | Tencent | (5759) clarify the session activation/deactivation for local MBS; (5760) clarify the session update for local MBS.
S2-2105892 | Samsung | SMF subscribes UE location in case of individual delivery (Limeng: but in TS it is to-be-specified?);
Companies’ views
Huawei: support for SMF subscribing UE location in case of local MBS service is considered and when individual delivery is used. NG-RAN should release the tunnel if it does not belong to MBS service area any more.
Ericsson0817: existing “area of interest” could be reused by SMF to determine UE’s in/out of MBS service area Q: when UE moves out, is UE join state kept?
CATT: Agree with Huawei. In addition, support to use MBS session update procedure to update MBS service area.
WF proposal
Clarify [section 6.2]: Local MBS is for supporting and non-supporting? MBS service area could be a geographical one. Clarify [section 7.2.4]: SMF subscribes UE location in case of individual delivery For local MBS update: SMF stops sending MBS data? RAN triggers shared tunnel release procedure?

## Slide 27: Topic #10: local MBS (merge proposal?)
- | Local MBS | -
S2-2105909 | 23.247: Update to Clause 6.9.1 about MBS Service Area. | LG Electronics
S2-2105627 | 23.247: Local MBS Service with support for Group Message Delivery. | KPN
S2-2106357 | 23.247: Resolving the ENs on Localised service [7.2.4]. | ZTE
S2-2106420 | 23.247: Individual Delivery for location-Based Multicast services. | Nokia, Nokia Shanghai-Bell
S2-2106077 | 23.247: Local MBS term clarification. | Huawei, HiSilicon
S2-2106335 | 23.247: Modification on handover procedure for local MBS Session | vivo
S2-2105759 | 23.247: MBS Session activation and deactivation for local MBS. | Tencent
S2-2105760 | 23.247: MBS Session Update for local MBS. | Tencent
S2-2105892 | 23.247: Update [7.2.4.3] Handover procedure with limited area MBS session. | Samsung
S2-2105906 | 23.247: Editorial update to Clause 7.2.4.3. | LG Electronics
S2-2106122 | 23.247: Support of multicast service available within a limited area. | Huawei, HiSilicon
S2-2106336 | 23.247: Modification on local MBS service with limited area. | vivo
S2-2106450 | 23.247: Changing service area of multicast session. | Nokia, Nokia Shanghai-Bell

## Slide 28: Topic #11: How to handle associated QoS flows for individual fallback in policy control
- |  |  | Local MBS | -
S2-2106433 | DISCUSSION |  | How to handle associated QoS flows for individual fallback in policy control | Nokia, Nokia Shanghai-Bell
S2-2106437 | CR | 23.503 | 23.503 CR0579R1 (Rel-17, 'B'): PCC impacts of 5MBS Revision of (Postponed) S2-2104017 from S2-145E | Nokia, Nokia Shanghai Bell
S2-2106435 | P-CR | 7.2.1.3 | 23.247: Corrections to Clause 7.2.1.3 to address PCF interactions. | Nokia, Nokia Shanghai-Bell

## Slide 29: Topic #12: Fallback to EPS MBMS for public safety
- |  |  | Local MBS | -
S2-2106119 | P-CR | 6.8 | 23.247: Clarification on 5MBS interworking with eMBMS at transport layer. | Huawei, HiSilicon,
S2-2106120 | P-CR | 6.8 | 23.247: 5MBS interworking with eMBMS for same MBS service at both side. | Huawei, HiSilicon
S2-2106363 | P-CR | 5.2 | 23.247: Adding 5G MBS and EPS eMBMS interworking architecture and modify the functionality description. | ZTE
S2-2106118 | P-CR | 5.2, 7.2.2.X, 7.4 | 23.247: MBS procedures for inter System Mobility. Revision of (Noted) S2-2104393 from S2-145E | Huawei, HiSilicon, LG Electronics
S2-2106487 | P-CR | 5.2, 6.8, 7.4 | 23.247: 5MBS interworking with eMBMS. Revision of (Noted) S2-2104664 from S2-145E | Qualcomm Incorporated, Ericsson, LG Electronics, AT&T, FirstNet, Norwegian Communications Authority, Softil, Ministère de l'Intérieur Français, UK Home Office, Erillisverkot
S2-2106488 | P-CR | 6.8 | 23.247: 5MBS interworking with eMBMS at transport layer. Revision of (Noted) S2-2104665 from S2-145E | Qualcomm Incorporated, Ericsson, AT&T, FirstNet, Norwegian Communications Authority, Softil, Ministère de l'Intérieur Français, UK Home Office, Erillisverkot
S2-2106364 | P-CR | 6.8 | 23.247: Adding clause 7.4.2, MBMS interworking when the same service is not provided via eMBMS and 5MBS. | ZTE

## Slide 30: Category #2

## Slide 31: Other documents (Inter system mobility)
- | Inter system mobility | -
S2-2106118 | 23.247: MBS procedures for inter System Mobility. | Huawei, HiSilicon, LG Electronics
S2-2106119 | 23.247: Clarification on 5MBS interworking with eMBMS at transport layer. | Huawei, HiSilicon,
S2-2106120 | 23.247: 5MBS interworking with eMBMS for same MBS service at both side. | Huawei, HiSilicon
S2-2106487 | 23.247: 5MBS interworking with eMBMS. | Qualcomm Incorporated, Ericsson, LG Electronics, AT&T, FirstNet, Norwegian Communications Authority, Softil, Ministère de l'Intérieur Français, UK Home Office, Erillisverkot
S2-2106488 | 23.247: 5MBS interworking with eMBMS at transport layer. | Qualcomm Incorporated, Ericsson, AT&T, FirstNet, Norwegian Communications Authority, Softil, Ministère de l'Intérieur Français, UK Home Office, Erillisverkot
S2-2106363 | 23.247: Adding 5G MBS and EPS eMBMS interworking architecture and modify the functionality description. | ZTE
S2-2106364 | 23.247: Adding clause 7.4.2, MBMS interworking when the same service is not provided via eMBMS and 5MBS. | ZTE

## Slide 32: Protocol stack
- | Protocol Stack | -
S2-2105634 | 23.247: Update [8.1] Control Plane Protocol Stack. | Ericsson
S2-2105635 | 23.247: Update [8.2] User Plane Protocol Stack. | Ericsson
S2-2105757 | 23.247: Update the User Plane Protocol Stack for MBS session. | Tencent
S2-2105899 | 23.247: Update [8] Control and user plane stacks. | Samsung
S2-2106350 | 23.247: Modification on clause 8, Protocol stack description. | ZTE
S2-2106079 | 23.247: Miscellaneous clarification. | Huawei, Qualcomm
WF proposal
For Control Plane Protocol Stack update: Take S2-2105634 as the baseline contribution. For User Plane Protocol Stack update: Take S2-2106350 as the baseline contribution.

## Slide 33: Service levels
- | Service levels | -
S2-2105645 | 23.247: Update [4.1] on service levels for the multicast communication service . | Ericsson
S2-2105885 | 23.247: Update [4.1] Principles of multicast and broadcast communication. | Samsung
S2-2106079 | 23.247: Miscellaneous clarification. | Huawei
WF proposal
Take S2-2105885 as the baseline contribution.

## Slide 34: Service provisioning
- | Service provisioning | -
S2-2105646 | 23.247: Correct [4.2.2] Broadcast data provisioning . | Ericsson
S2-2105886 | 23.247: Update [4.2] MB service provisioning. | Samsung
S2-2106080 | 23.247: Clarification on MB service provisioning. | Huawei
WF proposal
Take S2-2105646 as the baseline contribution for broadcast. Take S2-2105886 as the baseline contribution for Multicast.

## Slide 35: NF functionalities
- | NF functionalities | -
S2-2105887 | 23.247: Update [5.1] general architecture and [5.3] Reference points. | Samsung
S2-2105432 | 23.247: Update [5.3.2] Functional Entities. | Ericsson
S2-2106079 | 23.247: Miscellaneous clarification. | Huawei, Qualcomm
WF proposal
Take S2-2106079 as the baseline contribution.
Ericsson0817:
5628 handled separately ?
5647 handled separately?
S2-2105647 | 23.247: Update [5.3.2] NRF. | Ericsson
S2-2105628 | 23.247: Update [5.3.2] & [7.1.1] & [7.3] & [7.X] Clarification of MBSF and NEF. | Ericsson

## Slide 36: Session state model
- | Session state model | -
S2-2105636 | 23.247: Update [4.3] Multicast session state model. | Ericsson
S2-2106081 | 23.247: Multicast session state model. | Huawei
S2-2106507 | 23.247: Updates to Multicast session join and session establishment procedure. | Nokia, Nokia Shanghai-Bell
WF proposal
Take ? as the baseline contribution.

## Slide 37: Session ID
- | Session ID | -
S2-2105629 | 23.247: Update [6.5.1] MBS Session ID. | Ericsson
S2-2105889 | 23.247: Update [6.5.2] Temporary Mobile Group Identity. | Samsung
S2-2106079 | 23.247: Miscellaneous clarification. | Huawei, Qualcomm
WF proposal
Take S2-2106079 as the baseline contribution.
Ericsson0817: 6079 has many more aspects than MBS Session ID, does it mean that the other aspects in 6079 will be removed?
In slide “NF functionalities”, 6079 is also used as baseline?

## Slide 38: Service Announcement
- | Session state model | -
S2-2105630 | 23.247: Update [6.11] NID in Service Announcement. | Ericsson
S2-2106365 | 23.247: Update the clause 6.11 service announcement. | ZTE
S2-2106079 | 23.247: Miscellaneous clarification. | Huawei, Qualcomm
WF proposal
Take S2-2106365 as the baseline contribution.

## Slide 39: Session Context
- | Session Context | -
S2-2106197 | 23.247: MBS Session and Service Context. | Tencent
S2-2106079 | 23.247: Miscellaneous clarification. | Huawei, Qualcomm
S2-2106351 | 23.247: Update the clause 6.9.1 MBS Session/Service Context. | ZTE
WF proposal
Take S2-2106351 as the baseline contribution.

## Slide 40: Session join and establishment
- | Session join and establishment | - | 
S2-2105890 | 23.247: Update [7.2.1] MBS Join and Session establishment procedure. | Samsung | 
S2-2105915 | 23.247: MBS Session join and Session establishment. | CATT, CBN | 
S2-2106507 | 23.247: Updates to Multicast session join and session establishment procedure. | Nokia, Nokia Shanghai-Bell | 7.2.1.3
S2-2106083 | 23.247: Clarification of Session Join procedure. | Huawei, HiSilicon, Qualcomm | 
S2-2106359 | 23.247: Modification on the Multicast session join and session establishment procedure. | ZTE | Merged into 6507.
S2-2105631 | 23.247: Update [7.2.1.3] & [7.2.2.2] interactions between SMF and UPF for individual delivery. | Ericsson | 
S2-2106333 | 23.247: Make shared tunnel establishment common. | vivo | 
WF proposal
Take ? as the baseline contribution.

## Slide 41: Session leave and release
- | Session join and establishment | -
S2-2105891 | 23.247: Update [7.2.2] MBS Session leave and Session release procedure. | Samsung
S2-2105651 | 23.247: Update [7.2.2] UE leave MBS Session and MBS Session release. | Ericsson
S2-2106339 | 23.247: Modification on UE leave. | vivo
S2-2106088 | 23.247: Clarification on Session leave procedure. | Huawei, HiSilicon
S2-2105758 | 23.247: Update the MBS Session Leave procedure. | Tencent
S2-2106078 | 23.247: Clarification on SMF removing and Session release procedure. | Huawei, HiSilicon
S2-2106333 | 23.247: Make shared tunnel establishment common. | vivo
WF proposal
Take ? as the baseline contribution.

## Slide 42: Broadcast related
- | Session broadcast | -
S2-2105911 | 23.247: MBS Broadcast clarification. | CBN, Huawei, HiSilicon
S2-2105921 | 23.247: MBS procedures for broadcast session. | CATT
S2-2105898 | 23.247: Update [7.3] MBS procedures for Broadcast Session. | Samsung
S2-2106525 | 23.247: Updates to Delivery Status Indication for Broadcast. | Nokia, Nokia Shanghai-Bell
S2-2105642 | 23.247: Update [7.3] with the new AMF service for broadcast MBS Session. | Ericsson
WF proposal
Take S2-2106525 as the baseline for 7.3.5; Take S2-2105911 as the baseline for 7.3.1; Take S2-2105921 as the baseline for 7.3.2; Take S2-2105642 as the baseline for 7.3.3; Take S2-2105898 as the baseline for 7.3.4; For the documents above, remove the changes on other section(s).

## Slide 43: Other documents
- | Session Join/Leave/Update | -
S2-2106332 | 23.247: AF requested multicast session management procedure. | vivo, juniper
S2-2105652 | 23.247: Implication of associating UEs with an MBS Session in NG-RAN using PDU Session resource procedure. | Ericsson
S2-2106433 | How to handle associated QoS flows for individual fallback in policy control | Nokia, Nokia Shanghai-Bell
S2-2106090 | 23.247: Updates about MB-UPF Configuration. | Huawei, HiSilicon
S2-2106435 | 23.247: Corrections to Clause 7.2.1.3 to address PCF interactions. | Nokia, Nokia Shanghai-Bell
S2-2106337 | 23.247: Modification on multicast session update procedure. | vivo
S2-2106366 | 23.247: Update the clause 7.2.6 Multicast session update procedure. | ZTE
S2-2105952 | 23.247: Update [7.2] MBS Scalable QoS modification. | Panasonic Corporation, DENSO CORPORATION
S2-2105905 | 23.247: Update to Clause 7.2.2.4: Release of shared delivery toward RAN node. | LG Electronics, LG Uplus, KT Corp.
- | Other documents on concepts, principles and service provisioning | -
S2-2105818 | 23.501 CR3091 (Rel-17, 'D'): Update clause number for MB-UPF, MBSF and MBSTF in clause 6.2 | Ericsson
S2-2105644 | 23.247: Update to [6.6] QoS handling. | Ericsson
S2-2106431 | 23.247: MBS Policy. | Nokia, Nokia Shanghai-Bell
S2-2105643 | 23.247: Update [4.1] Potential issue of Individual MBS traffic delivery and its Mitigation . | Ericsson
Session management
General concept
S2-2105639 | 23.247: Update [7.1] Common Procedure with modified MB-SMF service operation . | Ericsson |  | 7.1.1, 7.1.3, 7.1.5
S2-2105640 | 23.247: Update [7.2] Multicast procedures with updated MB-SMF services . | Ericsson |  | Message name: 7.2.1.3, 7.2.1.4, 7.2.2.2, 7.2.2.3, 7.2.2.4, 7.2.5.2, 7.2.5.3, 7.2.6

## Slide 44: Other documents (501/502/503)
8.9 | - | - | - | Other 501/502/503 | - | - | Docs:=10 |  | -
8.9 | S2-2105901 | CR | Approval | 23.502 CR3006 (Rel-17, 'F'): Release of PDU Session associated with an MBS session | Samsung | Rel-17 |  |  | 
8.9 | S2-2106470 | CR | Approval | 23.501 CR3226 (Rel-17, 'F'): UPF configuration for traffic replication for MBS | Nokia, Nokia Shanghai-Bell | Rel-17 |  |  | 
8.9 | S2-2106472 | CR | Approval | 23.501 CR3227 (Rel-17, 'B'): SMF discovery for 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 |  |  | 
8.9 | S2-2106475 | CR | Approval | 23.502 CR2757R3 (Rel-17, 'B'): UDM extensions for 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 | Revision of (Withdrawn) S2-2104009 from S2-145E |  | 
8.9 | S2-2106491 | CR | Approval | 23.502 CR2878R1 (Rel-17, 'B'): BSF extensions for 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 | Revision of (Postponed) S2-2104785 from S2-145E |  | 
8.9 | S2-2106520 | CR | Approval | 23.501 CR2877R1 (Rel-17, 'B'): NRF extensions for 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 | Revision of (Noted) S2-2104003 from S2-145E. Confirm CR Revision - CR states -1! |  | 
8.9 | S2-2106523 | CR | Approval | 23.502 CR3121 (Rel-17, 'B'): NRF extensions for 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 |  |  | 
8.9 | S2-2106437 | CR | Approval | 23.503 CR0579R1 (Rel-17, 'B'): PCC impacts of 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 | Revision of (Postponed) S2-2104017 from S2-145E |  | 
8.9 | S2-2106456 | CR | Approval | 23.501 CR3223 (Rel-17, 'B'): AMF impacts of 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 |  |  | 
8.9 | S2-2106457 | CR | Approval | 23.501 CR3224 (Rel-17, 'B'): NEF impacts of 5MBS | Nokia, Nokia Shanghai Bell | Rel-17 |  |  | 
Ericsson0817: can moved to UP handling
- | Other 501/502/503 | - |  | -
S2-2106472 | 23.501 CR3227 (Rel-17, 'B'): SMF discovery for 5MBS | Nokia, Nokia Shanghai Bell | NOTED? | 
S2-2106475 | 23.502 CR2757R3 (Rel-17, 'B'): UDM extensions for 5MBS | Nokia, Nokia Shanghai Bell |  | 
S2-2106491 | 23.502 CR2878R1 (Rel-17, 'B'): BSF extensions for 5MBS | Nokia, Nokia Shanghai Bell |  | 
S2-2106520 | 23.501 CR2877R1 (Rel-17, 'B'): NRF extensions for 5MBS | Nokia, Nokia Shanghai Bell | merged into S2-2105819. | 
S2-2106523 | 23.502 CR3121 (Rel-17, 'B'): NRF extensions for 5MBS | Nokia, Nokia Shanghai Bell |  | 
S2-2106437 | 23.503 CR0579R1 (Rel-17, 'B'): PCC impacts of 5MBS | Nokia, Nokia Shanghai Bell |  | 
S2-2106456 | 23.501 CR3223 (Rel-17, 'B'): AMF impacts of 5MBS | Nokia, Nokia Shanghai Bell | merged into S2-2105819. | 
S2-2106457 | 23.501 CR3224 (Rel-17, 'B'): NEF impacts of 5MBS | Nokia, Nokia Shanghai Bell | merged into S2-2105819. | 

## Slide 45: Slides for information

## Slide 46: Topic #1: NF services for SMF/AMF/MB-SMF (for information)
# and source | MB-SMF-SMF | SMF-AMF | MB-SMF-AMF
S2-2105916 | Nsmf_MBSDataTransfer_Create | Namf_MBS_SessionStatusUpdate | Namf_MBS_N2MessageTransfer request
S2-2106121 | Nmbsmf_Information_Notify |  | Namf_MBSSession_Update Request (Similar as update)
S2-2106334 | Nsmf_MBSSession_Activation | Namf_Communication_MBSActivation | Namf_Communication_MBSActivation
S2-2106454 |  | Namf_MTMulticast_EnableReachability | 
S2-2105638 |  |  |