SA WG2 Meeting #146E	S2-210xxxx						S2-19xxxxx

August 16 – 27, 2021, E-Meeting

Source:	Ericsson

Title:	Update [9.1] MB-SMF services and Resolving ENs

Document for:	Approval

Agenda Item:	8.9

Work Item / Release:	5MBS/Rel-17

Abstract of the contribution: This paper updates MB-SMF service and service operations.

# Discussion

The following MB-SMF services are defined in TS 23.247 v1.0.0:

Table 9.1.1-1: NF services provided by MB-SMF

| Service Name | Service Operations | Operation Semantics | Example Consumer (s) |
| --- | --- | --- | --- |
| Nmbsmf_TMGI | Request | Request/Response | NEF, MBSF, AF |
|  | Release | Request/Response | NEF, MBSF, AF |
| Nmbsmf_Reception | Request | Request/Response | AMF, SMF |
|  | Release | Request/Response | AMF, SMF |
| Nmbsmf_Information | Request | Request/Response | SMF |
|  | Notify | Subscribe/Notify | SMF |
|  | Subscribe |  | SMF |
|  | Unsubscribe |  | SMF |
| Nmbsmf_MBSSession | Create | Request/Response | MBSF, NEF, AF |
|  | Update | Request/Response | MBSF, NEF, AF |
|  | Release | Request/Response | MBSF, NEF, AF |

There are several related ENs, e.g.

7.2.1.2	Establishment of a PDU Session that can be associated with multicast session(s)

…

Editor's note: What exact service operations will be used is FFS.

9.1.2	Nmbsmf_TMGI service

Editor's note: Whether TMGI allocation/deallocation can be combined with Nmbsmf_MBSSession service is FFS.

9.1.5	Nmbsmf_MBSSession Service

9.1.5.1	General

…

Editor´s note: Subscription for MBS Session Status and related notifications are ffs (and depend on the definition of related events).

For interaction between AF and 5GC (applicable for both multicast and broadcast),

In our view, the same MB-SMF service operation Nmbsmf_MBSSession_Create can be used for session creation with and without service requirement, i.e., Nmbsmf_MBSSession_Create can be used to

Create MBS Session requesting only TMGI allocation (for one or multiple TMGIs), i.e. without service requirement provided

Create MBS Session requesting TMGI allocation and with service requirement provided

Create MBS Session with service requirement provided

If TMGI is allocated separately, then Nmbsmf_MBSSession_Update is used to provide service requirement and remove service requirement.

[Proposal-1] It is proposed to include TMGI allocation as part of Nmbsmf_MBSSession_Create service operation (see also Figure 1)

For multicast MBS Session,

-	At UE join,

-	the SMF will need to do two things:

- Retrieves from MB-SMF the MBS QoS information and the IP multicast distribution info of MB-UPF of the MBS Session

- Inform MB-SMF to notify SMF the MBS Session status change (e.g. update/activate/deactivate the MBS session)

The above can be achieved by SMF subscribing to the MB Session context status with immediate reporting of the current QoS and IP multicast distribution info of MB-UPF using Nmbsmf_MBSession_ContextStatusSubscribe.

-	when NG-RAN informs the MB-SMF of MBS Session setup via AMF, the AMF forward the NG-RAN MBS UP information to the MB-SMF using Nmbsmf_MBSession_UpdateContext (similar as NG-RAN providing N3 Tunnel Info for an PDU session). At the same time the AMF may implicitly subscribe to change of the MB Session context status in MB-SMF, e.g. to update/activate/deactivate the MBS session.

-	At MBS Session update/activation/deactivation/release (triggered by AF),

-	the MB-SMF notifies the SMF of the MB Session context status change using Nmbsmf_MBSession_ContextStatusNotify.

-	the MB-SMF notifies the AMF of the MB Session context status change using Nmbsmf_MBSession_ContextStatusNotify.

-	At UE leave,

-	if it is the last UE leave, the SMF will invoke Nmbsmf_MBSession_ContextStatusUnsubscribe service operation.

-	If the SMF determines that Individual Delivery may be applied, at the first UE join, the SMF may update MB-SMF of the tunnel info for MBS data at UPF using Nmbsmf_MBSession_UpdateContext.

Based on the above, the following are proposed:

[Proposal-1] Replace “Nmbsmf_Information” with new service operation in Nmbsmf_MBSession, see Figure 1.

[Proposal-2] Replace “Nmbsmf_Reception” with new service operation in Nmbsmf_MBSession, see Figure 1.

Figure 1 Proposed service operation Nmbsmf_MBSSession.

# Proposal

It is proposed to update TS 23.247 v1.0.0 as follows:

* * * Start of change* * *

## 9.1	MB-SMF Services

### 9.1.1	General

The following table illustrates the MB-SMF Services for MBS.

Table 9.1.1-1: NF services provided by MB-SMF

| Service Name | Service Operations | Operation Semantics | Example Consumer (s) |
| --- | --- | --- | --- |
| Nmbsmf_MBSSession | Create | Request/Response | MBSF, NEF, AF |
|  | Update | Request/Response | MBSF, NEF, AF |
|  | Release | Request/Response | MBSF, NEF, AF |
|  | ContextStatusSubscribe | Subscribe/Notify | AMF, SMF |
|  | ContextStatusUnsubscribe |  | AMF, SMF |
|  | ContextStatusNotify |  | AMF, SMF |
|  | ContextUpdate | Request/Response | AMF, SMF |

### 9.1.1	Nmbsmf_MBSSession Service

#### 9.1.1.1	General

Service description: This service operates on the multicast and broadcast sessions. The following are the key functionalities of this NF service:

-	(between MBSF/NEF and MB-SMF) Allocate TMGI, Create/Modify/Activate/Deactivate/Release of multicast sessions;

-	(between MBSF/NEF and MB-SMF) Allocate TMGI, Create/Modify /Release of broadcast sessions;

-	(between SMF and MB-SMF, only for multicast MBS Session) Request QoS of MBS Session, request notification of MBS Session context status change, provide tunnel info for MBS data at UPF for individual delivery

-	(between AMF and MB-SMF) Forward NG-RAN MBS UP info, request notification of MBS Session context status change.

Editor's note:	Parameters of the service operations are FFS.

#### 9.1.1.2	Nmbsmf_MBSSession_Create service operation

Service operation name: Nmbsmf_MBSession_Create.

Description: Create a new multicast session or broadcast session.

Input, Required: Session Type, Request Type

Input, Optional: MBS Session ID (source specific multicast address or TMGI), DNN, S-NSSAI, MBS service area, MBS activation time, MBS termination time, service description, QoS information, Input Transport Address Request, session activity status (active/inactive).

Output, Required: Result Indication.

Output, Optional: TMGI(s), Cause, MB-UPF tunnel info.

Multiple TMGIs may be allocated in one request.

#### 9.1.1.3	Nmbsmf_MBSSession_Update service operation

Service operation name: Nmbsmf_MBSession_Update.

Description: AF provides service requirement (e.g. QoS, flow description) if TMGI is allocated in advance, or AF updates the established multicast session or broadcast session, e.g. QoS update.

Input, Required: MBS Session ID.

Input, Optional: QoS information, flow description, MBS service area, session activity status (active/inactive).

Output, Required: Result Indication.

Output, Optional: Cause.

#### 9.1.1.4	Nmbsmf_MBSSession_Release service operation

Service operation name: Nmbsmf_MBSession_Release.

Description: Release the multicast session or broadcast session.

Input, Required: MBS Session ID.

Input, Optional: None.

Output, Required: Result Indication.

Output, Optional: Cause.

#### 9.1.1.5	Nmbsmf_MBSSession_ContextUpdate service operation

Service operation name: Nmbsmf_MBSSession_ContextUpdate

Description: This service operation, which is applicable to multicast MBS session, is used by the consumers to update MBS Session, e.g. forward the NG-RAN MBS UP info.

Input, Required: MBS Session ID

Input, Optional: NG-RAN MBS UP information, UPF MBS UP information.

Output, Required: Result Indication.

Output, Optional: Cause.

NG-RAN MBS UP information is provided by NG-RAN and sent transparently by the AMF to the MB-SMF.

UPF MBS UP information is only applicable for individual delivery of multicast session.

#### 9.1.1.6	Nmbsmf_MBSSession_ContextStatusSubscribe service operation

Service operation name: Nmbsmf_MBSSession_ContextStatusSubscribe

Description: This service operation, which is applicable to multicast MBS session, is used by the consumer to subscribe to change of the MBS Session context status.

Input, Required: MBS Session ID, Status information to be subscribed

Input, Optional: Immediate Reporting Indication.

Output, Required: Result Indication.

Output, Optional: Cause, QoS profile(s) of the MBS Session, MBS IP Multicast Distribution

Status information to be subscribed may be one of the following events:

-	session update, session deactivation (only for multicast MBS Session), session re-activation (only for multicast MBS Session), session release.

Immediate Reporting Indication is always included and the MB-SMF returns the QoS profile(s) of the MBS Session and MBS IP Multicast Distribution.

#### 9.1.1.7	Nmbsmf_MBSSession_ContextStatusUnSubscribe service operation

Service operation name: Nmbsmf_MBSSession_ContextStatusUnSubscribe

Description: This service operation, which is applicable to multicast MBS session, is used by the consumer to unsubscribe to change of the MBS Session status.

Input, Required: MBS Session ID

Input, Optional: None.

Output, Required: Result Indication.

Output, Optional: Cause.

#### 9.1.1.8	Nmbsmf_MBSSession_ContextStatusNotify service operation

Service operation name: Nmbsmf_MBSSession_ContextStatusNotify

Description: This service operation, which is applicable to multicast MBS session, is used by the MB-SMF to notify its consumers about the status change of an MBS Session.

Input, Required: MBS Session ID, Status information

Input, Optional: QoS information of MBS Session, MB service area

Output, Required: Result Indication.

Output, Optional: Cause.

Status information may include one of the following events:

-	session update, session deactivation, session re-activation (only for multicast MBS Session), session release.

* * * End of changes * * *