## Slide 1
New SID proposal on
Enhancement of 5G AM Policy in R18
Zhuoyi Chen
China Telecom

## Slide 2
  AM Policy alignment in interworking scenario (4G and 5G)
  Finer granularity
  New trigger for AM policy
The Access and Mobility Policy control introduced in 5G encompasses the management of service area restrictions, the management of the RFSP functionalities and UE-AMBR by PCF.
Some potential enhancements for study in AM Policy are identified based on the Rel-17 SA2 issues and Rel-18 SA1 requirements:
  FS_eAMP for Rel-18

## Slide 3
  AM Policy Alignment in Interworking Scenario (4G and 5G)
A PING-PONG Issue from RFSP Index conflict:
While the UE is in 5G, the PCF decide to change the subscription RFSP Index to direct the UE to 4G.
While the UE is in 4G, the MME select its RFSP Index according to Subscription Data or Local configuration, and direct the UE to 5G.
Also, it needs to support RFSP Index update for UE to move from 4G to 5G.
  AM Policy is NOT supported in EPC. It may result in AM parameters conflict while a UE is in an interworking scenario.
A dynamic mechanism needs to be investigated to support AM policy update for the EPC side.

## Slide 4
  Solutions for roaming cases
New mechanism needs to be investigated for the notification of application detection from H-PCF to V-PCF.
  The DCAMP solution for R17 only applies to non-roaming cases. In HR cases, how V-PCF (AM) to subscribe notification of application detection from user plane via H-PCF (SM) are not discussed.
Overall roaming reference architecture of policy and charging control framework for the 5G System - home routed scenario
To receive the detection of application in use from user plane, the V-PCF (AM) needs to subscribed to the H-PCF (SM) where PCRT is reported from SMF and UPF.
Current mechanism do not have interaction between H- and V- PCF that responsible for different policy control.

## Slide 5
  New triggers for AM policy
  Policy decisions based on spending limits is a function that allows PCF taking session related policy actions related to the status of policy counters that are maintained in the CHF. Some scenarios may have the PCF for a UE make policy decision based on spending limits a useful function for AM policy control as well.
  **This topic might be updated according to the WID_TEI_18_SLAMUP
The new triggers for AM policy, e.g., from CHF and the procedure to be used in both non-roaming and roaming scenarios should be investigated.

## Slide 6
  Timeline for Study
  Expect to start with other R18 studies depending on SA2 time plan
    Estimated 3 TUs for study phase，and 1.5 TUs for normative phase.
  Sent to TSG for information in June 2022
  Sent to TSG for approval in Sep. 2022

## Slide 7
THANK YOU