## Slide 1: Authentication & Subscription info checking for Disaster Roaming service
Hyunsook Kim
LG Electronics, KT Corp., LG Uplus, SK Telecom

## Slide 2: TS 23.501 Registration procedure
UE Authentication for Roaming Disaster service
UE subscription info for Roaming Disaster service

## Slide 3: Option 1 – Disaster Roaming indication
During the authentication and subscription information checking,
“Disaster Roaming indication” is transferred from AMF to AUSF/UDM
Direct and clear notification for AUSF/UDM behavior/management
Option 2 – Configuration via OAM
Basically, disaster roaming will be started based on the request by the government agencies or the authorities (out of 3GPP scope)
the configuration via OAM based on operator policy and the request by the government agencies when the disaster roaming occurs.
During the authentication and subscription information checking, no additional signaling

## Slide 4: Proposals
It is proposed to specify both options
for operator’s flexible deployment and preference.
Proposed CRs: TS 23.501 (S2-2107159), TS 23.502 (S2-2107160)

## Slide 5: Annex. (option 1) authentication procedure
+ Disaster Roaming indication,
[TS 33.501]

## Slide 6: Annex. (option 1) AUSF service
+ Disaster Roaming indication
[TS 33.501]

## Slide 7: Annex. (option 1) UDM service
+ Disaster Roaming indication
+ Disaster Roaming indication
[TS 33.501]
[TS 23.502]

## Slide 8: Annex. (option 2) Registration procedure
For Disaster Roaming service,
the AUSF and the UDM are configured
with Disaster Condition via OAM
based on operator policy and the request by the government agencies.
Based on this local configuration,
the AUSF executes authentication of the UE.
Based on this local configuration,
the UDM provides the subscription data to the AMF.