## Slide 1
2021.10.12
Study on AI based Positioning in Rel-18 eNA Ph3

## Slide 2
Applicable use cases for AI based Positioning
  Compared to Rel-16/Rel-17 solutions, AI based solutions could increase the accuracy dramatically at least for the following scenarios
    To combat NLOS in Indoor Factory with Dense clutter and High base station height (InF-DH) scenarios
    To combat synchronization error between different TRPs
    To combat Tx-Rx timing error between different TRPs and UEs
Parameters：Deployment and channel model is based on current Rel-17 Positioning item discussion. InF-DH {0.6,6,2} is focused..

## Slide 3
AI enhanced positioning without new measurement
Positioning
  Data samples can be collected by the network to train a neural network model applied at LMF with Rel-17 specified measurement and report
  Inference of UE location at LMF based on Rel-17 specified measurement and report (e.g first path delay and power)
  Model transfer may be needed between Nodes (e.g LMF and NWDAF)

## Slide 4
AI enhanced positioning with new measurement
Positioning
  Data samples can be collected by the network to train a neural network model applied at LMF with Rel-17 specified measurement and report and newly defined measurement and report beyond Rel-17
  Inference of UE location at LMF is based measurement and report specified in R17 and beyond (e.g. channel impulse response, phase difference)
  There is potential AI model transfer between Nodes(e.g between LMF and NWDAF)

## Slide 5: Potential network architecture enhancement for AI based positioning
  Led by eNA_Ph3:
  Enhanced architecture for AI based positioning, supporting：
    Model training for AI based positioning in NWDAF(MTLF)
    AI positioning inference in NWDAF(AnLF, collocated with LMF)
  Data collection by NWDAF(MTLF)
    Training data collection triggered by NWDAF(MTLF) from LMF and optionally from other entities (e.g. UE, AF or OAM)
  Led by eLCS_Ph3:
  Data collection via NRPP or NRPPa for inference and model training，i.e. measurement and report specified in R18 and beyond.

## Slide 6: Conclusion
AI based positioning increases LCS accuracy with or without newly defined measurements at least for some identified use cases;
It is proposed to study AI based positioning in FS_eNA_ph3 and FS_eLCS_ph3 with following coordination:
  - Potential network architecture enhancements for AI based positioning and NWDAF triggered data collection led FS_eNA_Ph3;
  Data collection via NRPP or NRPPa led by FS_eLCS_ph3