## Slide 1: eNPN Status Report
Peter Hedman
Ericsson (Rapporteur)

## Slide 2: eNPN status after SA2#147E (1/4)
General
  2 editorial cleanup CRs agreed (23.501, 23.502)
  No consensus whether SNPN can support network slicing features defined in Rel-16/17 (e.g. NSSAA, NSAC, NSSRG) (LS from CT1 postponed)
  No agreement whether NSAC needs to be possible for slice(s) used for onboarding (topic postponed including LS from CT1, replies and CR)
  LS reply sent to to RAN2 (cc: CT1) on limited-service availability of an SNPN, but no consensus whether R17 SNPN-capable UEs that are not in SNPN Access Mode can or cannot camp on an SNPN cell supporting emergency services to obtain emergency services via any SNPN. CR in S2-2107315 postponed
  LS sent to GSMA TSG asking whether a device is required to have/signal separate IMEI for each simultaneous registration towards separate network (PLMN and SNPN)
Related to Key Issue 1 (Enhancements to Support SNPN along with credentials owned by an entity separate from the SNPN):
  1 CR agreed to 23.501 clarifying that updating CH controlled lists via SoR is not applicable for CH with AAA server
  1 CR agreed to 23.501 clarifying that while roaming is not supported it is possible for a UE to access an SNPN with credentials from a CH
  Next Steps: maintenance
WI Code | Work Item Title | WP | Target Date | WID#
eNPN | Enhanced support of Non-Public Networks | 95% > 97% | Sept, 21 | SP-200980

## Slide 3: eNPN status after SA2#147E (2/4)
Related to Key Issue 2 (NPN support for Video, Imaging and Audio for Professional Applications (VIAPA))
  No CRs submitted
  Next Steps: maintenance
Related to Key Issue 3 (Support of IMS voice and emergency services for SNPN)
  No CRs agreed
  Discussion without conclusion on possible need to update IMC definition in 21.905
  Next Steps: maintenance
WI Code | Work Item Title | WP | Target Date | WID#
eNPN | Enhanced support of Non-Public Networks | 95% > 97% | Sept, 21 | SP-200980

## Slide 4: eNPN status after SA2#147E (3/4)
Related to Key Issue 4 (UE Onboarding and remote provisioning)
  1 CR agreed to 23.501 clarifying the onboarding architecture with two DCS options (with AAA or AUSF/UDM)
  2 CRs agreed to 23.501 and 23.502 updating NF discovery and selection for SNPN Onboarding
  1 CR agreed to 23.501 clarifying the network selection for ON-SNPN
  1 CR agreed to 23.501 clarifying when UE triggers procedure to be provisioned with credentials used for NSSAA or secondary authentication/authorization over UP remote provisioning
  1 CR agreed to 23.501 updating ON-SNPN to ONN, in order to include both SNPN and PLMN as the Onboarding Network to provide UP Remote Provision related info to UE
  1 CR agreed to 23.501 clarifying that for PLMNs it is assumed that DNN and S-NSSAI used for onboarding are only used in the context of UE onboarding
  1 CR agreed to 23.501 clarifying that for remote provisioning of credentials for NSSAA or secondary authentication SMF sends PVS address information to the UE via PCO based on the UE’s subscribed DNN(s)/S-NSSAI(s)
  1 CR agreed to 23.502 correcting the NF/NF service discovery between SNPN and DCS
  1 CR agreed to 23.501 clarifying that based on operator policy, PCC rules can be configured to restrict traffic other than provisioning traffic between PVS/DNS server(s) and UE(s)
  1 CR agreed to 23.501 clarifying UE Configuration Data and PVS address(es) handling
  1 CR agreed to 23.503 clarifying the PVS address(es), and that DNS address(es) are locally configured at the PCF
  Next Steps: maintenance
WI Code | Work Item Title | WP | Target Date | WID#
eNPN | Enhanced support of Non-Public Networks | 95% > 97% | Sept, 21 | SP-200980

## Slide 5: eNPN status after SA2#147E (4/4)
  RAN impacts and dependencies:
  As per agreed CRs the RAN impacts are SIB related for changes related to Key issues 1, 3 and 4; new RRC indication for solutions related to Key issues 4
SA3 dependencies
  SA3 dependencies identified functionality related to support of Credentials Holder, support of IMS voice and emergency, and support for UE onboarding.
  SA3 feedback expected on e.g. Onboarding architrecture related to DCS and CP provisioning of credentials for NSSAA and/or secondary authentication
Contentious Issue:
  -
Focus for the Next Meeting (SA2#148E):
  Maintenance including changes required to support input from other WGs e.g. SNPN support for network slicing features, and limited-service logic
Overall Plan:
  Maintenance
Risks:
  Completion of the work dependent on progress in SA3 (KI#4)

## Slide 6: eNPN Status at SA#94e
Progress since SA#92-e:
  To be added
  RAN impacts and dependencies:
  RAN impacts as per agreed CRs:
    Impacts are SIB related for changes related to Key issues 1, 3 and 4; new RRC indication for solutions related to Key issues 4
Next steps:
  Corrections, and alignments with other WGs
WI Code | Work Item Title | WP | Target Date | WID#
eNPN | Enhanced support of Non-Public Networks | 95% > xx% | Sept, 21 | SP-200980
NOT UPDATED