## Slide 1: Motivation for Study on Seamless UE context recovery (Samsung)
S2-2107384

## Slide 2: Problem Statement#1:
For the events which needs only MM context recovery, the SM context and Application context is also deleted. Example events that lead to MM context reset to occur:
    Silent reset at Modem
    Security patch updates
    OS upgrade
    Modem feature or system SW updates
    Device reboot upon Modem setting changes
    Network initiated Detach Request with “Re-Attach Required”
AS-IS (problem)
Device reboots (De-registration followed by Re-Registration):
Device Side:
All active PDU sessions are deactivated.
MM & SM contexts Released
Network side:
UE’s MM & SM context released.
Socket connections to APP servers released
Impacted nodes: UE, AMF, SMF, UPF, All Apps

## Slide 3: Problem Statement#1(contd):
AS-IS (problem)
Device Side:
All active PDU sessions are deactivated.
MM & SM contexts Released
Network side:
UE’s MM & SM context released.
Network Tunnels released.
Impacted nodes: UE, AMF, SMF, UPF, All Apps
TO-BE (Solution)
Device Side:
Only MM context recovery steps are executed.
SM and App context is retained.
Network side:
MM context is recovered without impacting SM context.
No impact to APP context.
Impacted nodes: UE, AMF

## Slide 4: Traffic for discussed events due to legacy handling.
Chart: 
| 100 Million | 200 Million | 300 Million | 400 Million
Minimum | 300 | 600 | 900 | 1200
Maximum | 1000 | 2000 | 3000 | 4000
Number of subscribers in network
Number of Message exchanges in millions between NFs per day
Kindly refer to Annex for detailed analysis.

## Slide 5: Observations in legacy handling.
1) Signalling overload:
Lets take event binary upgrades as an example. Today when UE is required to perform upgrades. Following steps are executed:
  Binary is pushed in the UE.
  UE performs detach procedure. UE and Network looses MM context, SM context, All the application context.
  UE installs the binary.
  UE performs attach procedure. Performs MM signalling and get the MM context, Performs SM signalling for each PDU session and creates SM context, Perform all Applications signalling and create the Application level context.
As seen in previous slide, i.e. Total signalling per UE = MM signalling + X * (SM signalling) + Y * (App level signalling)
X= Number of PDU sessions active before upgrade.
Y= Number of Application
Total signalling on the network = Total signalling per UE * Number of UEs facing an event. We believe majority part of this load can be easily avoided.
2) Communication of internal 3GPP system aspects to 3rd party applications:
Whenever a reset of MM layer occurs for example due to silent restart at the UE or NF restart in 3GPP system, it is instantly communicated all the way up to the application layer, because IP address allocated to the UE is also lost. In 5GS, with increasing verticals expected to get integrated with 3GPP system and various deployment models, such communication of internal aspects in the 3GPP system to those 3rd party applications/verticals is not desirable. This may lead to a situation where such 3rd party applications interacting with multiple operators are able to rank the quality of serving operator, resulting in unintended consequences for the serving operators. Thus study aims for application unaware UE context recovery.
3) The service re-activation time is increased.
Within the current 3GPP system, the MM context reset recovery procedure involves first, the re-establishment of MM context, followed by SM context re-establishment, and then re-establishment of application layer instead of simply recovering MM context alone. This leads to comparative delays in re-establishing the application sessions. If those applications are time sensitive applications any delay in re-establishing the application layer sessions is not desirable.

## Slide 6: Problem Statement#2(Background):
Application Server
Operator
Three Entities are involved for upgrade procedure Device(UE) manufacturer, Operator and Application server.
For open market devices binary updates are pushed by device manufacturer.
For operator owned devices binary is pushed either by operator or device manufacturer.
Once binary is pushed into the device when exactly the upgrade procedure will be performed is up to UE implementation.
Upgrade procedure is executed in the order of the minutes and during this period UE is not available for any services.
Traditionally for smartphones only impacts of services was for the user thus smartphones seek the user input before such upgrade procedures are executed.
Device manufacturer

## Slide 7: Problem Statement#2:
UE becomes unavailable in the order of minutes whenever upgrades are performed by the UE. Further UEs become unavailable without Application server or core network having knowledge about it.
This can impact the critical operations of application server, if UE is responsible for it during the “unavailability period” of the UE.
Thus there is a need for co-ordination between UE and Network/Application Function. For example if application server is aware that UE will not be available for up to 3 minutes at 12 in the night due to the upgrades it can assign alternate(or backup) UE to perform the respective critical operation and take care that alternate UE does not get into upgrade operation during same period.
NOTE: Upgrade is just an example discussed here, UE becomes unavailable for other events too as discussed in earlier slides.
Application Function or Core Network
On UE side:
UEs have received the binary. UE-1 & UE-2 has decided to perform upgrade procedure.
Both UE-1 && UE-2 decides to perform upgrade operation at 12 in the night.
They starts upgrade procedure at 12 in the night and becomes unavailable to the network.
On Application Function side:
At 12:01 an event occurs due to which the UE-1 is required to gather some data in the UE-1 environment. Thus Application Function is trying to reach the UE-1. UE-1 is unavailable.
AF tries to reach UE-2, UE-2 is also not available.
AF is wondering why both the UEs are not reachable and are not aware how long they are not available.
This non co-ordination of “unavailability time” can have impacts to the services of application function.
UE-1
UE-2

## Slide 8: Proposed SID Objectives: Seamless UE context recovery
Following objectives are expected to be studied:
  Objective 1 (WT#1): Study the mechanisms in which the “unavailability period” is determined for the UE based on co-ordination between UE-5GC and 5GC-AF(s).
  Objective 2 (WT#2): Study the mechanisms for zero or minimal cross layer impact on the UEs contexts at both UE and network side (e.g AMF, SMF), minimizing session management and upper layer service interruptions when UE gets into RM-DEREGISTERED state and re-register again.

## Slide 9: Annexure

## Slide 10: Number of UEs per day face the event.
 | Percentage Users per day | Event
 | 3.33 | Security patch updates are done per month
 | 1.11 | MR i.e. Modem binary updates once in quarter
 | 0.25 | OS upgrades per year
 | 2.5 | Silent reset. Field data from one operator indicates 2.5-4% UEs perform this event but its hard to believe that this is true globally thus we consider lower band value i.e. 2.5%
 | 1 | There are multiple other triggers as discussed in earlier slides.
Total | 8.19 | 
Lets assume 3% as lower bound and 8% as upper bound.
NOTE 1: In the field sometimes security patch, MR and OS upgrades are clubbed together.

## Slide 11: Signalling per UE during re-registration.
MM Signalling:: Figure 4.2.2.2.2-1: Registration procedure(23.502)
X * (SM Signalling per UE:: Figure 4.3.2.2.1-1: PDU Session Establishment (23.502))
Y * (Application signalling per UE::Figure 5.1: IMS Registration (23.228)

## Slide 12: Number of message exchanges between NFs:
From 23.502: number of message exchanges:
Attach procedure : 25
Deregistration procedure : 8
PDU session : 63 (3*21 where 3 is number of PDU sessions active before the event)
Application signalling : 40 (4* 10 assuming 10 applications with 4 message exchanges for recovery)
== 136.
Additionally few other procedures may get executed for e.g. security and NSSAA etc.
Let us consider range of message exchanges = 100 to 125
Minimum calculation:
3% of the UEs per day face this event, If we assume 100 million subscribers, 3 million subscribers face this event per day.
Thus total message exchanges between NFs and NF-UE = 3 million * 100
= 300 million message exchanges per day.
Maximum calculation:
8% of the UEs per day face this event, If we assume 100 million subscribers, 8 million subscribers face this event per day.
Thus total message exchanges between NFs and NF-UE = 8 million * 125
= 1000 million message exchanges per day.