## Slide 1
SA2#148E
Discussion on UE ID of SNPN UE used for accessing emergency services in PLMN
vivo

## Slide 2
Background
A SNPN subscribed UE in limited states can access to a PLMN for emergency services
A PLMN may authenticate a UE during emergency registration or not
During the emergency registration, in case of authentication failure, the network may still accept the UE access or not, depend on operators’ policy
A PLMN doesn’t support NID and doesn’t support NSI based SUCI with NID
A SNPN’s MCC and MNC may not be unique

## Slide 3
Issues
Scenario1: the MCC and MNC of of the subscribed SNPN is unique
NSI based SUPI shall not be used since the serving PLMN doesn’t support the NID nor use it to select AUSF. So the authentication cannot be performed. If authentication is required by the PLMN, the SNPN subscribed UE may be rejected by the PLMN.
IMSI based SUPI shall be used in order to support the possible authentication by the serving PLMN.
Proposal1: for scenario1, IMSI shall be used, NSI based SUPI shall not be used.

## Slide 4
Issues
Scenario2: the MCC and MNC of the subscribed SNPN is not unique
Issue1: The AMF of serving PLMN cannot index the AUSF of subscribed SNPN based on the PLMN ID of the IMSI, so the authentication cannot be performed when IMSI is provided.
Issue2: UE A and UE B with the same IMSI may access a PLMN and the PLMN AMF cannot distinguish UE A and UE B
Propose2: use PEI instead for scenario 2

## Slide 5
Proposals
Comment: how the UE knows the MCC and MNC of the SNPN is unique or not?
Proposal3: whether the MCC and MNC of the SNPN is unique or not is pre-configured in the subscription/credential.
Conclusions
  the NSI based SUPI shall not be included;
  the IMSI based SUPI shall be included if and the MCC and MNC of the SNPN is unique;
  the PEI shall be included when the MCC and MNC of the SNPN is not unique;
  whether the MCC and MNC of the SNPN is unique or not is pre-configured in the subscription/credential.

## Slide 6
Thank You!