## Slide 1
Uu based Sensing
vivo
2021-11-15

## Slide 2
Sensing mode
End-to end Arch. supporting sensing
Sensing function: management, control and computing, etc.
Procedure(s):
  Sensing Control procedure
  Sensing Data report procedure
Prioritize Uu interface based sensing for Network Based Sensing ：
Existing UL reference signals for measurements executed by BS (Uu)
Existing or new measurements between BSs
Existing or new measurements based on BS echo
Existing DL reference signals for measurements executed by UE (Uu)
Sensing mode | Mode No. | Transmitter | Receiver
Network based sensing | 1 | UE | BS
 | 2 | BS A | BS B
 | 3 | BS A | BS A
 | 4 | BS | UE
UE based sensing | 5 | UE A | UE B
 | 6 | UE A | UE A
Network based sensing
(between RAN(s) , or between RAN and UE(Uu interface))
Notes: 注：可扩展到多UE多基站

## Slide 3
Uu interface based sensing(BS -> UE & UE -> BS) complements BS echo detecting
 | Transmitter BS A, receiver BS A (echo detecting) | BS -> UE & UE -> BS (Uu based sensing)
Sensing range | BS position is fixed; The number of BS is much smaller than the number of UE; The sensed area/objects is restricted | UE is widely distributed in the cell and the number of UE is larger than the number of BS. The sensed area/objects is greatly extended.
Sensing use cases | Rader-like sensing use cases including range/velocity/angle measurements | More use cases are supported (See Table 2).
Hardware implementation | In order to support echo detecting, BS need to support full duplex/pulse signal | No new hardware requirements.
Measurements |  | DL/UL | Use cases
Existing measurements | RSRP | BS -> UE & UE -> BS | Information of weather; air quality; traffic/personnel flow
 | RSRP, angle | BS -> UE & UE -> BS | 3D environment construction
New measurement | CSI (amplitude and phase of frequency domain channel response) | BS -> UE & UE -> BS | Heartbeat and breathing monitoring
 | … | … | …
Table 1: Comparison between BS echo detecting and Uu based sensing
Table 2: Example of measurements and use cases for UE involved sensing
Notes: 上报周期
耗电
NRPPa CN下任务给RAN，可能需要UE辅助。
LPP CN下任务给UE

## Slide 4
Case3:
Bodyweight exercises 3
Requirement 3:
Count and recognize different typical bodyweight exercises.
Case1:
Respiration monitoring 1
Requirement 1:
Acquire the target respiration rate of a person.
Case2:
Indoor intrusion detection 2
Requirement 2:
Detect the intrusion of a person walking inside the monitored area and track his movements.
Reuse existing reference signals for communication (e.g., SRS, CSI-RS) to support sensing.
Use cases for UE involved sensing (Uu interface sensing)
Source1 : Youwei Zeng et. al., "Farsense: Pushing the range limit of wifi-based respiration sensing with csi ratio of two antennas"
Source2 : O. Kaltiokallio and M. Bocca, "Real-Time Intrusion Detection and Tracking in Indoor Environment through Distributed RSSI Processing"
Source3 : S. Li, X. Li, Q. Lv, G. Tian and D. Zhang, "WiFit: Ubiquitous Bodyweight Exercise Monitoring with Commodity Wi-Fi Devices"

## Slide 5
Case6:
Environment Mapping 3
Requirement 6:
Exploit the multipath component information for simultaneous localization and mapping.
Case4:
Hand gesture recognition 1
Requirement 4:
Recognize dynamic hand gestures for human-computer interaction.
Case5:
Weather Monitoring 2
Requirement 5:
Use Communication links for real-­time rainfall monitoring.
Reuse existing reference signals for communication (e.g., SRS, CSI-RS) to support sensing.
Use cases for UE involved sensing (Uu interface sensing)
Source1 : W. Chen et al., "Robust Dynamic Hand Gesture Interaction using LTE Terminals"
Source2 : Messer H , Gazit L ., "From cellular networks to the garden hose: Advances in rainfall monitoring via cellular power measurements"
Source3 : C. B. Barneto, E. Rastorgueva-Foi et al., "Millimeter-wave Mobile Sensing and Environment Mapping: Models, Algorithms and Validation"

## Slide 6
Sensing procedure:
Acquire channel frequency response data based on the received reference signal (CSI-RS)
Preprocess the data(e.g., denoising, outliers removing, filtering) and execute measurement
Report measurements to the core network
Calculate sensing results
Trial (sensing for respiration monitoring) setup:
System：5G NR, Central frequency 3.63GHz, bandwidth 100MHz
Scenario：indoor
gNB-UE distance： 2 meters
Person-UE distance： 0.5 meter
CSI-RS periodicity: 20 ms
Sensing trial based on NR: trial setup
Sensing trial based on Uu interface: Respiration monitoring based on DL existing reference signals

## Slide 7
Breathing rate:~0.268Hz (16 breaths per minute)
Sensing trial based on Uu interface: trial results
Target person for breathing monitoring
Amplitude of channel frequency response
Phase of channel frequency response
Step 1: channel estimation on 1 PRB based on CSI-RS
Step 2: channel frequency response of Rx 1 ./ channel frequency response of Rx 2
Step 3: do FFT on the data from Step 2, and get the breathing rate of the target people
Utilizing the channel frequency response of existing reference signal (e.g., CSI-RS for DL and SRS for UL), the receiver can monitor the breathing rate of the target people.

## Slide 8
Observations and Proposals
Observation:
  In addition to sensing based on BS echo detecting, Uu interface sensing is also meaningful and has some practical use cases.
  It is feasible to perform Uu interface sensing by utilizing existing downlink reference signals in some use cases.
  Similar to Uu interface sensing based on downlink reference signals, Uu interface sensing based on uplink reference signals is also feasible in principle .
Proposal :
  Study how to provide network based sensing service in 3GPP network, which includes sensing based on BS echo detecting and Uu interface based sensing.
  Study Uu interface sensing service based on existing uplink/downlink reference signals (preferred in R18).

## Slide 9
THANK
YOU

## Slide 10
Sensing Contents and Scenarios
Category of comm. sensing | Sensing contents | Potential scenarios
Macro information sensing | Information of weather, air quality, etc. | Meteorology, agriculture, life services
 | Target tracking, ranging, speed measurement, shape measurement, etc. | Application scenarios of radar
 | Statistics of the traffic flow at the intersection, personnel flow (including intrusion detection) | Intelligent transportation, business services
 | 3D environment construction (including reflector detecting) | Intelligent driving and navigation (car/UAV), smart city (3D map), network planning and optimization
Short distance refined information sensing | Heartbeat and breathing monitoring | Health care, medical care
 | Imaging, material detection, etc. | Security check, industry, etc.
In wireless communication, electromagnetic waves propagation transmits signals and carries environmental information at the same time
The integration of communication and sensing is one of the most effective means to build a digital twin world

## Slide 11
Potential Architecture enhancement(s) for Supporting Network based Sensing
1) Investigate architecture enhancement for sensing by introducing a new Sensing Function and corresponding procedure(s) for sensing control and sensing data report – 3GPP SA2
2) Investigate how to handle user privacy (SA2+SA3)
3) Sensing based charging (SA2+SA5-Charging)
Fig1a. Architecture for Sensing Control (per UE)
Fig2a. Architecture for Sensing Data Report (per UE)
Fig2b. Architecture for Sensing Data Report (per area)
Fig1b. Architecture for Sensing Control (per area)

## Slide 12
1. The AMF receives the Sensing Service Request from AF (via NEF optionally), which may include the target Area/UE ID, the required QoS.
2. The AMF selects an Sensing Function based on the factors may including the required QoS, Sensing Function capabilities and its load.
3. The AMF sends the Sensing Service Request to the Sensing Function .
4. The Sensing Function selects the RAN-Node and/or UE based on the target Area/UE and decides the sensing method to be used.
5. The Sensing Function performs sensing procedures with RAN-node to collect sensing data to obtain the sensing result.
6. Sensing measurement based on UE existing measurements or RAN existing/new measurements.
7. Sensing measurement report to SF.
8-10.The Sensing Function returns the Sensing Service Response towards the AMF and AMF returns it to the source of request.
Overall procedures(per UE or Per Area)

## Slide 13
Summary: Evolution routes of network based sensing
Based on the impact of sensing on standards, there are four potential evolution phases of communication and sensing integration.
 | Phase 1 (R18) | Phase 2(see Note 2) | Phase 3 | Phase 4 (6G)
Signal (e.g. waveform, RS) | Existing signal | Existing signal | + sensing signal | Joint design of communication and sensing
Uu Measurements | Existing measurements (see Note 1) | + new sensing measurements | + new sensing measurements | + new sensing measurements
Network architecture | + Sensing Function | + Sensing Function | + Sensing Function or new architecture supporting sensing | new architecture supporting sensing
Impact on UE (RAN layer) | No | Yes |  | 
5G Advanced (R18，R19…)
6G
Note1：except the existing measurement(s) between UE and NG-RAN in R18, new sensing measurement(s) implemented by NG-RAN (outside of the 3GPP standard) could also be used for network based Sensing in R18.
Note2：If new sensing measurement(s) in Phase 2 are acceptable, Phase 2 can be combined into Phase 1.