## Slide 1: On providing Configured NSSAI to the RAN NOKIA, Nokia Shanghai Bell Convida wireless

## Slide 2: Proposal
Allow the RAN to receive the Configured NSSAI and the related RFSP and approve CR S2-2108310
This is not alternative to Target NSSAI and its RFSP, rather complementary.
  It is used at the time of determining the UE-specific camping policies to prevent redirections, not when a unsuccessful registration triggers a redirection (Target NSSAI role is linked to redirections)
  The Target NSSAI is used to redirect (after RR failure for a S-NSSAI at least) to a more specific or more generic band than current Allowed NSSAI-based band
  The Configured NSSAI is used to let the UE camp on a more generic band that supports more Slices than the allowed NSSAI and including the Allowed NSSAI. This minimizes (or even can eliminate in some configurations) the redirections based on TARGET NSSAI.
So both approaches can coexist and the provision of configured NSSAI and related RFSP to the RAN can be used by the PLMN operator to avoid RR failure due to the UE camping in more specific bands than necessary, subject to RRM policy.

## Slide 3: How is the RFSP Index sent to RAN with the Allowed NSSAI calculated?
Today, the RAN can determine the UE-specific CellReselectionPriorites it sends to the UE in the RRC Connection Release message based on the RFSP and the Allowed NSSAI of the UE.
RFSP in use is determined by AMF e.g. by using the PCF Npcf_AMPolicyControl_Create service operation by taking as input the Subscribed RFSP (which the HPLMN UDM sends to the AMF) and the Allowed NSSAI.
RFSP Index = f(RFSP Index subscribed , Allowed NSSAI)
subscribed RFSP Index, the Allowed NSSAI are optional inputs of Npcf_AMPolicyControl_Create service operation which has output as in following slide

## Slide 4: How is the RFSP Index sent to RAN with the Allowed NSSAI calculated?
Information name | Description | Category | PCF permitted to modify in a UE context in the AMF | Scope
UE-AMBR | This defines the UE-AMBR value that applies for a UE | Conditional (NOTE 5) | Yes | UE context
Service Area Restrictions | This part defines the service area restrictions |  |  | 
List of allowed TAIs. | List of allowed TAIs (NOTE 3) (NOTE 4). | Conditional (NOTE 1) | Yes | UE context
List of non-allowed TAIs. | List of non-allowed TAIs (NOTE 3). | Conditional (NOTE 1) | Yes | UE context
Maximum number of allowed TAIs | The maximum number of allowed TAIs. (NOTE 4) | Conditional (NOTE 1) | Yes | UE context
RFSP Index | This part defines the RFSP index |  |  | 
RFSP Index | Defines the RFSP Index that applies for a UE | Conditional (NOTE 2) | Yes | UE context
SMF selection management | This part defines the SMF selection management instructions |  |  | 
DNN replacement of unsupported DNNs | Defines if a UE requested unsupported DNN is requested for replacement by PCF | Conditional (NOTE 6) | Yes | UE context
List of S-NSSAIs | Defines the list of S-NSSAIs containing DNN candidates for replacement by PCF | Conditional (NOTE 6) (NOTE 7) | Yes | UE context
Per S-NSSAI: List of DNNs | Defines UE requested DNN candidates for replacement by PCF | Conditional (NOTE 6) | Yes | UE context
NOTE 1: If service area restrictions is enabled. NOTE 2: If RFSP index is enabled. NOTE 3: Either the list of allowed TAIs or the list of non-allowed TAIs are provided by the PCF. NOTE 4: Both the maximum number of allowed TAIs and the list of allowed TAIs may be sent by PCF. NOTE 5: If UE-AMBR is enabled. NOTE 6: If SMF selection management by PCF is enabled. NOTE 7: The List of S-NSSAIs contains S-NSSAIs, valid in the serving network, of the Allowed NSSAI. |  |  |  | 
23.503 Table 6.5-1: Access and mobility related policy control information
The RFSP Index defines the RFSP Index for radio resource management functionality.
This index points to connected and idle mode policies in the RAN.
However this is based on Allowed NSSAI + Subscribed RFSP and in general cannot be also consider, for Idle mode camping policies, the set of slices the UE could potentially use (the Configured S-NSSAIs).

## Slide 5: Why is the current RFSP Index sent to RAN not sufficient?
The RAN can decide UE-specific Idle mode camping policies based on the pair (Allowed NSSAI, RFSP Index)
However, RFSP Index = f(RFSP Index subscribed , Allowed NSSAI)
So, the RFSP-Index is conditioned to optimally serve the Allowed NSSAI based on the above. The RAN has no information on what slices the UE could potentially use (the Configured NSSAI) nor an RFSP Index based on the Configured NSSAI.
For us, the RAN should be optionally able to receive information to provide the UE with Camping policies that can also take into account the slices the UE can potentially use. For example, camping policies could favour cells that support the whole Configured NSSAI (i.e. not just the Allowed NSSAI).
The RFSP Index as defined today cannot convey the same benefit as otherwise we should have that the RFSP Index is related to the Configured NSSAI and not the Allowed NSSAI.
  That would mean that, irrespective of the Allowed NSSAI provided to the PCF, the PCF outputs the same RFSP Index that is related to the configured NSSAI, which also means that the Allowed NSSAI is not a meaningful parameter to be sent to the PCF to derive the RFSP Index.
If however for some values of Allowed NSSAI a different RFSP Index exists and in particular for some value of the Allowed NSSAI we have
    f(RFSP Index subscribed , Allowed NSSAI) != f(RFSP Index subscribed , Configured NSSAI)
then there is benefit for the RAN to consider the additional information as the RAN may decide it is better to let the UE camp on the bands of the Configured NSSAI than a more specific band for the Allowed NSSAI only (taking into account many factors including RAN status, cells neighbouring with the current cell, and other policies the RAN implements which cannot be exported to the CN).
It has to be decided whether the RFSP Index and camping policies are the same whichever the Allowed NSSAI, for a Given Configured NSSAI for a UE (in which case the Allowed NSSAI has no value as input to the PCF for RFSP Index decision), or whether RFSP Index and camping policies can be different for the Allowed NSSAI and Configured NSSAI for a UE. If they can be different, it is proposed it is beneficial to provide the Configured NSSAI and related RFSP index to the RAN as ADDITIONAL information for RRM

## Slide 6: Why is it beneficial to send configured NSSAI also for UE impacting solutions RAN2 is discussing?
The RAN can provide the UE with slice specific Camping policies/priorities in RRC connection release.
By knowing the Configured NSSAI, the RAN can provide all the information the UE needs to perform any reselection within the bands set valid for Configured Slices
  there is no use to provide the UE with all the information on all bands available, and it too is restrictive to just provide the Allowed NSSAI bands as then the UE would not be able to camp on the bands of Intended slices and so the result is that we have like for pre-Rel-17 UEs the same need to use Target NSSAI (so what is the benefit of impacting the UE?)
It is beneficial to provide the Configured NSSAI and its related RFSP Index to the RAN also for rel-17 UE impacting solutions

## Slide 7: Further background
TR 23.700-40 concluded the Configured, target NSSAAI approaches should both be considered in normative phase. These are NOT alternative with one another.
The Configured NSSAI provision to RAN was controversial as some claimed this was impacting negatively RAN
In S2-2105158, SA2 asked RAN2 and RAN3 whether it is harmful to provide the Configured NSSAI to the RAN.
In S2-2107011, RAN2 responded “RAN2 has concluded that this mechanism has no impact on RAN2 specifications.”
In S2-2105377, RAN3 responded that “there is little specification impact to signal the Configured NSSAI IE over the NG interface from RAN3 point of view.” And that there is “no consensus in RAN3 on the negative impact and the benefits of adding the Configured NSSAI.”