## Slide 1: New identifier for broadcast in SIBs
Background:
  SA2 received an LS from RAN2 requesting to introduce a new identifier for reducing the volume broadcasted in SIB (to be used instead of TMGIs). SA2 agreed a reply LS in S2-2108175 announcing the intention to introduce such an identifier:
  SA2 agrees to introduce an additional MBS identifier for reducing the volume broadcasted in SIB. The identifier can be associated with several TMGIs to avoid that those TMGIs need to be broadcasted in the System Information.SA2 did not yet conclude whether this additional identifier will denote service areas. SA2 intends to agree related CRs that detail the concept and related procedures in the next meeting. The additional MBS identifier can be used in SIB and the service announcement for Broadcast.
This paper analyses this issue and makes some proposals.
A related CR is in S2-2108965

## Slide 2: New identifier for broadcast in SIBs
Observations:
In LTE, the static SAIs never worked well for the small and dynamic service areas encountered for public safety; for that use case Cell IDs to describe service areas were subsequently added and used instead. The UE sends the cell IDs where it resides to the AF and the AF decides based on the number of UEs in the cell whether to establish a broadcast session. The MB2 interface in TS 29.468 uses Service area ID(s) or Cell ID(s) to identify a service area.
The current encoding agreed for service areas in TS 23.247 is based on tracking area IDs and Cell IDs. Advantages:
  Routing of requests to AMFs for broadcast can currently be based on TAIs and thus does not require related additions in the NRF and new administered structures in the network. (I assume the agreed stage 3 CT4 solution to structure cell lists according to the TAIs the cells belong to, see C4-215085).
  Thus no new administered topology needs to be introduced in the network
  The encoding is entirely flexible and does not require any prior knowledge of service areas for future servicesd
  Location based services and local services towards non-supporting RAN nodes can be supported (using existing event reporting capabilities based on TAIs and Cell IDs)

## Slide 3: New identifier for broadcast in SIBs
Observations (continued):
The identifier desired by RAN2 is for frequency selection and aims to group TMGIs to reduce the size of signaling messages in SIBs
  However the related message size would by 3000 bytes and could thus allow to accommodate quite a number of TMGIs
  The relationship with areas primarily comes from the fact that broadcast sessions denoted by the TMGIs have service areas.
  It would be straight-forward to combine services with the entire PLMN or the same large region as service area, but for services with smaller service areas the combination becomes increasingly complicated
Static configured identifiers in RAN will hardly be able to reflect all details of a broadcast session:
  There is a RAN3 agreement to assign such static identifiers via OAM
  At the moment only RAN nodes in the broadcast service area are aware of a broadcast session and exchange of dynamic information about broadcast sessions between RAN nodes for inclusions in the SIBs or neighboring cells is still controversial in RAN.
  Static configured identifiers can hardly reflect:
    If a broadcast session still exists and whether it is active or inactive.
    The exact service area of a broadcast session, in particular for small and dynamic service areas as encountered for public safety
  In LTE frequency selection based on such identifiers was still deemed acceptable, although there was a risk of changing to a frequency even if the desired broadcast service was not available in that cell

## Slide 4: New identifier for broadcast in SIBs
Proposals:
Maintain existing encoding of service area and possibility to identify service areas via Cell IDs
Introduce a new identifier for broadcast Frequency selection (e.g. BFSID):
  BFSIDs are not used to encode service areas and for request routing
  BFSIDs are assigned to RAN nodes and made known to the MB-SMF or NEF via OAM
  BFSIDs can be selected by MB-SMF, NEF, or AF(assuming that the AF has related knowledge via business agreements)
    One BFSID can be assigned to several TMGIs
    One TMGI can be assigned to several BFSIDs
    => Depending on operator policy, BFSIDs could be used similar to 4G SIDs, or simply to group TMGIs, and also allow for several frequencies for different broadcast services
  The BFSIDs are communicated in the service announcement towards the UE
  BFSIDs are signaled towards the RAN at broadcast session establishment
    The RAN selects a BFSID out of the assigned ones and uses it in the SIB
    This allows to guide frequency selection dependent on the service
For discussion, to enable a more accurate representation of available services in a cell for frequency selection:
  Optional to assign a BFSID to a TMGI
  If no BFSID is provided in service announcement and session establishment, the TMGI is used in SIBs