## Slide 1: NSAC: resolution of open issues NOKIA

## Slide 2: Configuration of S-NSSAIs subject to NSAC vs subscription data
While NSAC is a property per S-NSSAI and not per UE, we have examples of features that apply per S-NSSAI or even DNN or (S-NSSAI, DNN) that are subject to subscription information
The benefits are clear:
  avoid global configuration of AMFs/NSSFs
  Fast commissioning and decommissioning
    Change based on update of subscription data
Slice Selection Subscription data (data needed for | Subscribed S-NSSAIs | The Network Slices that the UE subscribes to. In roaming case, it indicates the subscribed network slices applicable to the serving PLMN (NOTE 11).
Slice Selection as described in clause 4.2.2.2.3 and | Default S-NSSAIs | The Subscribed S-NSSAIs marked as default S-NSSAI. In the roaming case, only those applicable to the Serving PLMN (NOTE 12).
in clause 4.11.0a.5) | S-NSSAIs subject to Network Slice-Specific Authentication and Authorization | The Subscribed S-NSSAIs marked as subject to NSSAA.
 | Network Slice Simultaneous Registration Group (NSSRG) Information | Optionally, for each S-NSSAI in the Subscribed S-NSSAIs, the one or more value of Network Slice Simultaneous Registration Group(s) (NOTE 11) associated with the S-NSSAI.
Table 5.2.3.3.1-1: UE Subscription data types
SMF Selection | SUPI | Key
Subscription data (data needed for SMF | SMF Selection Subscription data contains one or more S-NSSAI level subscription data: | 
Selection as described | S-NSSAI | Indicates the value of the S-NSSAI.
in clause 6.3.2 of | Subscribed DNN list | List of the subscribed DNNs for the UE (NOTE 1).
TS 23.501 [2]) | Default DNN | The default DNN if the UE does not provide a DNN (NOTE 2).
 | DNN(s) subject to aerial services | List of DNNs that are used for aerial services (e.g. UAS operations or C2, etc.) as described in TS 23.256 [80]. (see NOTE 13).
 | LBO Roaming Information | Indicates whether LBO roaming is allowed per DNN, or per (S-NSSAI, subscribed DNN).
 | Interworking with EPS indication list | Indicates whether EPS interworking is supported per (S-NSSAI, subscribed DNN).
 | Same SMF for Multiple PDU Sessions to the same DNN and S-NSSAI | Indication whether the same SMF for multiple PDU Sessions to the same DNN and S-NSSAI is required.
 | Invoke NEF indication | When present, indicates, per S-NSSAI and per DNN, that NEF based infrequent small data transfer shall be used for the PDU Session (see NOTE 8).
 | SMF information for static IP address/prefix | When static IP address/prefix is used, this may be used to indicate the associated SMF information per (S-NSSAI, DNN).
Having NSAC requirements for S-NSSAIs part of subscription information is a necessary condition for ease of deployment: proposed way forward is to make NSAC and EPS Counting requirement part of subscription data.

## Slide 3: EPS Counting support
Support of EPS counting is required by GSMA and is based on the number of PDN sessions in EPS and number of UEs with at least one PDN connection in EPS
  Benefits include
  Uniform constraints irrespective of the access technology/system
  Ability to ensure continuity of service in the face of Intersystem mobility.
Problem: do we still benefit from UE counting triggered by AMF in slices for which EPS counting is active?
  It seems to create non uniform experience and also the potential for dropped sessions in 5GS when UEs without sessions in 5GS cause UEs with sessions to not be able to use the 5GS
  It causes the need to have separate counting interactions (per UE and per PDU/PDN session) at the SMF+PGW-c.
    This in turn causes the need of additional signalling to keep coherent counters when the result of UE NSAC and PDU sessions NSAC are not aligned (see NEC CRs at last meeting)
Having both SMF+PGW-c and AMF engaged in Counting of UEs is not productive and actually severely complicates the system while bringing mostly downsides: Proposal: AMF-triggered counting not needed and the SMF+PGWc should only update the #of PDU sessions/PDN connections towards the NSACF per UE-ID and then the same NSACF perform both UE and PDU sessions/PDN connections NSAC

## Slide 4: Home-based control in roaming
This is needed for two reasons:
A Slice is allowed to have a mix of LBO and non LBO sessions, so this is the only way to make it possible to enforce one quota for PDU sessions per slice.
A slice can be used in roaming and non roaming at the same time, so this is the only way for the HPLMN to be able to report instantaneously to its customer the number of UEs per Slice in which PLMN, and also to enforce a single quota of UEs in the slice (also, GSMA does not define a quota per VPLMN as part of NG.116, so the scenario of single global quota needs support).
Having Home control of quota enforcement is necessary condition to meet basic requirements: proposed way forward is to make it possible for V-NSACF and H-NSACF to interact (V-NSACF proxying to H-NSACF)

## Slide 5: Coexistence of home control and Service area
The NSACF for a service area may be simply proxy for centralized decision in a central NSACF
This can both work in roaming and non roaming cases
Having a proxying mechanism also permits easy handling of different NSACFs per service area and allows the possibility to have a consistently updated centralized counter. Proposal: proxying allows resolving the issue of service continuity also inside a PLMN with Service Areas concept by having a single quota across SAs, if so desired.