## Slide 1: Discussion about Horizontal Federated Learning
vivo

## Slide 2: Background (clients selection)
The clients selection step in Horizontal Federated Learning has three methods.
  Random select:
    Consider each potential device if it meets the requirements （like enough required data).
    From those clients, the server randomly select.
  Iteration efficiency first:
    Considering data size, computing power, model difference and other factors, the server will choose the clients those can help the models to converge efficiently.
  Experience based:
    Based on the history of clients selections, the server will learn a policy and use this policy to choose clients.

## Slide 3: Background (large files)
In horizontal FL, the interaction and the communication between a server and clients may be a high cost in learning stage.
( first step is exchanging the Secret key and some privacy operations.)
The servers will send learning configurations, model files and other information to clients.
  Most of famous and developed models are large and the size are more than 500MB.
In practice, a TensorFlow model is 150MB and about 9MB is the weights and parameters file which could be used to transport for updating models in federated learning. (about 6% of a model is data file)
 | Complexity (OPs) | Ratio of capacity of the typical chipset in 1 second
Inception V2 | 4.1G | 2.7e-4
Inception V3 | 12G | 8.0e-4
CaffeNet | 724M | 4.8e-5
GoogleNet | 2G | 1.3e-4
MobileNet | 1.15G | 7.7e-5
AI network for DMRS in the slides | 2.9M | 1.9e-7 (1.9e-4 in 1ms)
AI network for CSI feedback in the slides | 8.9M | 5.9e-7 (5.9e-4 in 1ms)
AI network for beam management in the slides | 544K | 3.7e-8 (3.7e-5 in 1ms)
AI for channel prediction in the slides | 7.3M | 4.9e-7 (4.9e-4 in 1ms)

## Slide 4: Background (large files and multi times interactions)
Another example is that a very small network with architecture like “FC + RELU + FC + Softmax” with 512 inputs, the communication cost is about 67 Kb.
On the other hands, the TensorFlow Lite which is optimized for mobile and IoT devices, one file may about 1MB. (which may lead to a low Accuracy,)
However, in order to converge, about 5000-10000 rounds of training are needed. Thus, the communication cost is not a low level.

## Slide 5: Observation
In summary, there are large files and multi times interactions in the FL process, it will lead to heavy data traffic if FL interaction data is transferred between server and client(s) via 5GS.
As a consequence, the clients selection and data transmission in FL training should be more careful in 5G. It is necessary to ensure that the training process of FL not lead network performance degrading and traffic/fee for clients increasing substantially.

## Slide 6: Proposal
It is proposed to study how to support Horizontal Federated Learning by 5GS, including:
  1) How to select members for FL to avoid degrading of network performance and service experience for clients .
  2) How to transmit FL interaction data to avoid degrading of network performance and service experience for clients.

## Slide 7: Thank you