## Slide 1: Discussion on ML model Sharing for different vendors
vivo

## Slide 2: Background
Current R17 NWDAF supports AI/ML model sharing in single vendor. (eNA_ph2)
R18 SA2 starts to do research about AI/ML model sharing for different vendors. (eNA_ph3)
The current R17 NWDAF can be decomposed into NWDAF Training (MTLF) and NWDAF Inference (AnLF), and has defined AI/ML model interaction between them.
However，R17 MTLF and AnLF were restrict to one single vendor, didn’t define whether and how to share the ML models between different.
In R18 FS_eNA_Ph3, there is a WT# 3.2 proposed to study ML model sharing in different vendors

## Slide 3: Difference among ML model frameworks leads to difficult of model sharing
ML model can be trained and inferred based on some specific AI framework (e.g. TensorFlow, Pytorch, Caffe… ), but it cannot be understood and used by other AI frameworks.
Because the properties of each AI framework are different, including different:
  Network topology
  Execution flow
  Data format
  Supporting language
  Designing motivation
  Operating system
  …
Training
ML model
xxx.meta for model architecture
xxx.data for weights parameter
TensorFlow
Caffe
Loading Errors!!!
Inferring
ML model
Saving model

## Slide 4: Potential methods to sharing ML model----Interact via a convertor
The ML model architecture and weights data can be transformed into new Framework via an additional convertor module.
For each combination of two AI frameworks, at least one related convertor (e.g.TensorFlow->Caffe) needs to be developed.
Training
ML model
TensorFlow
Caffe
Convertor for TensorFlow
Developed by Caffe
Saving model
xxx.caffemodel
Inferring
ML model
xxx.meta for model architecture
xxx.data for weights parameter

## Slide 5: Potential methods to sharing ML model----Interact via a 3rd party format
For every AI framework, only one convertor needs to be developed, i.e., loading and saving.
The 3rd data format e.g. ONNX(Open Neuro Network Exchange) is used for data interaction.
The 3rd data format can be replaced by any other construct for specific scenario (even a New data structure designed for 3GPP)
Training
ML model
TensorFlow
Caffe
ONNX
Inferring
ML model
Loading model from an ONNX file
ONNX
Saving model to an ONNX file

## Slide 6: ML Model Sharing for different vendors in R18
  observation:
  The current R17 NWDAF supports AI/ML model sharing in single vendor, which has limitation since the models cannot be shared between NWDAFs provided by different vendors. It is necessary to study how to support model sharing for different vendors.
  Some potential methods have been identified can be used to share ML model in different AI frameworks , such as “Interact with a convertor” and “a 3rd party data format”. And there will be other ones may be found.
  Proposal: Add a KI to the new TR for the FS_eNA_Ph3, to study whether and how to enhance trained ML Model sharing for different vendors, including:
  Study whether and how to define ML model in standard?
  Study feasible solutions to share ML models in different vendors? E.g. 3rd party data format , convertor, 3GPP new defined data format …

## Slide 7: Thank you