## Slide 1: FS_AMP Status Report
Zhuoyi Chen
China Telecom (Rapporteur)

## Slide 2: FS_AMP status after SA2#149E (1/2)
General
  TR 23.700-89 v0.1.0 is available.
  Total TUs requested for Study Phase is 1.5 TUs, and 1 TU is remaining
  TR skeleton, scope, architecture assumptions, one key issue and two new solutions are documented.
Key Issue #1: RFSP Index consistency when UE moves from 5GC to EPC
  2 P-CRs are agreed as new solutions
    One new Solution#1 was added to propose to defer the AM policy association termination when UE move from 5GC to EPC to allowed further RFSP Index update from PCF to AMF and the AMF uses N26 interface to deliver the new RFSP Index to MME.
    One new Solution#2 was added to propose AMF provides Authorized RFSP Index to EPC via UDM/HSS. When UE moves from 5GC to EPC, the HSS provides the authorized RFSP value to MME.
  Next Steps: Resolve ENs in solution(s), complete existing solutions, and capture new solution(s)
  RAN impacts and dependencies:
  No RAN impacts or dependencies are identified
WI Code | Work Item Title | WP | Target Date | WID#
FS_AMP | Study on 5G AM Policy | 0% > 35% | Sept, 22 | SP-211642

## Slide 3: FS_AMP status after SA2#149E (2/2)
Contentious Issue:
  None
Focus for the Next Meeting (SA2#150E):
  The last meeting for any new solutions for the only Key Issue#1
  Complete the existing solutions
Overall Plan:
  SA2#149-E, 0.5 TU assigned, TR Skeleton, TR Scope, Architectural Assumption, Key Issues, allow solutions.
  SA2#150-E, 0.5 TU assigned, no new Key Issue could be allowed and the last e-meeting for new solution(s).
  SA2#151-E, no TU assigned.
  SA2#152-E, 0.5 TU assigned, for solution clean-up, evaluation and conclusion. Normative WID creation. Submit TR23.700-89 to SA#97E.
Risks:
  None

## Slide 4: FS_AMP status at SA#95E
General
  TR skeleton , scope, Architecture Assumptions are agreed
  1 KI agreed
  2 Solutions agreed
  RAN impacts and dependencies
  No RAN impacts or dependencies are identified
Next steps
  SA2#150E (0.5TU): Complete existing solutions and capture new solution(s) (last chance for new solution)
WI Code | Work Item Title | WP | Target Date | WID#
FS_AMP | Study on 5G AM Policy | 0% > 35% | Sept, 22 | SP-211642