## Slide 1: Proposal on slice priority and slice group
China Mobile
SA WG2 Meeting #150e
April 6 – 12, 2022; Elbonia
S2-2202676

## Slide 2
Background
  RAN2 defines Slice list and priority information for cell reselection in Rel-17 and send LS to SA2 to complete the E2E solution(S2-2107039).
  The latest LS sent from RAN2(R2-2203807) indicate:
    RAN2 understands whether per TA or per PLMN granularity has no major RAN2 impacts. However, RAN2 assumes (based on majority views in RAN2) that the mapping of slice to the slice groups for cell reselection is per TA.
    RAN2 also assumes that the NAS layer in the UE is able to provide slice group priorities to AS layer in the UE.
    RAN2 has achieved the following agreements:
      A slice is not associated with multiple slice groups for the same purpose within a slice to slice group mapping “granularity”. A slice can be associated at most with one slice group for RACH and with one slice group for reselection, within the same granularity.
      Both for RACH and for cell reselection, the UE NAS needs to provide the slice information to the UE AS. The UE AS is aware of the slice group ID (s) based on such slice information provided by the UE NAS.
  The discussion status in SA#95 emeeting:
    SA2 is expected to get some agreement in April meeting, which can help the work in RAN2/RAN3 and CT.
  The discussion status in RAN#95 emeeting:
    The approved alternative: The CR package for RAN slicing and Common RACH partitioning are approved in RAN#95e and can be updated according to SA2 situation after their April meeting. This is conditioned on that network control for slice based cell reselection is ensured.
    Another suggestion part from RAN discussion is :Network can use NAS signaling to provide slice group priorities to UE, which then uses those acoordin g to slice-specific reselection procedures defined in RRC and 38.304 specifications

## Slide 3: Some analysis for the slice priority
Rel17 slice aware cell reselection frequency priority handling (agreed CR for TS 38.304 in RP-220490)
  the UE shall derive frequency priority list by using: slice group priorities provided by NAS, slice specific frequency priority per slice group and legacy frequency priority.
  Frequencies that support at least one prioritized slice group received from NAS have higher re-selection priority than frequencies that support no prioritized slice groups.
  Frequencies that support at least one slice group are prioritized in the order of the NAS-provided priority for the highest prioritised slice group of the frequency.
How UE NAS layer is aware of slice group priority?
  Option 1: Left to UE NAS layer implementation
    Pros: Simple in specification. UE may have the knowledge of what slice the subscriber is in favor.
    Cons: UE behavior is unpredictable. Network side has no idea which slice is prioritized by the UE. And as consequence, network can not predict which frequency will be taken as the highest priority by the UE.
  Option 2: AMF sends slice group priority through NAS signaling to UE
    Pros: UE’s behavior of frequency priority handling is predictable by the network side. AMF can derive the slice priority based on the subscription info from UDM.
    Cons: Network decision may not be aligned with the subscriber behavior.
From operator’s point of view, it would be more important to guarantee the UE behavior of frequency priority handling is predictable, so we would prefer Option 2.

## Slide 4: Some analysis for the slice group
In the past several emeetings, there are two sets of solutions and one is for per TA level, and another is for per PLMN.
For per TA level, these solutions can provide flexibility for operators to configure the slice group information in RAN.
For PLMN level, less signaling from 5GC to UE with updating the slice group information.
Both solutions can solve the slice group requirement,and both solutions can work anyway.
We propose to use per TA level solutions(this part maybe updated based on the upload CRs), which can make the slice group configuration more flexible which leads to high possibility to be used in real network.

## Slide 5: Proposal for working agreement
The following aspects are expected to be agreed as the working agreement.
Network slice priority is realized with supporting 5GC sending NAS signaling to UE;
Network slice group granularity is realized by TA level;