## Slide 1
Discussion: validating MEC4AUTO Resource Sharing Scenarios 3A and 3B
18 Feb 2022

## Slide 2: Introduction
MEC4AUTO TR2 proposed three main scenarios of MEC resource sharing (inter-MNO):
  Scenario 1 - Both MNO A and MNO B have MEC platform and MEC App X
  Scenario 2 - Both MNO A and MNO B have MEC platform, but MEC App X is available only in MNO A
  Scenario 3 - Only MNO A has MEC platform and MEC App X is available only in MNO A
    Connectivity can be realized in two different options (see next slides) leading to Scenario 3A and 3B
General assumptions:
  Client application X, running in a vehicle, needs to connect to MEC App X running in a MEC platform.
  The MEC platform can belong to either a 3GPP Mobile Network Operator (MNO) or a 3rd party.
  All required business agreements are in place between the involved parties in order to allow the UE/vehicle to access the requested MEC apps located in the related MEC platform.
  Following slides assume that MEC platform is deployed in a 5G network but basic principles shown are also valid in case of 4G Evolved Packet Core (EPC).

## Slide 3: Scenario 1: Both MNO A and MNO B have MEC platform and MEC App Y / multiple OEM vehicles use case
RAN
“Local” UPF
MEC platform (AF)
Local access to DN
N3
“Central” UPF
DN
RAN
“Local” UPF
N3
App Y
“Central” UPF
DN
Operator B
Operator A
N6
Local access to DN
GW
GW
MEC App Y
N6
App Y
MEC platform (AF)
MEC App Y
Legend
“control” / edge service plane
data plane
Controlled IP Network
V2X Information Service
Other MEC services
V2X Information Service
Other MEC services
Notes: Each client app communicates with the local server app. Moreover, the server apps communicate with each other.

## Slide 4: Scenario 2: Both MNO A and MNO B have MEC platform, but MEC App X is available only in MNO A
Legend
“control” / edge service plane
data plane
RAN
“Local” UPF
MEC platform (AF)
Local access to DN
N3
“Central” UPF
DN
RAN
“Local” UPF
N3
App Y
“Central” UPF
DN
Operator B (e.g., three)
Operator A (e.g., Telia)
N6
Local access to DN
GW
MEC App Y
N6
GW
MEC platform (AF)
Controlled IP Network
V2X Information Service
Other MEC services
V2X Information Service
Other MEC services
App Y
Notes: Examples of MEC services: Location service, Radio Network Information Service (RNIS), V2X Information Service (VIS).
MEC App X: for example, ee Through application server, ToD application server.
NOTE: The MEC platform in MNO A and the MEC platform in MNO B are synchronized with regards to which remote services they provide.
“Long blue line”: MEC App X in MNO A consumes remotely MEC services in MNO B (although not always optimal, from a delay perspective)
GW is a BGW and possibly also other GWs, such as NAT GW

## Slide 5: Scenario 3A: Only MNO A has MEC platform and MEC App Y is available only in MNO A, multiple OEM vehicles use case
Legend
“control” / edge service plane
data plane
RAN
“Local” UPF
MEC platform (AF)
MEC App Y
Local access to DN
N3
“Central” UPF
DN
RAN
“Local” UPF
N3
“Central” UPF
DN
N9
Operator B (e.g., 3)
Operator A (e.g., Telia)
5GS home routed roaming
N6
Local access to DN
N6
App Y
App Y
V2X Information Service
Other MEC services
Real-world problem
Not a corner case
Has enough commercial interest

## Slide 6: Scenario 3B: Only MNO A has MEC platform and MEC App Y is available only in MNO A, multiple OEM vehicles use case
Legend
“control” / edge service plane
data plane
RAN
“Local” UPF
MEC platform (AF)
Local access to DN
N3
“Central” UPF
DN
RAN
“Local” UPF
N3
App Y
“Central” UPF
DN
Operator B
Operator A
N6
Local access to DN
GW
GW
MEC App Y
N6
App Y
Controlled IP Network
V2X Information Service
Other MEC services

## Slide 7: Considerations on Scenarios 3A and 3B
Scenarios 3A and 3B enable an App Y running in a UE to connect to a MEC App Y deployed in the DN or a co-located PLMN while using RAN of home PLMN
  NOTE - This is different from roaming because in roaming case the UE uses the RAN of the visited PLMN
  NOTE – in scenario 3B PSA UPF (the UPF that terminates the PDU Session towards the DN) is in the home PLMN, in scenario 3A PSA UPF is in the co-located PLMN and there is an intermediate UPF located within HPLMN
  3GPP Rel-17 does not support Scenarios 3A and 3B because of some identified gaps:
    3A&3B: Since the DNAI is a PLMN specific string
      Missing procedure for UPF to register to NRF according to DNAI of a co-located PLMN [cl. 6.1.6.2.13 of TS 29.510]
      Missing procedure for SMF to select a UPF based on a DNAI of a co-located PLMN [cl. 6.3.3.3 of TS 23.501 and 6.6.2.15 of TS 29.510]
      NOTE – this could be solved if there is a transparency in terms of DNAI support between home and co-located PLMNs
    3A:
      Missing procedure for home SMF to select a PSA UPF in the co-located operator based on target DNAI while an intermediate UPF is selected in home PLMN [cl. 6.3.3.3 of TS 23.501 and 6.6.2.15 of TS 29.510]
      Missing procedure – during PDU Session establishment - to provide UE sufficient information for EAS selection (via EASDF) in co-located PLMN [cl. 6.2 of TS 23.748]
      Needed configuration – e.g. per TA or per cell – which co-located PLMN and which PSA UPF in each co-located PLMN needs to be used for traffic routing, depending on the MEC application traffic [5.6.1 of TS 23.501, 4.3.6 of TS 23.502, 6.3.1 of TS 23.503]
If there is interest in Scenarios 3A and 3B, 5GAA should iaise with 3GPP SA2 to introduce support in future 3GPP releases

## Slide 8
Thank you!