## Slide 1: FS_AMP Status Report
Zhuoyi Chen
China Telecom (Rapporteur)

## Slide 2: FS_AMP status after SA2#150E (1/3)
General
  TR 23.700-89 v0.2.0 is available.
  Total TUs requested for Study Phase is 1.5 TUs, and 0.5 TU is remaining
  Eight new solutions and one solution update are documented.
Key Issue #1: RFSP Index consistency when UE moves from 5GC to EPC
  8 P-CRs are agreed as new solutions
    3 new solutions are for N26 based scenario
      Solution #3 proposes PCF provides validity timer along with authorize RFSP Index to AMF, and AMF provides this information to target MME via N26 in handover procedure.
      Solution #6 proposes AM association and AMF registration to UDM should both be kept after UE moves from 5GC to EPC, to allowed further authorized RFSP Index from PCF and deliver to MME via N26, AMF may queries the HSS + UDM for the serving MME.
      Solution #10 propose the MME uses the RFSP Index in use from AMF via N26. When the configured duration is reached, the MME may remove the "5GC Authorized RFSP Index" from its context for the UE and start using the "subscribed RFSP Index" that was received from the HSS.
    4 new solutions are for without N26 interface scenario
      Solution #4 proposes PCF provides validity timer along with authorize RFSP Index to AMF, the AMF use ParameterProvision service to update this information to HSS+UDM. Target MME receive the validity timer and authorize RFSP index from HSS + UDM while UE attaches to MME.
      Solution #5 proposes PCF provides validity timer along with authorize RFSP Index to AMF. During the 5GS to EPS mobility, the AMF provides this information to HSS+UDM, and the MME receive the validity timer and authorize RFSP index from HSS + UDM.
WI Code | Work Item Title | WP | Target Date | WID#
FS_AMP | Study on 5G AM Policy | 0% > 80% | Sept, 22 | SP-211642

## Slide 3: FS_AMP status after SA2#150E (2/3)
Key Issue #1: RFSP Index consistency when UE moves from 5GC to EPC (Cont.)
      Solution #7 proposes AM association and AMF registration to UDM should both be kept after UE moves from 5GC to EPC, to allowed further authorized RFSP Index from PCF and deliver to HSS + UDM by AMF, and the serving MME receives the update from HSS + UDM.
      Solution #8 proposes if MME aware a UE is from 5GC and no available UE context as no N26 interface deploys, the MME locally set the RFSP index in use as 4G-prioritize and reselect the RFSP index in use after a locally set time period.
    1 new solution is for both N26 and without N26 interface scenarios
      Solution #9 proposes PCF provide authorized RFSP Index to HSS+UDM, and MME receive the authorized RFSP Index via S6a interface.
  1 P-CR is agreed as solution update.
    Remove EN in Solution#1, by adding new service to allow AMF to get notify of serving MME change from HSS + UDM.
Next Steps: Resolve ENs in solution(s), evaluate solutions and capture conclusion.
  RAN impacts and dependencies:
  No RAN impacts or dependencies are identified
WI Code | Work Item Title | WP | Target Date | WID#
FS_AMP | Study on 5G AM Policy | 0% > 80% | Sept, 22 | SP-211642

## Slide 4: FS_AMP status after SA2#150E (3/3)
Contentious Issue:
  None
Focus for the Next Meeting (SA2#151E):
  NO TU assigned. No paper will be handled.
Overall Plan:
  SA2#149-E, 0.5 TU assigned, TR Skeleton, TR Scope, Architectural Assumption, Key Issues, allow solutions.
  SA2#150-E, 0.5 TU assigned, no new Key Issue could be allowed and the last e-meeting for new solution(s).
  SA2#151-E, no TU assigned.
  SA2#152-E, 0.5 TU assigned, for solution clean-up, evaluation and conclusion. Normative WID creation. Submit TR23.700-89 to SA#97E.
Risks:
  Conclusion may not be reached at SA2#152-E due to unsolved Editor’s Note of some solutions.

## Slide 5: FS_AMP status at SA#96E
General
  TR skeleton , scope, Architecture Assumptions are agreed
  1 KI agreed
  10 Solutions agreed
  RAN impacts and dependencies
  No RAN impacts or dependencies are identified
Next steps
  SA2#152E (0.5 TU): for solution clean-up, evaluation and conclusion. Normative WID creation. TR23.700-89 ready to SA#97E for approval.
WI Code | Work Item Title | WP | Target Date | WID#
FS_AMP | Study on 5G AM Policy | 0% > 80% | Sept, 22 | SP-211642