## Slide 1: Discussion on PIN issues and corresponding proposals
Zhenhua Xie
vivo
S2-2209007

## Slide 2
Issue of architecture and proposal
Two architecture alternatives:
  AF based
    Enhance AF-NEF/PCF functionalities for providing PIN parameters
    PIN parameters for PIN management include membership information, PEGC-PINE association information, etc.
    PIN topology information are exposed to AF for PIN management
    PIN parameters for PIN communication configuration include traffic descriptions
  Non-AF based
    PIN management is done among PEGC, PEMC, and PINE
    PEGC initiates PDU Session Establishment/Modification procedure according to PEMC’s command for PIN communication configuration
Issue of “AF based”:
  AF is not a trust entity to user (although the operator can authenticate and authorize the AF)
  Complicated security requirement related to privacy concern: membership and topology concealment, authorization of PEGC manipulation by PEMC via AF, etc.
  More coordination with SA3, which may delay the study significantly
Issue of “non-AF based”:
  5G system resources for PIN is pre-configured, not managed dynamically

## Slide 3
Issue of architecture and proposal
Proposal:
  “non-AF based” is mandate
    User subscribes PIN service with GPSIs of PEMCs and PEGCs
    Pre-configuration is used for statically managing 5G system resources for PIN, i.e., PDU Sessions of PEGC(s) and PEMC(s)
  “AF based” is optional, only for provisioning parameters for dynamic 5G system resources management without privacy concern, i.e.,
    URSP generation information for PIN per PIN service subscription instead of per UE
    Number of PIN limited by PIN service subscription
    QoS authorization information per PIN (i.e., what kinds of QoS are allowed for a PIN)

## Slide 4
Issue of URSP and proposal
Traffic descriptor (TD) of URSP rule:
Issues:
  IP range of a PIN may be determined during/after PDU Session Establishment
  PIN session is not application related
  Domain/Non-IP/Connection are not suitable for PIN
Information name | Description | Note
Application descriptors | It consists of OSId and OSAppId(s). | The information is used to identify the Application(s) that is(are) running on the UE's OS. The OSId does not include an OS version number. The OSAppId does not include a version number for the application
IP descriptors | Destination IP 3 tuple(s) (IP address or IPv6 network prefix, port number, protocol ID of the protocol above IP). | A URSP rule cannot contain the combination of the Traffic descriptor components IP descriptors and Non-IP descriptors
Non-IP descriptors | Descriptor(s) for destination information of non-IP traffic | 
Domain descriptors | Destination FQDN(s) or a regular expression as a domain name matching criteria. | 
DNN | This is matched against the DNN information provided by the application. | 
Connection Capabilities | This is matched against the information provided by a UE application when it requests a network connection with certain capabilities. (NOTE 4) | The format and some values of Connection Capabilities, e.g. "ims", "mms", "internet", etc., are defined in TS 24.526 [19]. More than one connection capabilities value can be provided

## Slide 5
Issue of URSP and proposal
Alternative solutions:
  Alt#1: Extend TD of URSP for PIN traffic mapping, e.g., using “source descriptors” or “gateway descriptors”
    Pros:
      Is able to be used for gateway UE other than PIN feature, i.e., it is a solution with a common framework for matching by gateway UE
    Cons:
      PEMC does not know the extension so different URSP may be needed
      Different feature still need to specify different value type of the field, e.g., PIN ID for PIN feature and MAC address/device ID for 5WWC feature
      Application descriptors also is a kind of source, “source descriptors” may cause confusion
  Alt#2: Do not extend URSP, but provisioning mapping info with URSP, e.g., <PIN ID, DNN>, i.e., PIN UE policy consist of URSP and mapping info
    Pros:
      Using DNN for TD, network does not need to distinguish PEMC and PEGC for providing UE policy before PDU Session Establishment
      Different feature can use different mapping info without URSP enhancement
    Cons:
      Additional IE needs to be provisioned with URSP
Proposal:
  Alt#2 is suggested to be the way forward

## Slide 6
Issue of PDU Session number per PIN and proposal
Interim conclusion:
  A PEGC may establish a Single or multiple PDU Sessions used for PIN communication. One PEGC may serve more than one PIN and in this case, there is at least one PDU session per PIN
Issue:
  Not clear what is the purpose for a PIN to have more than one PDU Sessions per PEGC
  QoS differentiation is able to be done by QoS flows
  If one PIN at a PEGC has two PDU Sessions is allowed, it is same that divide the PIN into two, and one per PDU Session
Proposal:
  Only one PDU session per PIN per PEGC/PEMC

## Slide 7
Issue of non-3GPP QoS assistance information and proposal
Interim conclusions:
  5G QoS parameters (including QoS characteristics, GFBR/MFBR) may be sent to PEGC to assist the deriving of N3GPP QoS parameters
  5GC may take into account the delay budget between PINE and PEGC to guarantee the end to end delay for PINE traffic.
Issue:
  “5G_QOS_INFO” described in TS 24.502 is sent by N3IWF/TNGF to UE when initiating child SA creation, the Additional QoS Info in the 5G_QOS_INFO may include (table 9.3.1.1-2 of 24.502):
    QoS characteristics (resource type: GBR, Delayed critical GBR, non-GBR; priority level: 1-127; PDB; PER; AW; MDBV)
    Maximum Flow Bit Rate downlink (MFBR downlink);
    Maximum Flow Bit Rate uplink (MFBR uplink);
    Guaranteed Flow Bit Rate downlink (GFBR downlink);
    Guaranteed Flow Bit Rate uplink (GFBR uplink);
    Notification Control;
    Maximum Packet Loss Rate downlink; and
    Maximum Packet Loss Rate uplink.
  It is N3IWF/TNGF instead of 5GS that generates Additional QoS Info who takes into account the 5G QoS profile received via N2 instead of N1
  Non-3GPP delay budget is in the QoS characteristics of the “Additional QoS Info”
Proposal:
  5GC (i.e. PCF/SMF) may send the non-3GPP QoS assistance information that is same as described in table 9.3.1.1-2 of TS 24.502 to PEGC to assist the deriving of N3GPP QoS parameters
  Notification Control shall not be sent to the PEGC