## Slide 1: DP on the effectiveness of asynchronous redundant steering mode
Source: Alibaba

## Slide 2: Why multi-path transmission with different packet is need?
  Nowadays, live video broadcasting Service and online gaming become more and more popular. These kinds of applications need both low latency and how throughput because customer can not tolerate long delay when opening the video/game or watching the video or playing the online game.
  In order to meet the aforementioned requirement, multi-path transmission is needed because the additional path can be used to transmit different packets in order to ensure the throughput requirement of the applications. A single path transmission cannot guarantee the throughput even if it has low latency.

## Slide 3: Why MP out-of-order needs to be solved?
  In the case that two path transmit different packets, MP out-of-order delivery issue happens when the 2 path has big delay difference. The delay difference may happen due to the faster varying wireless environment.
  As shown in the left figure 1, during the multi-path transmission, the path 1 (e.g. non-3GPP path) is deteriorated because of fast changing wireless environment, causing serious MP out-of-order delivery issue on the UE side.
  As shown in the left figure 2, the UE suffers from serious video re-buffering because of the severe MP out-of-order issue. This results in serious QoE downgrade from UE side.
(1) Throughput for different paths
(2) UE buffer level when MP out-of-order delivery happens

## Slide 4
Effectiveness of A-RSM
  As shown in the above figure, A-RSM can provide sufficient re-transmitted packets in order to maintain sufficient cached bytes in the UE’s buffer so that the smoothness of the video play can be ensured.
(1) Buffer level with asynchronous redundant transmission