## Slide 1: AF deployed in VPLMN triggered EAS Re-discovery via interacting with VPLMN
EDGE_Ph2
KI#1/HR
Source: Huawei, HiSilicon

## Slide 2: Background
TR 23.700-48 v18.0.0
  NOTE 2: The baseline procedure for AF triggered EAS Re-discovery for an AF interacting with VPLMN will be determined in normative phase.
In Rel-17 EC procedures, AF needs to interact with 5GC in the following procedures:
  AF influence on traffic routing procedure to support
    N6 traffic routing requirement provisioning
    AF triggered EAS re-discovery
    AF triggered EAS IP replacement
    AF change during Edge relocation
    ……
  User plane management event exposure(e.g. exposure of DNAI change)
    UE mobility triggered Edge relocation
    AF change during Edge relocation
    …..
  EDI provisioning from AF
For HR-SBO case, if an AF can only interact with VPLMN, how to support the above procedures in VPLMN is not clear.
  Especially, AF influence on traffic routing procedure goes through PCF(see details in next page), while it was concluded that “no V-PCF in VPLMN”, thus how the AF can perform “AF influenced traffic routing” needs to be investigated.

## Slide 3: Existing AF influenced traffic routing procedure goes via PCF
TS 23.502 clause 4.3.6: Application Function influence on traffic routing
23.502 clause 4.3.6.2:
NOTE1: The 5GC functions used in this scenario are assumed to all belong to the same PLMN (HPLMN for non-roaming case or VPLMN in the case of a PDU Session in LBO mode).
NOTE2: Nnef_TrafficInfluence_Create or Nnef_TrafficInfluence_Update or Nnef_TrafficInfluence_Delete service operations invoked from an AF located in the HPLMN for local breakout and home routed roaming scenarios are not supported.
Figure 4.3.6.4-1: Handling an AF request targeting an individual UE address to the relevant PCF
Figure 4.3.6.2-1: Processing AF requests to influence traffic routing for Sessions not identified by an UE address
In the existing AF influence procedure, PCF is used to handle the AF request.
It is not clear how the AF deployed in VPLMN interacts with the VPLMN without V-PCF.

## Slide 4: Potential solutions to resolve AF interacts with VPLMN for HR-SBO
Alt#1: V-NEF interacts with V-SMF directly
  For this solution, the interaction between V-NEF and V-SMF needs to be standardized without V-PCF.
Alt #2: V-NEF interacts with V-SMF via HPLMN
  To support this solution, the interaction between V-NEF and H-NEF needs to be standardized.
  For edge relocation, the signalling path of AF request will introduce too long latency and may cause service interruption.
Alt #3: If a V-AF can only interact with VPLMN, AF influenced traffic routing procedure will not be supported.
  As a result, the following procedures will not be supported if a AF cannot access H-PLMN(e.g. a V-EHE without SLA with HPLMN)
    AF triggered Edge relocation
    N6 routing policy provisioning from AF triggered EAS re-discovery
    AF triggered EAS IP replacement
    ....
Any other Alternatives?
V-UPF
UE
V-SMF
AMF
H-UPF
H-SMF
RAN
H-PCF
UDM
AF
V-NEF
H-NEF
L-DN
L-PSA
This discussion paper intends to trigger discussion on common understanding on which Alt we should go forward.
Alt#1
Alt#2