## Slide 1: DetNet 3GPP SA2 offline discussion
Ericsson, 2022 November

## Slide 2: Outstanding issues
UE
RAN
UPF
SMF
AMF
PCF
TSCTSF
CPF: DetNet controller
DetNet network
5GS logical DetNet Node
DetNet end system
NW-TT
1. Support an optional NEF?
2. Should uplink routing information be reported to the DetNet controller?

## Slide 3: NEF Alt 1: protocol conversion
TSCTSF
CPF: DetNet controller
NEF
YANG over Netconf/Restconf
N85
Protocol conversion
Optional NEF converts between the IETF based protocol and 3GPP signalling. NEF talks IETF protocols to DetNet controller, 3GPP protocols to TSCTSF.
Conversion adds unnecessary complexity.
Complexity for NEF to parse YANG.
Different functionality split with/without NEF since no NEF deployment also needed. - Without NEF: TSCTSF parses YANG - With NEF: NEF parses YANG

## Slide 4: NEF Alt 2: transparent N85 container
TSCTSF
CPF: DetNet controller
NEF
YANG over Netconf/Restconf
YANG over container in N85
Optional NEF transparently relays YANG config between the IETF based protocol and 3GPP signalling. Lower complexity, but still impacts NEF.
No need for NEF to interpret YANG
No protocol conversion
Requires container in N85 to carry YANG
NEF to support Netconf/Restconf Note: in the TSN case, Netconf support is at the TSN AF, and NEF is not involved.

## Slide 5: NEF Alt 3: no NEF in this release
TSCTSF
CPF: DetNet controller
YANG over Netconf/Restconf
No NEF supported for DetNet in this release.
TSCTSF can perform firewalling, only accept signalling from known sources (independent of NEF).
TSCTSF can validate YANG configuration (independent of NEF).
Trust in the DetNet controller is ensured by operator business agreement with DetNet controller provider (if different from operator).
            Note: such business agreement is always needed since DetNet controller can influence QoS for all UEs in a given network, not just for a single UE as in the case of an AF.

## Slide 6: NEF: conclusion
Alt 1: protocol conversion has too high complexity impact – not justified
Alt 2: transparent N85 container, moderate complexity impact – less preferred alternative
Alt 3: no NEF in this release has no impact, business agreements ensure trust – preferred alternative

## Slide 7: Routing information: overview
In general (fixed) deterministic networks, DetNet controller may provide explicit flow routing to routers
DetNet controller may collect topology information
  Not DetNet specific function, general RFCs may be used for Routers to provide neighbour info.
No routing info from Routers to controller
CPF: DetNet controller
R
R
R
R
R
R
E
E
Explicit flow routing for DetNet

## Slide 8: Routing information: 5GS aspects, DL
Out of scope of study to influence routing in 5GS.
DL routing determined by Endhost behind the terminal – no need to influence DL routing by DetNet controller.
Possible to support multiple IP@ per PDU Session (i.e., framed routing)
5GS does not support generic IP router functionality DL, i.e., support of a single IP@ reachable over multiple PDU Sessions
No routing problem in DL.
CPF: DetNet controller
5GS
R
R
R
R
R
E1
E
E2
E3

## Slide 9: Routing information: 5GS aspects, UL
No issue if:
  Only one UL interface exists
  There is a single path only to an endhost
  Static UL routing configured if it is also known in the DetNet controller.
Should 3GPP define functions to provide static UL routing table towards the DetNet controller?
Note: alternative deployment option exists, see next slide.
CPF: DetNet controller
5GS
R
R
R
R
R
E1
E
E2
E3

## Slide 10: Deployoment option for UL handling
Model the N6 uplink router as a separate logical Router entity.
N6 routing is already today out of 3GPP scope, implementation specific.
DetNet controller may directly control N6 UL routing.
Signalling between DetNet controller and Router on N6 can be considered out of scope of 3GPP; setting explicit routes possible by controller.
No need for 5GS to provide UL routing information.
CPF: DetNet controller
5GS
R
R
R
R
R
E1
E
E2
E3
R
UL routing on N6, implementation specific (out of 3GPP scope)

## Slide 11: UL Routing information: conclusion
No need for 3GPP to define mechanisms to provide UL static routing information from UPF/NW-TT to DetNet controller.
  In many deployments, there is no need (single interface, single route to host)
  If the UL routing is static, it can easily be configured into the controller also
  Deployment option with direct interface between DetNet controller and N6 UL routing function if signalling is needed
  N6 UL routing is in general out of 3GPP scope, so we should avoid standardizing 3GPP functionality