## Slide 1: Edge Ph2 drafting
22/02/2023
Patrice Hédé, rapporteur

## Slide 2: Agenda
KI#1
  Source of VPLMN roaming offloading policy
  AF influence request path in VPLMN
  routing of UE DNS requests to vEASDF
  DNS request traffic routing between vEASDF and HPLMN DNS server

## Slide 3: VPLMN roaming offloading policy
(covered by "Technical issue 2" in 2771)
source can be UDM or PCF
  2814 (Samsung): hPCF → hSMF
  2685 (Huawei): hPCF → hSMF
  2831 (Nokia): UDM → hSMF
agreement: 1 solution
PCF preference: 4
UDM preference: 2
we will go for PCF source

## Slide 4: VPLMN roaming offloading policy
(covered by "Technical issue 2" in 2771)
content of VPLMN roaming offloading policies
  2685 (Huawei), 2832 (Nokia): FQDN range(s) and/or IP address range(s)
  2816 (Samsung): FQDN range(s) and/or IP address range(s), Authorized Session AMBR for Local part of DN
  2335 (Ericsson): FQDN range, IP range, AMBR for the local part of DN and charging policy
FQDN range(s) and/or IP address range(s)
Authorized Session AMBR for Local part of DN → double check if can be covered by existing parameter
charging policy → double check if already covered? FFS

## Slide 5: AF influence request path in VPLMN
  2519/2520 (Samsung): vAF → vNEF → vUDR ⇒ vSMF
  2691/2692 (Huawei), 2828/2829/2830 (Nokia): vAF → vNEF → vUDR ; vUDR ⇒ vNEF ⇒ vSMF
  → flow // ⇒ notification
  vAF → vNEF → vUDR ; vUDR ⇒ vNEF ⇒ vSMF

## Slide 6: routing of DNS requests to vEASDF
(covered by "Technical issue 1" in 2771)
2335(Ericsson): NAT at the PSA
2685(Huawei): via UL-CL/BP+PSA
not discussed in drafting

## Slide 7: DNS request traffic routing between vEASDF and HPLMN DNS server
(covered by "Technical issue 6" in 2771)
2399 (CMCC): UL/CL in VPLMN to change dest IP address from vEASDF to HPLMN DNS server
2827 (Nokia): DNS traffic injection with tunnels
issue includes keeping privacy of DNS requests
we will not attempt to resolve this in this meeting, this will be discussed further in CC before next meeting. may improve EN in the meantime.