## Slide 1: TR-369 (USP) on the 5G-RG
A quick guide for 3GPP writers looking to map to new BBF standards

## Slide 2: About TR-369 – The User Services Platform
USP is the successor to TR-069, though TR-069 is still being deployed.
The biggest features for your use case questions are:
  Multi-controller architecture
  Re-use of the TR-181 Device:2 data model

## Slide 3: The USP ecosystem
Internet
Broadband Network
USP Controller as ACS, or co-existence with TR-069
Third party MSP, vendor, or application provider
Mobile end-user with app on computing device
Local end-user with app on computing device
Data collector
Device and application capabilities managed and controlled with standard TR-181 data model, directly or by proxy
USP messages
USP messages or HTTP bulk data
USP messages
USP messages
USP messages
USP messages
Home automation gateway
Network setup and config
Network and security feature control
Software container management
Firmware and software upgrades
Diagnostic commands
Bulk data telemetry
Custom commands & events
IoT sensors and controls
TR-181/Device:2 Data Model Capabilities
USP Controllers and Agents have:
Persistent connections to reduce handshakes
Clear trust relationship establishment
Optional end-to-end application layer TLS session context
Role-based access control to service elements for privacy and security
Flexible transport that can be cloud independent or not
USP Agents

## Slide 4: Multi-controller architecture
Unlike TR-069, a 5G-RG using USP is not bound to a single ACS
Multiple “Controllers” can access and manipulate a USP Agent
Each Controller is bound by Role Based Access Control (RBAC) to only those objects and parameters (e.g. interfaces and functions) allowed by that Role.
Ergo, one Controller can handle some responsibilities while another handles other responsibilities.
Those Controllers can be operated by entirely different parties.

## Slide 5: Re-use of TR-181 Device:2 Data Model
USP uses the TR-181 Device:2 Data Model to describe device functions and perform operations
New 5G interface options have been added since Device:2.14
QoS objects and the ability to assign them to interfaces, hosts, and applications have existed for some time

## Slide 6
5G-RG with USP Agent
Operator Function with USP Controller
Operator Function with USP Controller
Example Use
RBAC to appropriate USP Agent functions
RBAC to appropriate USP Agent functions

## Slide 7: USP and TR-069 can operate together!
Another valid use case is to use TR-069 for traditional ACS functions while operating a USP Agent for other operator functions
Unified use of Device:2 data model allows for this