## Slide 1
SA2#156E
Discussion on how to provide traffic characteristics
vivo

## Slide 2: Editor’s note: The method used to provide the Periodicity information to SMF is FFS.
As introduced by rel17, the AF (not TSN AF) provides the parameters of traffic characteristics (i.e. periodicity, etc.) to the 5GS. When the AF is untrusted, the NEF forward those parameters to the TSCTSF to generate TSC Assistance Container. The PCF forwards the TSC Assistance Container received from the TSCTSF to the SMF.
When XRM is introduced, there used to be a proposal to reuse TSCAC for XRM. For this proposal, the following concerns have been received:
  Concern1：The AF has supported to provide parameters (i.e. periodicity, etc.) of traffic characteristics to 5G network. In theory, parameters of traffic characteristics are possible be provided to the PCF directly when the AF is trusted. Why the AF repeat to provide TSC Assistance Container.
  Concern2：The proposal makes both AF and TSCTSF generate TSCAC and work being repeated.
  Concern3：TSC Assistance Container literally is used for TSC scenario and is not sufficiently forward compatible to the non-TSC traffic. It can be foreseen more and more traffic characteristic information may be considered in the network and the traffic can be non-TSC, so the TSC Assistance Container is not sufficiently forward compatible.
Observation1: The issue is not as simple as “reusing TSCAC or not” only, but also about whether the same handling is needed for both TSC and XRM or not.

## Slide 3: Options
During the CC discussion, there are many options are proposed to be considered. In our view, they can be categorized as the following:
Category 1, Legacy for TSC in unchanged, different handling for TSC and XRM in AF, PCF and/or SMF.
Category 2: Same handling for TSC and XRM in AF/PCF/SMF with one container:
  AF provide one container, PCF forwards the received container to SMF.
  TSCTSF doesn’t generate container anymore but forwards the received container to the PCF
Category 3: Same handling for TSC and XR in AF/PCF/SMF with explicit parameters:
  AF provide parameters, PCF receives and forwards the parameters to SMF
  TSCTSF doesn’t generate container anymore but forwards the received parameters to the PCF.
Proposal1: In both catergory1 and 2, TSCAC or new container is under consideration. We should determine different handling or the same handling of TSC and XR firstly, the TSCAC or new container later.

## Slide 4: Catetory1:Legacy for TSC in unchanged, different handling for TSC and XR in AF, PCF and/or SMF
Option1.1 and Option 1.3: handling in AF, PCF and SMF are different
Option1.2: handling in AF is different, handling in PCF and SMF are same
Option1.4: different in AF, PCF, handling in SMF is same
Proposal2: Option1.4 should be excluded, since the motivation of PCF is transparent to the PCF, it is wired to let PCF to generate TSCAC based on parameter.
 | TSC (Legacy) | XR Option 1.1 | XR Option 1.2 | XR Option 1.3 | XR Option 1.4
AF -> | Parameter | New Container | TSCAC | Parameter | Parameter
NF->PCF | TSCAC | New Container | TSCAC | Parameter | Parameter
PCF-> SMF | TSCAC | New Container | TSCAC | Parameter | TSCAC

## Slide 5: Catetory2: Same handling for TSC and XR in AF/PCF/SMF with one container
AF provide one container, PCF forwards the received container to SMF.
TSCTSF doesn’t generate container anymore but forwards the received container to the PCF.
Traffic characteristics is a kind of objective information, the time sensitive traffic and non-time sensitive traffic might have different characteristics but some characteristics are common (e.g. periodicity). Same transfer handling of Traffic characteristics is good for future extension and avoid unnecessary of determinisation of TSC or non TSC.
 | TSC | XR
AF -> | Container | Container
NF-> TSCTSF | Container | Not related
NF-> PCF | Container | Container
PCF-> SMF | Container | Container
The Category2 unified container can be:
Option2.1 Rename TSCAC as a generic container or new container for both TSC and XR
Option2.2 Reuse TSCAC for both TSC and XRM

## Slide 6: Catetory3 Same handling for TSC and XR in AF/PCF/SMF with explicit parameters:
Option3.1 Same handling for TSC and XR in AF/PCF/SMF with explicit parameters:
  AF provide parameters, PCF receives and forwards the parameters to SMF
  TSCTSF doesn’t generate container anymore but forwards the received parameters to the PCF.
 | TSC | XR
AF -> | Parameter | Parameter
NF-> TSCTSF | Parameter | Not related
NF->PCF | Parameter | Parameter
PCF-> SMF | Parameter | Parameter

## Slide 7: Options proposed to be took into consideration
(Alt3)Category 1:
  Legacy for TSC in unchanged, different handling in XR at AF, PCF and/or SMF
  Option1.1.(S2-2304399)
Proposal3:
  If WF is category2, better to have a new name of TSCAC but is OK with TSCAC as well.
  If WF is category 1, favor new container as Option1.1.
Category 3 is not proposed since its doesn’t show extra benefit comparing to Category 2
(Alt1) Category 2:
  Option 2.1 Same handling for TSC and XR in AF/PCF/SMF with TSCAC (S2-2304397)
(Alt2) Category 2:
  Option 2.2 Same handling for TSC and XR in AF/PCF/SMF with TSCAC and rename TSCAC to a general name(S2-2304398)
 | TSC | XR
AF -> | TSCAC | TSCAC
NF-> TSCTSF | TSCAC | Not related
NF->PCF | TSCAC | TSCAC
PCF-> SMF | TSCAC | TSCAC
 | TSC (Legacy) | XR Option 1.1 | XR Option 1.2 | XR Option 1.3
AF -> | Parameter | New Container | TSCAC | Parameter
NF->PCF | TSCAC | New Container | TSCAC | Parameter
PCF-> SMF | TSCAC | New Container | TSCAC | Parameter

## Slide 8
Thank You!