## Slide 1
Discussion on two ambiguous aspects of event report allowed area
SA2#156e
vivo

## Slide 2
The conclusion of FS_eLCS_Ph3 KI#11 Enhance Triggered Location for UE power saving purpose:
  For key issue #11, it is concluded that solution#25 (Event Report in an Allowed Area) is used as the baseline for normative work with the two ambiguous aspects identified in clause 7.11 also being resolved in the normative phase.
Two ambiguous aspects are:
  whether a UE should occasionally send event reports when outside an allowed area to show an HGMLC and LCS Client that event reporting is still active in the UE.
  whether an allowed area can be used in an opposite sense where a UE only reports when outside a certain area (e.g. where a UE spends most time in the area but UE location is only needed when the UE is outside the area).
General

## Slide 3
Q1：Whether a UE should occasionally send event reports when outside an allowed area?
  Answer: No!
  For area type, if the target area is large than the allowed area, the UE will not report locations when it is inside the target area but outside the allowed area. The LCS client will never receive the ‘leave’ report from UE.
  For periodic location type, the LCS client may terminate the LCS session if considering the event report is not active in UE.
  For motion type, the UE will not report locations if the relative motion distance is outside the allowed area. The number of the report will be decreased and limited.
Observation 1: No reporting outside the allowed area saves the UE power but degrades the commercial location service experiences.
  Answer: Yes!
  The UE can report locations conditionally when it is outside the allowed area. In such a case, the LCS session will not be terminated caused by the event report inactivity in UE. The LCS client will collect location reports as much as possible with considering the UE power-saving purpose.
Observation 2: Reporting conditionally outside the allowed area can balance the demand between the UE power-saving purpose and commercial location service experiences.
Discussion

## Slide 4
Q2：Whether an allowed area can be used in an opposite sense?
  Answer: No!
  The allowed area can only be used in a positive sense that the UE only report locations when it is inside a certain area.
  Answer: Yes!
  For some scenarios, there is no need to perform deferred reports often when the UE is inside a certain area. On the contrary, the periodic location information will be more valuable when UE is outside a certain area. For example, the old men in the nursing home or the children in the kindergarten may spend most time inside the nursing home/kindergarten. The location report outside this area will be helpful in lost old men or lost children accidents.
Observation 3: Using allowed area in an opposite sense will bring more valuable data in some scenarios (e.g., old men in nursing home and children in kindergarten).
Discussion
Event report allowed area
A
B
Positive sense or opposite sense | Area A | Area B
Positive | Inside | Outside
Opposite | Outside | inside
How to understand using allowed area in an opposite sense:

## Slide 5
Observation 1: No reporting outside the allowed area saves the UE power but degrades the commercial location service experiences.
Observation 2: Reporting conditionally outside the allowed area can balance the demand between the UE power-saving purpose and commercial location service experiences.
Observation 3: Using allowed area in an opposite sense will bring more valuable data in some scenarios (e.g., old men in nursing home and children in kindergarten).
Proposal 1: UE is allowed to report conditionally when outside the allowed area. How to report should fully consider the demand between the power-saving and location service experiences.
Proposal 2: Allowed area can be used in an opposite sense.
Conclusions