## Slide 1: Discussion on Accuracy Information
vivo

## Slide 2: Background
During past meetings, Accuracy Monitoring has been introduced as a method for evaluating whether a ML model should be retrained or if a consumer NF should continue use analytics output.
When MTLFs or consumer NFs request AnLF(s) to monitor accuracy, an Accuracy deviation threshold may be included to indicate when/how the accuracy information should be reported. And one explanation of this threshold is:
“[Optional] Accuracy deviation threshold(s): a reporting threshold of deviation value, which is indicated that the NWDAF can provide accuracy information to the analytics consumer when deviation value is above this threshold. The deviation value indicates the deviation of the predictions from the actual network data. ……
  Editor's note: It is FFS to determine whether the deviation refers to a difference between accuracy values or difference of prediction from the actual network data.”
However, there are 2 problems:
  The relationship between accuracy and deviation is not clear here;
  The deviation is a good measurement method for the regression, however it does not apply to the classification.

## Slide 3: Two types of AI tasks
Type | Explanation | Common measurement | 
Classification | Prediction for discrete values tasks by supervised learning. e.g. the RAT type of an UE. | , precision, Recall, etc. | 
Regression | Prediction for continuous values tasks by supervised learning. e.g. the traffic information of a WLAN. | MSE, MAE, RMSE, etc. | 
Type | Explanation | Common measurement | 
Classification | Prediction for discrete values tasks by supervised learning. e.g. the RAT type of an UE. |  | 
Regression | Prediction for continuous values tasks by supervised learning. e.g. the traffic information of a WLAN. | MSE, MAE, RMSE, etc. | 
, correctness refers to the number of correct predictions out of all predictions, which has been used as a general performance measurement for classification.
MSE, MAE, RMSE could be used as general performance measurements for regression and is same as deviation as proposed/adopted in KI#1.
See the next slide for the detailed discussion regarding measurement.
Notes: https://www.javatpoint.com/regression-vs-classification-in-machine-learning

## Slide 4: Observations - Deviation/Correctness
Accuracy measurement method(s) in AI community | Explanation | Formula
MSE for regression (Mean squared error) | The average squared difference between the predicted values and the actual value (ground truth). | 
Correctness for classification | The number of correct predictions out of all predictions. The correct predictions means the predictions match (equal to) the ground truth. | 
Accuracy measurement method(s) in AI community | Explanation | Formula
MSE for regression (Mean squared error) | The average squared difference between the predicted values and the actual value (ground truth). | 
Correctness for classification | The number of correct predictions out of all predictions. The correct predictions means the predictions match (equal to) the ground truth. | 
Observation 1: For regression, the deviation should be used to measure how much the predictions vary from the ground truth as agreed/concluded in KI#1 and MSE is a implementation example of deviation.
Observation 2: For classification, the correctness is a suitable measurement of how well the predictions represent the ground truth, which, similar to MSE, is a general performance measurement in AI community.

## Slide 5: Observations –sample number
Formula
Formula
Observation3: Except deviation and correctness, the corresponding number of samples is essential information for consumer e.g. MTLF calculating a global ML model accuracy or NF consumer determining whether analytics accuracy is good or bad.
In clause 6.1.3, TS23.288, the consumer NF can include the following parameter to improve the confidence level and reliability of the accuracy information.
[OPTIONAL] Minimal number of analytics output occurrences: determines the minimal number of analytics output provided by NWDAF that have to be considered in the determination of the accuracy information.
The number of samples should be used to calculate a global accuracy when MTLF is determining if a ML model is degraded based on accuracy information from multiple AnLF.
If the global accuracy is a arithmetic mean calculated by taking the average of all local accuracies, rather than weighted average, it cannot reflect a real accuracy since the arithmetic mean is susceptible to extreme values.
For example, C has 90% accuracy with 50 samples, while D has 50% accuracy with 2 samples. Their arithmetic mean is 70%, however their weighted average is 88%.
The NWDAF1 has a higher accuracy, however, the consumer may think the NWDAF2 is more reliable and use the analytics output from the NWDAF-B.
 | Times of prediction | Correct prediction | correctness
NWDAF1 | 1 | 1 | 100%
NWDAF2 | 1,000 | 950 | 95%

## Slide 6: Proposal
Proposal 1: Clarify in KI#1 that Analytics/ML Model Accuracy Information is to represent general performance measurements for analytics and ML Model respectively, which are composed of the correctness for the classification and the deviation for the regression (e.g. MSE) .
  In case of classification, the correctness refers to the number of correct predictions out of all predictions;
  In case of regression, the deviation refers to the difference of the analytics prediction using the trained ML Model from the corresponding ground truth data which is collected from Data Producer NF(s).
Proposal 2: Further clarify, except deviation and correctness, the corresponding number of samples is essential information for consumer and should also included in Accuracy Information.

## Slide 7
Backup slides

## Slide 8
回归问题 -
1、SSE(The sum of squares due to error) The sum of the squares of residuals (deviations predicted from actual empirical values of data).
It is a measure of the discrepancy between the data and an estimation model.
2、MSE(Mean squared error) Measures the average of the squares of the errors—that is, the average squared
difference between the estimated values and the actual value.
3、RMSE(Root mean squared error)
Or called RMSD (root mean square deviation)
RMSD is the square root of the average of squared errors. The effect of each error on RMSD is proportional to the size of the squared error; thus larger errors have a disproportionately large effect on RMSD. Consequently, RMSD is sensitive to outliers.
4、MAE(Mean Absolute Error)
A measure for the average difference between the predicted value and the actual value;
5、MAPE (Mean Absolute Percentage Error)
Is a measure of prediction accuracy of a forecasting method in statistics.
6、MAE(Median Absolute Error)
Could reduce the influence of outliers. Deviation is calculated by taking the median of all absolute differences between target and prediction.
Notes: https://juejin.cn/post/6997563709157539847