## Slide 1: Way forward proposal for PIN
vivo

## Slide 2: Issue of multiple PINs one PDU Session
UE policy for PIN uses URSP rule with PIN ID as TD
Handling of URSP rules has been specified in 23.503 that if multiple URSP rules share same RSD, same PDU Session may be used
In case URSP rules with different PIN IDs share same RSD, it is possible for multiple PINs share same PDU Session
UP management (i.e., PDR and FAR configuration) is per PIN differentiated by different IP domain, which naturally support the sharing if different PIN is assigned by different IPv6 prefix
SMF assigning multiple IPv6 prefix to UE for delegation is already supported
Proposal: remove the corresponding EN

## Slide 3: Issue of one PIN multiple PDU Sessions
Enabling one PIN multiple session first means PIN ID can be combined with other TD
Session number per PIN impact mapping handling
  Mapping “outer side” interface to PIN or mapping “outer side” interface to PIN and PDU session
In case “one PIN one session”, multiple PINs can do all tasks that “one PIN multiple sessions” does
Mapping of inner interface to PIN and PDU session may need more effort for PEGC, e.g., allowing input or exposure of DNN, APP ID, IP descriptor, etc.
Considering multiple PINs may share same PDU Session, it will make the mapping very complicated
Allowing one PIN multiple session also makes it a little complicated for the data structure design for PIN information in UDM/UDR
Proposal: considering the limited TU left, one PIN one PDU Session in R18.
Most possible efficient PEGC implementation
Black line is “inner side”, red line is “outer side”
Green line is for traffic over "inner side" interface routing back over the “inner side” interface

## Slide 4: Issue of PIN activation and deactivation
PIN is fully controlled by PEMC or AF
All the communication configuration is made by PEMC or AF
PEMC or AF is able to remove all communication configuration
5GC providing SBI for PIN activation/deactivation can simplify the operation
5GC provides SBI will have impact on NFs, e.g., NEF, UDM, UDR
Proposal: in order to minimize impact on 5GC and considering limited TU left, remove the corresponding EN

## Slide 5: Issue of PIN identifier
PIN includes PEGCs and PEMCs, an ID shall be used targeting to multiple UEs
In case PCF is deployed, for UE policy provisioning, an ID is needed for AMF of PEGC sending it to PCF that enables PCF getting PIN related information or subscribe UDR notification for PIN related information change
Internal Group ID is a kind of inner ID used by 5GC to identify multiple UEs, and AMF already support sending Internal Group IDs in AM subscription data to PCF
Proposal: in order to minimize impact on 5GC, PIN ID is a kind of External Group ID that will be assigned with a Internal Group ID

## Slide 6: Issue of QoS differentiation for PIN
Procedure of DNN and S-NSSAI specific Group Parameters described in clause 4.15.6.3e of TS 23.502 supports group QoS configuration
Procedure of Multi-member AF session with required QoS for a list of UEs described in clause 4.15.6.13 of TS 23.502 supports QoS configuration for traffic between group UEs
Proposal: QoS differentiation for PIN reuses existing methods

## Slide 7: Issue of PIN capability indication from UE to SMF
A PIN is associated with a (DNN, S-NSSAI), two URSP rules may share same RSD with the (DNN, S-NSSAI), one with PIN ID the other not, e.g., intend to use same PDU Session for PIN traffic and for PIN management
PIN traffic does not always need a PDU Session (i.e., routing via PEGC only), the UE may initially establish a PDU Session according to the URSP rule without PIN ID, this PDU Session is not for PIN traffic, and shall not use PIN traffic UP management by the SMF
When PIN traffic is needed to be forwarded via 5GS, the PDU Session is needed for PIN traffic, indication is needed for SMF to apply PIN traffic UP management
Proposal: in order to inform when to apply UP management for PIN, an indication is included in UE 5GSM Core Network Capability when traffic routing for PINE is needed

## Slide 8: Issue of enabling PIN management by PEMC
PEMC APP can be installed on any UE as well as on devices
The UE with PEMC APP (called PEMC UE) may not have direct connection with any PEGC
The communication of a PIN is fully controlled by PEMC/AF, in case AF is not deployed, the PEMC UE shall be able to communicate with PEGC to enable the management of the PIN via 5GC local switch
Proposal: enabling PIN management by PEMC via local switch
Why PEMC needs to communicate with PEGC via 5GC local switch

## Slide 9: Issue of enabling PIN management by PEMC
The PDU Sessions of PEGCs and PEMCs are anchored at same SMF without impact on SMF selection
For resource efficiency, the PEGC’s PDU Session for PIN management could be the PDU Session for PIN traffic (URSP rule with PIN ID and URSP rule without PIN ID share same RSD), depends on operator policy or AF request
If PDU Session for PIN is not PDU Session for PIN management, 5G VN feature can be reused for enabling PIN management by PEMC
If PDU Session for PIN is PDU Session for PIN management, UP management (PDR and FAR configuration) for PIN and for PIN management needs to be considered together for configuration efficiency (i.e., less PDRs/FARs is better)
For a PIN associated with (DNN, S-NSSAI), the Internal Group ID corresponding to the PIN can be configured to PEMC’s AM subscription data to enable the PEMC be provisioned with URSP rule associated with the (DNN, S-NSSAI)
The Internal Group ID corresponding to the PIN can be configured to PEMC’s SM subscription data to enable the SMF identifies the PDU Session for PIN management
The proposed principle for PEMC communicating with PEGC via 5GC local switch

## Slide 10: Issue of PINE indirect communication configuration
PIN is mostly used in consumer scenarios instead of industry scenarios as described in SA1
PEMC/AF performs permission control for any PINE indirect traffic (via 5GS or not)
Some UEs may support full traffic filtering, but not all UEs support, it depends on device capability
At least for smartphone, considering power and computing capability, full traffic filtering is not applicable
URSP rule with PIN ID is intend for efficient traffic routing for PINEs, but routing all traffic to OS/APP then back will make traffic of PINEs is same as traffic of APPs, this will make the URSP rule with PIN ID meaningless
To make communication module have a interface for APP/OS installing filters is almost not feasible
Proposal: SMF initially does not configure PDRs and FARs for PINE indirect communication via 5GS to support permission control, and configures PDRs and FARs according to packet filters received, which is the natural performance of SMF.
Most possible efficient PEGC implementation
Black line is “inner side”, red line is “outer side”
Green line is for traffic over "inner side" interface routing back over the “inner side” interface

## Slide 11: An example of UP management for PINs – PEMC UE is able to manage PIN#1 and PIN#2
In order to enable the management data handling by PEGC APP, in this example, the URSP for PEGC include two URSP rules share same RSD that one with PIN ID as TD and the other with PEGC APP ID or IP descriptor or DNN as TD .
PDRs and FARs for PDU Session#1 (PEGC#1) |  | PDRs and FARs for PDU Session#3 (PEGC#3) |  | PDRs and FARs for PDU Session#0 (PEMC UE) | 
PDR#11 for management UL |  | PDR#31 for management UL |  | PDR#01 for management UL | 
Source interface | "access side" | Source interface | "access side" | Source interface | "access side"
CN tunnel info | N3 TEID for PDU Session#1 | CN tunnel info | N3 TEID for PDU Session#2 | CN tunnel info | N3 TEID for PDU Session#0
Packet Filter Set | src: PEGC IP#1 | Packet Filter Set | src: PEGC IP#3 | Packet Filter Set | dst: PIN#1 IP ranges
FAR#11 for management UL |  | FAR#31 for management UL |  | FAR#01 for management UL | 
Network instance | PIN#1 | Network instance | PIN#2 | Network instance | PIN#1
Destination interface | "5G VN internal" | Destination interface | "5G VN internal" | Destination interface | "5G VN internal"
PDR#12 for management and traffic DL |  | PDR#32 for management and traffic DL |  | PDR#02 for management DL | 
Source interface | "5G VN internal" | Source interface | "5G VN internal" | Source interface | "5G VN internal"
Network instance | PIN#1 | Network instance | PIN#2 | Network instance | PIN#1
Packet Filter Set | dst: PEGC IP#1 ¦¦ PINE IP#11 | Packet Filter Set | dst: PEGC IP#3¦¦ PINE IP#31 | Packet Filter Set | dst: PEMC IP#0
FAR#12 for management and traffic DL |  | FAR#32 for management and traffic DL |  | FAR#02 for management DL | 
Destination interface | "access side" | Destination interface | "access side" | Destination interface | "access side"
Outer header creation | N3 TEID for PDU Session#1 | Outer header creation | N3 TEID for PDU Session#3 | Outer header creation | N3 TEID for PDU Session#0
NOTE: The DL PDRs and FARs for PEGCs are shared by both management and traffic data |  |  |  |  | 
PDR#13 for traffic UL |  | PDR#33 for traffic UL |  | PDR#03 for management UL | 
Source interface | "access side" | Source interface | "access side" | Source interface | "access side"
CN tunnel info | N3 TEID for PDU Session#1 | CN tunnel info | N3 TEID for PDU Session#2 | CN tunnel info | N3 TEID for PDU Session#0
Packet Filter Set | src: PINE IP#11 dst: PINE IP#21 | Packet Filter Set | src: PINE IP#31 dst: PINE IP#41 | Packet Filter Set | dst: IP ranges for PIN#2
FAR#13 for traffic UL |  | FAR#33 for traffic UL |  | FAR#03 for management UL | 
Network instance | PIN#1 | Network instance | PIN#2 | Network instance | PIN#2
Destination interface | "5G VN internal" | Destination interface | "5G VN internal" | Destination interface | "5G VN internal"
 |  |  |  | PDR#04 for management DL | 
 |  |  |  | Source interface | "5G VN internal"
 |  |  |  | Network instance | PIN#2
 |  |  |  | Packet Filter Set | dst: PEMC IP#0
 |  |  |  | FAR#04 for management DL | 
 |  |  |  | Destination interface | "access side"
 |  |  |  | Outer header creation | N3 TEID for PDU Session#0