## Slide 1: Edge_Ph2 Issues related to DNS over TLS (DoT) and DNS over HTTPS (DoH) Discussion Paper
Sony
S2-2305049

## Slide 2: How DoT & DoH works
Pre-requirements:
The UE (DNS client) must know the FQDN to the DNS Server supporting DoT or the URI Template (RFC 8484) to the DNS Server supporting DoH
UE have a storage of installed trusted root certificates
The UE send an insecure DNS request to resolve the FQDN/URI to an IP address of the secure DNS Server, this is usually the same as the IP of the insecure DNS server
UE initiates a TLS tunnel to the Secure DNS Server and retrieves a certificate with the public key of the secure DNS Server
UE validate that the retrieved certificate contains the same FQDN and that it is trusted via using its own trusted root certificates
For DoH then the UE construct the URI to be used to the DNS Server based on the URI Template.
UE sends DNS request to the Secure DNS Server

## Slide 3: What we have specified today 1(2)
23.501 clause 5.6.10.1:
If the UE indicates support of DNS over (D) TLS to the network and the network wants to enforce the use of DNS over (D)TLS, the configuration information is sent by the SMF via PCO may also include the corresponding DNS server security information as specified in TS 24.501 [47] and TS 33.501 [29].
24.501 clause 6.4.1.3:
NOTE 9: Support of DNS over (D)TLS is based on the informative requirements as specified in 3GPP TS 33.501 [24].
33.501 Informative Annex P.2:
It is recommended that the UE and DNS server(s) support DNS over (D)TLS as specified in RFC 7858 [83] and RFC 8310 [84]. The DNS server(s) that are deployed within the 3GPP network can enforce the use of DNS over (D)TLS. The UE can be pre-configured with the DNS server security information (out-of-band configurations specified in the IETF RFCs like, credentials to authenticate the DNS server, supported security mechanisms, port number, etc.), or the core network can configure the DNS server security information to the UE. NOTE: The use of DNS over (D)TLS with DNS server(s) that are deployed outside the 3GPP network is outside the scope of this document.

## Slide 4: What we have specified today 2(2)
24.008 ePCO:
000DH DNS Server IPv4 Address
0031H DNS server security information with length of two octets
23.548 clause 5.1.1 EASDF
Terminates the DNS security, if used
23.548 clause 5.2 EDC Functionality
This definition only uses the ePCO to configure the DNS Client with the IP address of the DNS Server. Secure DNS or usage of DNS server security information is not included.

## Slide 5: Issues
Observation 1:
Provisioning of the FQDN/URI Template of the Secure DNS Server as an ePCO in PDU Session Establishment/Modification is not specified. The UE must have it for DoH and to validate the TLS session.
SA3 has specified the “DNS server security information” as optional informative annex containing “DNS server security information” that the UE vendor could in a proprietary way implement to support DoT.
Proposal:
Expect that SA3 will specify provisioning of what is needed in the UE to use a Secure DNS Server, they may for example do it either as a new ePCO or replace the existing informative one that contains optional “DNS server security information” with normative configuration for the UE to use the Secure DNS Server but it is up to SA3 to define.
Alternative solution:
We uses the informative “DNS server security information” and specify how it is used as normative in the EDC for Edge Computing. Generic DoT and DoS should not be specified for Edge only, but this alternative does not require any SA3 impact.

## Slide 6: Issues
Observation 2:
Normative specification of the UE behavior to use the Secure DNS that is provisioned from ePCO is not defined.
Proposal:
We specify in 23.501 how to configure the DNS Client supporting DoT. This part could also be specified in SA3 later.
  DoT support in 23.501 - S2-2305052
  Updating EDC functionality with reference to 23.501 for configuring DNS Client including security – S2-2305053

## Slide 7: Issues
Observation 3:
23.501 and SA3 specifications only reference to RFC 7858 and RFC 8310 which is DNS over TLS. There is no support or reference to DNS over HTTPS (DoH).
23.501 specifies that the UE indicate its support for DoT but we don’t have any indication when the UE supports DoH
If DoH should be supported, then the UE (DoH Client) needs to be provisioned with the URI Template according to RFC 8484 to be able to construct the URI to use for the DNS Server
Proposal:
We expect that we and SA3 will do that is future release. This may also impact capability exchange signaling specified in 23.501. UE may for example need to indicate if it supports DoH and, in that case, the SMF should also provide additional ePCO to configure the UE with the URI Template to be used in DoH according to RFC 8484.
Add a NOTE that DoH is not supported – S2-2305052

## Slide 8: Issues
Observation 4:
The EDC functionality is trying to redefine the DNS Client functionality that we already specified in 23.501, 24.501, 22.501 and 24.008 but everything related to security, i.e. the ePCO for DNS server security information etc. and how it is used is missing
Proposal:
Reduce the definition for the EDC and instead reference 23.501 for how the EDC is configured with the DNS sever configuration (including the security part) – S2-2305052

## Slide 9: Issues
Observation 5:
IP address replacement is in reality only working if it is the same owner (owner of the private certificate of the different secure DNS Server). Therefore, using DoT when roaming with IP Address replacement is not supported.
Resolution proposal:
Add a NOTE that DoT is not supported when IP Address replacement is used, S2-2305053

## Slide 10: Alternative solutions
Summary of the proposed solutions:
Only specify how DoT configuration to the UE is supported once and expect that SA3 will do that as normative specification since that is generic functionality and not Edge specific. We may need to provide alignment CR to our specifications in the future when that is done in SA3.
An LS to SA3 is prepared in case we want use it – S2-2305054.
Alternative solution (not recommended):
We specify everything our self to support DoT and uses the optional informative ePCO that SA3 specified (DNS server security information) as FQDN to the secure DNS Server and we specify that as normative in either 23.501 or possible 23.548. This has no SA3 impact but not recommended.