## Slide 1: Study on IMS event exposure framework
George Foti
Ericsson

## Slide 2: Outline
There are currently no standard defined mechanisms in IMS for an external (to the PLMN trust domain) API invoker to subscribe to specific events related to a specific IMS subscriber / group of IMS subscribers.
The serving IMS NFs (providing / producing said events / data) cannot be dynamically located by the API invoker.
An example of a specific event that can be subscribed to is “IMS user call-state” (e.g., idle, busy, registered etc.).
The objective of the study is to update the IMS reference architecture (i.e., TS. 23.228) to provide a framework whereby external (to the PLMN trust domain) API invokers can dynamically subscribe to IMS events related to a specific IMS subscriber or group of IMS subscribers via subscribe / notify mechanism.

## Slide 3: Content
It is proposed to study the following items in 3GPP R19:
IMS event subscription mechanisms via subscribe / notify procedures to external API invokers,
identify IMS events that can be subscribed to,
locator functionality whereby the IMS NF / IMS NFs serving the specific subscriber(s) for which the specific event was requested is found,
subscribe / notify procedures from the IMS NF / IMS NFs serving the specific subscriber(s) for the requested event,
synergies with the Network Exposure Framework defined in 5GS (e.g., exposure of events to external API invokers via the network exposure function (NEF) from the IMS NF / IMS NFs).
IMS exposure framework
S
AF
S
AF
S
AF
S
IMS NF
S
IMS NF
S
IMS NF
Trust domain
S
Overview

## Slide 4: Summary
Study standard defined mechanisms in IMS enabling an external (to the PLMN trust domain) API invoker to subscribe to specific events related to a specific IMS subscriber / group of IMS subscribers:
  define event subscription mechanism,
  define specific events,
  define locator functionality,
  define synergies with the Network Exposure Framework defined in 5GS (e.g., NEF).