## Slide 1: Study Proposal on Enhanced 5G Core Support for AI (FS_5GC_AI)
Samsung
3GPP TSG-SA WG2 Meeting #157
22 – 26 May 2023, Berlin, Germany
S2-2306475

## Slide 2: Background
Groundwork for support of AI across the 5GS was pioneered by SA2 with the introduction of NWDAF as a 5GC NF, and past releases have both expanded the set of data analytics and a framework for model sharing/federated learning in the 5GC
Rel-18 AIMLsys in SA2 introduced 5GC support for AI/ML-based services with a set of new monitoring, exposure and policy capabilities as well as a new functionality hosted in NEF to provide assistance for member UE selection to an AF executing AI/ML operations
Meanwhile, more AI functionalities are being introduced in other domains of 5GS by different WGs
In Rel-19, we propose to enhance the 5GC capabilities to enable improved support for AI by focusing on i) cross-domain coordination aspects incl. RAN and UE, ii) extension of recommendations for 5GC NFs, and iii) detection/mitigation of network risks

## Slide 3: Proposed Objectives
Objective 1: Architecture extensions for coordination of cross-domain AI/ML functionalities
  Support for AI/ML related data and/or model sharing between 5GC and RAN entities.
  Support for AI/ML coordination between MTLF and MDAS.
  Further 5GC support for UE-based data collection and/or exposure and AI-related processing with AI servers located in AF, 5GC, RAN, or other UE.
Objective 2: Architectural and functional extensions to support AI-based 5GC recommendation capabilities
  Identify new use cases to apply AI-based 5GC recommendations for network and UE operations.
  Study required architecture extensions to support AI-based 5GC recommendation capabilities.
  Enhancements of AI-related 5GC functionality relevant to recommendations (e.g. AI model accuracy monitoring, AI model performance feedback, confidence levels, etc.).
Objective 3: Extensions for AI-based detection and mitigation of performance degradation and/or operational conflict
  Definition of network risk in relation to performance degradation and operational conflict.
  Support 5GC-based network risk detection as well as network actions leveraging AI and recommendations to mitigate the detected network risk.
  Initial focus on mobility management optimization use case, including 5GC and RAN based AI/ML. For example, UE trajectory predictions available both at NWDAF and NG-RAN leading to potential performance degradation and/or operational conflict when 5GC and RAN jointly performing handover decisions. Other use cases to be explored.

## Slide 4: Objective 1: Additional Information
1a) RAN WGs have done extensive work on AI/ML potentially requiring support from 5GC:
  RAN 1/2 are considering the 5GC (incl. LMF) as an option for AI/ML model transfer/delivery point to the UE via both control and user planes for CSI, beam management and positioning use cases
  RAN3 has developed separate AI-based UE mobility predictions from NWDAF analytics for their mobility optimization use case.RAN-5GC coordination is desired to optimize network behavior and prevent overlapping/conflicting decisions
1b) Rel-18 developed some use cases for NWDAF/MDAS collaboration, but still need much improvement to support, e. g., model sharing/coordination between entities.
1c) Rel-18 developed UE data collection mechanism for NWDAF analytics, and did not conclude exposure of AI-related information to the UE. UE-based AI operation with AI servers in different domains requires enhancement on the 5GC including data collection and exposure framework for wider use.

## Slide 5: Objective 2: Additional Information
Rel-18 introduced the capability for NEF to provide recommendations to support AI application (AF) i.e., for member UE selection and other recommended parameters for AI application operations such as time window, QoS, UE location, etc.
2a) Usage of recommendation is limited in Rel-18. New use cases should be investigated to apply 5GC recommendations to network operations (consumed by 5GC NF) and UE application client operations
  SA4 FS_AI4Media study is expected to require support from 5GC on exposure/ recommendations to UE to support split inferencing and intermediate data transfer as shown in TR 26.927
2b) NEF was selected for recommendation in Rel-18. Architecture extensions should be investigated for new use cases, e.g. which NF to provide recommendations, new required services, new procedures, etc.
2c) AI model related functionality previously specified only addresses analytics. Hence, AI functionalities should be extended to address recommendations

## Slide 6: Objective 3: Additional Information
AI functionalities are defined in different domains by different WGs, which have risks for degradation and/or operational conflict. Cross-domain coordination between 5GC and RAN, UE as well as recommendations need to be considered to enable detection and mitigation of AI-related risks
3a) Such network risks should be defined at the 5GC e.g. as related to performance degradation and/or operational conflict
3b) Recommendations can be leveraged within the 5GC to mitigate the detected potential problem
3c) Mobility management optimization between 5GC-RAN may be studied as first use case to jointly leverage cross-domain AI and recommendations to align AI-based predictions and corresponding decisions to executive handover.

## Slide 7: Thanks!