## Slide 1: Analysis of UP based QoS Notification Control
Dan Wang, China Mobile

## Slide 2: Background
  In XRM study and normative work, There is an EN about QNC exposure through user plane.
  In 155 meeting, SA2 has sent LS to RAN3(S2-2303813) for checking this method. And the LS response from RAN3(S2-2306312) is shown as below:
  RAN3 discussed the UP based QoS Notification Control and reached no consensus on the benefits of this feature. This feature may be feasible, but RAN3 has not analysed the details. During RAN3´s discussions the following possible technical issues were raised by some companies that may need to be further clarified by SA2:
  - UP based QNC may not be able to support reporting alternative QoS parameters.
  - Even in UP based QNC, QNC reporting delay is also possible, e.g. due to the hysteresis before determining the QNC result, and the delay depends on RAN’s implementation.
  - UP based QNC is on top of GTP-U/UDP which may cause out of sequence delivery.
The LS from RAN3 has the following information:
1) it is feasible for RAN to expose QNC through user plane to UPF.
2)RAN3 ask SA2 to clarify 3 aspects.

## Slide 3: Analysis for RAN3 question
  Q1: UP based QNC may not be able to support reporting alternative QoS parameters.
  Answer: in SA2, the QNC is intent for the TS 23.501 5.7.2.4.1a Notification Control without Alternative QoS Profiles. We do not study/discuss about the alternative QoS scenario, therefore in Rel18, QNC is not for Alterantive QoS profile.
  Q2: Even in UP based QNC, QNC reporting delay is also possible, e.g. due to the hysteresis before determining the QNC result, and the delay depends on RAN’s implementation.
  Answer: the intention for UP based QNC is to reduce the delay for the core network control plane transmission i.e.NG-RAN->AMF->SMF->PCF->NEF->AF(25ms,NOTE1) generally 5ms per step based on network experience). In SA2 R17, the method of UPF direct notification has been introduced (TS23.548 6.4.2.1), therefore in R18, XRM have discussed to reuse the UPF direct notification method to expose QNC, i.e. NG-RAN->local UPF->local NEF->AF(15ms, NOTE2). So the delay for QNC reporting through UP is smaller than delay for QNC reporting through CP.
  NOTE1: In order to compaired the deplay, it can be supposed that the control plane NFs and UPF are all deplyed with in the same province. In real network experience, generally, 5ms per interaction between two NFs. NG-RAN-AMF communication delay is larger than 5ms, but to make the scnario more simplified, this can also be counted as 5ms.
  NOTE2: N3 transmission time within the same province is usually around 5ms.

## Slide 4: Analysis, Observation, and Proposal
  Q3: UP based QNC is on top of GTP-U/UDP which may cause out of sequence delivery.
  Answer: Since the UP based QNC for alternative QoS profie is not supported, the QNC meaning based on UP only intent to show that one GBR QoS profile cannot be guaranteed. So even out of sequence delivery, there is no impact for the method.
  Observation:
  XRM service need the quick notification of QNC once the GBR flow cannot be guaranteed, which can help application server adjust the DL packet data rate in time.
  UP based QNC do have the advantage to expose the QNC to AF in low latency.
  The RAN3 concern about the UP based QNC is not a problem.
  Proposal:
  It is suggested SA2 can support the UP based QNC mechanism in Rel-18.