## Slide 1: Motivation for Generalized framework of data collection from UE
Qualcomm Incorporated, vivo, OPPO
S2-2306506

## Slide 2: UE data collection standard status –SA2
Rel-17
  SA2 approved UE data collection solution by using EVEX architecture in clause 6.2.8 in TS 23.288 since Rel-17.
    It is allowed to collect UE application layer data from UE to 5GC
    Both direct data collection ( UE->DCAF->NWDAF) and indirect data collection (UE->DCAF->AF->NWDAF) are supported
    Both 3GPP and non-3GPP defined information is supported

## Slide 3: UE data collection standard status –SA6
SA6 is also discussing UE data collection and exposure between UE and 5GC in Rel-18 in ADAES and eSEALs.
The LS S6-231059 was sent from SA6 to SA4 to express the following requirements for EVEX architecture:
  The ASP shall be able to retrieve/pull collected data on-demand (i.e. without need for setting up session) from the UE Application through a request/response mechanism.
  The UE Application shall be able to send/push collected data on-demand (i.e. without need for setting up session) to ASP through a request/response mechanism.
  The ASP shall be able retrieve collected data from the UE Application through a subscribe/notify mechanism.
  The ASP shall be able to configure the subscription for the UE Application including the specific information to be reported, the triggering criteria and reporting configuration.

## Slide 4: UE data collection standard status –RAN1 & RAN2
AI/ML for NR Air Interface is being discussed in RAN1 and RAN2 in Rel-18
RAN2 is leading the discussion about data collection from UE for ML model training and ML model transfer / delivery to UE.
Several solutions which include EVEX-enhanced solution were proposed in RAN2.
The work should require SA expertise as it goes beyond RAN’s scope for the following reasons:
  RAN can not track a UE between RRC connections.
  ML model training maybe performed by the UE vendor, while the data is available at the operator. We need a standard way to transfer the data out of the operator’s network that is visible and controlled by the operators.
  The SA teams should be involved in designing the architecture for data collection and data storage for RAN AI/ML purposes.

## Slide 5: UE data collection standard status –SA Plenary
SA is considering the new requirements about UE data collection / exposure activities ongoing in SA2, SA4 and SA6. The LS was sent to SA4 in SP-230394.
SA also triggered the discussion that which WG would lead the discussion in Rel-19 for the new requirements.

## Slide 6: Conclusion
“UE data collection from UEs” are being discussing in different WGs, including SA2, SA4, SA6 and RAN1/2.
It is desired to have a common framework that meets all the requirements among different WGs. SA2 is the natural WG that defines common system frameworks.
It is proposed to approve the following proposal as objectives in the SID regarding 5G AI/ML in Rel-19 in SA2, for example S2-2306462:
  A general framework of data collection from UEs